## Slide 1: Upgrade of trigger and DAQ for CsI at BelleII
Vladimir Zhulanov for BelleII ECL group
Budker INP, Novosibirsk
INSTR2014, Novosibirsk
2014/02/28

## Slide 2: Outline
Overview of the ECL (CsI Electromagnetic CaLorimeter) readout electronics
Fitting algorithm and its realization
Interface with BelleII DAQ and trigger systems
Summary

## Slide 3: Waveform sampling readout
Shaper output signal
Gate width=100ns
Signal charge
↓
Timing (leading/trailing edges) with range information by QtoT converter (MQT300A)
↓
Digitized by TDC
2MHz, 18bits digitizer,
waveform fit to get energy and timing (i.e. Digital Signal Processing)
Reduction factors;
×7 BG showers
×1.5~2 pileup noise
→ t
→ t
From Miyabayashi’s slides
Notes: Early today Miyabayashi-san presented the upgrade of the BelleII electromagnetic calorimeter and mentioned about the reasons to change the electronics architecture to the pipelined architecture.

## Slide 4: ECL electronics
ShaperDSP
ShaperDSP
ECLCollector
ShaperDSP
FTSW
COPPER
Trigger& timing
belle2link
HSLB
HSLB
HSLB
HSLB
12 ShaperDSP
Modules
ShaperDSP serves 16 CsI counters
FAM
TMM
Global
trigger
PA
PA
PA
TTD
(Trigger & Timing Distribution)
CPU
Event Builder
8736 CsI counters in total => 52 VME crates
TMM

## Slide 5: ShaperDSP
Shaper
ADC
18 bit
Fast
shaper
Vref.
PA
ADC
XILINX Spartan
CYCLONE
DDR
DeSer.
Ser
control
1
2
ALTERA
Interface
with
EclCollector
Temperature
Fast out
DATA
1
16
1
16
16
ADC & Digital Pot Control
3
15
14
13
2
SCK - Clock,
RCK -Sync, conf
10
10
FAM
Conf
DCPs

## Slide 6: ShaperDSPb photo
ADCs
Shapers
I/F with EclCollector
DDR memory
FPGA Xilinx
FPGA ALTERA
Connectors to PreAmps
(readout signal, Calib, power supply)
LDO power converters
DCPs

## Slide 7: Tasks of the ECL Collector module.
Collect and merge data from 12 connected ShaperDSP modules
Provide interface with Belle II TTD and DAQ
Configure Xilinx FPGA on ShaperDSPb modules
Synchronization of sampling process in ShaperDSPb modules
Generation of a calibration signal
Ethernet interface for stand-alone operation and upload of DSP coefficients
Store coefficients for DSP processing
SER/DESER
SCK, RCK
FPGA
Xilinx
Virtex5
Or
Spartan6
RocketIO
DAQ
Flash memory
512 MByte
DAC
LVDS
TTD
calib
Ethernet
JTAG over LVDS

## Slide 8: EclCollector photo
Serializer/Deserializer modules TI SCAN928028
TI SCAN926260
IFC with ShaperDSP
SFP connector
Ethernet, Trigger,
JTAG-over-LVDS
HV
Calib
FPGA Spartan6
XC6SLX150T-3
Parallel flash
memory
CPLD
DAC for calibration pulse generation AD9726 16 bits @80 MHz
Calibration pulse is
Based on LUT – imitate signal from PD

## Slide 9: Fitting algorithm

## Slide 10: Parallel calculation
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Iteration 1
Iteration 2
Iteration 3
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs
MAC
DIV
Load coefs.
MAC
DIV
Core 2
Core 1
ShaperDSP easily digitally processes 16 channels @ Trigger rate = 50 kHz
while the BelleII designed maximum TR=30 kHz, and maximum ECL channel occupancy = 1/3
is calculated after the end of 3rd itertion and is compared to specified threshold => Data quality flag
Output: Amplitude (18 bits), Time (12 bits), Quality flags (2 bits)

## Slide 11: ECL data processing
ShaperDSP
FPGA
ADC1
ADC12
DSP
ADC DATA BUFFER
+ buffer for
512 samples
16 ch.
DDR 1
DDR 2
PACKAGER
Trigger Controller (FIFO)
DeSer
Collector
Trigger
Event data
Event data
HSLB
FTSW
Trigger

## Slide 12: Algorithm comparison: HW vs SW
Hardware reconstruction algorithm fully corresponds to its software version
This is verified by reading out the raw ADC data together with reconstracted A, T and Q

## Slide 13: Linearity

## Slide 14: Time resolution

## Slide 15: ECL TRG system
From Y.Unno’s slides

## Slide 16: FAM
From Y.Unno’s slides

## Slide 17: TTD system protocol
Trigger data is distributed over home-made TTD protocol
encoded with 8b/10b @ 127 MHz
FTSW board distributes trigger information between FEE
From M.Nakao’s slides

## Slide 18
From T.Higuchi’s slides
COPPER - COmmon Pipelined Platform for Electronics Readout
PMC CPU
local bus
PCI bus
from detector
mezzanine (add-on) modules
Network I/F
Trigger Module
Detector I/F
Detector I/F
Detector I/F
Detector I/F
Bridge
PMC modules
FIFO
to event builder
4 HSLB (High-Speed Link Board) modules are installed in each COPPER.
HSLB – unified data collecting board

## Slide 19: Summary
The pipelined architecture for ECL electronics has been designed.
Algorithm tests at the Belle detector (before its shutdown for upgrade) were successfully carried out.
Currently the electronics mass production is in progress

## Slide 20
Thank you