## Slide 1: LONG TERM EXPERIENCE AND PERFORMANCE OF COMPASS RICH-1
COMPASS RICH-1
Vessel, radiator gas and mirror system
MWPC’s with CsI photocathodes
The MAPMT based detectors
PID Performances of COMPASS RICH-1
The upgrade with MPGD-based PDs
Fulvio Tessarotto
( I.N.F.N. – Trieste )
For the COMPASS RICH Group

## Slide 2
COMPASS II Collaboration
Experiments with muon beam:
  Spin structure, Gluon polarization
  Flavor decomposition
  Transversity
  Transverse Momentum-dependent PDF
  DVCS and HEMP
  Unpolarized SIDIS and TMDs
COMPASS - I (2002 – 2011)
COMPASS - II (2012 – 2017) …
Experiments with hadron beams:
  Pion polarizability
  Diffractive and Central production
  Light meson spectroscopy
  Baryon spectroscopy
  Pion and Kaon polarizabilities
  Drell-Yan studies
Bochum,
Bonn (ISKP
& PI),Erlangen,Freiburg,
Mainz,München TU
USA (UIUC)
Saclay
Tel Aviv
Calcutta (Matriviani)
Torino (University,INFN),
Trieste (University,INFN)
Warsawa (NCBJ),
Warsawa (TU)
Warsawa (U)
CERN
Yamagata
Praha (CU/CTU)
Liberec (TU)
Brno (ISI-ASCR)
Дубна (LPP and LNP), Москва (INR, LPI, State University),Протвино
Lisboa/Aveiro
Taipei (AS)
~ 250 physicists
from 24 Institutions
of 13 Countries

## Slide 3
DAQ: 40 kB, 30 kHz, O(PB)
BEAM, TARGET AND SPECTROMETER
50m
Target
region
Large
Angle
Spectrometer
Small
Angle
Spectrometer
SM1
SM2
1 Tm
4 Tm
RICH-1
P. Abbon et al., Nucl. Instr. and Meth. A 567 (2006) 114
160 or 190 GeV/c µ+ (or µ-), 4 . 108 µ/spill, Pm ~ 80%
190 GeV/c p, π+, π- , K+ ,K- beams
Polarized ( p , d) target
first GEMs and Micromegas used in a HEP Experiment
Various targets used
Proton recoil detector
(not in scale)
new: pixel GEMs

## Slide 4
hadron PID from 3 to 60 GeV/c
acceptance: H: 500 mrad V: 400 mrad
trigger rates: up to ~50 KHz
beam rates up to ~108 Hz
material in the beam region: 1.2% Xo
material in the acceptance: 22% Xo
detector designed in 1996
in operation since 2002
upgraded in 2006
total investment: ~ 4 M €
a new upgrade is foreseen in 2016
radiator:
C4F10
5 m
6 m
3 m
MWPC’s + CsI
UV mirror
wall
Al vessel
radiator gas: C4F10
COMPASS RICH-1
is a large gaseous RICH
with two kind of photon detectors
providing:
PMT’s
beam pipe

## Slide 5
The principle and a typical event

## Slide 6: The principle and a typical event

## Slide 7
the vessel and the mirror support wall
Large and accurate mechanics
light front and rear windows
100 m of O-rings, 80 m3 C4F10

## Slide 8
mirrors and alignment
measurement of mirror alignment
via laser autocollimation
21 m2, 116 mirrors radius: 6.6 m
angular regulation screws

## Slide 9
problems with mirrors
reflectance
λ(nm)
reflectance stability
2002
2001
2000
(at coating)
initial alignment accuracy: ~100 μrad
alignment instability: 1 mrad (first year)
surveying accuracy: ~ 60 μrad
alignment instability: ~ 100 μrad after 2002
alignment check  surveyors inside  opening the vessel: contamination, dust,
risky operations, work load, expenses.

## Slide 10
CLAM: mirror alignment monitoring
CLAM system in operation since 2007
accuracy: 30 μrad
4 cameras
at corners
with LED’s
retroreflective grid
“CLAM” picture for mirror monitoring
photogrammetric calibration of cameras  measurement of absolute mirror tilt

## Slide 11
weight = 15 g
2012: a new light beam pipe
Old: 150 µm thick stainless steel pipe:
0.85 % X0 for orthogonal crossing
Suspension and tensioning system: 1 x 7 wires ss rope 30 μm diam.
1 microflange and 1
Material: 4 x 25 μm thick Mylar + 200 nm Al coating (by Sheldahl)
winding by Lamina (6 µm glue)
1 microflange for suspension + gas connection + window holding
New pipe: 0.044 X0 for orthogonal crossing

## Slide 12: Safety issues for working inside the RICH
1) Radiation level: < 2 μSv/h
2) Scaffolding installation
3) Old pipe removal
4) Mirror alignment measurement
5) New pipe installation + alignment
6) Removal of scaffolding +cleaning

## Slide 13
The radiator gas system
has excellent performance

## Slide 14
on-line filters with separate functions:
  Cu catalyst, ~ 400C for O2
  5A molecular sieve, ~ 100C for H2O
Typical RICH-1 C4F10 transparency
stable gas composition: 97.5% C4F10, 2.5% N2

## Slide 15
Problems with the radiator gas
Buying C4F10 is non trivial (out of market for years)
It comes dirty (very dirty sometimes): pre-cleaning is a must
(dedicated system, unavoidable losses, expert manpower)
Inserting it into the vessel (and recovering it) is delicate,
losses ~ 2%, incomplete (97.5% maximum)
Critical circulation system with feedback to keep Δp < 0.1 mbar challenged by weather
C4F10 leaks out (50 l/day): refill is needed
It integrates contaminants: some can be accepted (N2, Ar), others need
continuous filtering out (O2, H2O) ; the filters have limited capacitance
(significant contaminations fill them quickly); regeneration takes several days
Monitoring the transparency is a must (dedicated system, expert
manpower, significant gas consumption for each measurement)
Thermal gradients problem:  fast circulation (20 m3/h) implemented in 2009
Accidents can become disasters; emergency intervention to be granted in short time:
EXPERT ON CALL 24 h/day, 7 days/week for 7 months/year: heavy load on experts

## Slide 16: In the family of gaseous detectors, with a glorious tradition
1908: FIRST WIRE COUNTER
USED BY RUTHERFORD IN THE STUDY OF NATURAL RADIOACTIVITY
E. Rutherford and H. Geiger , Proc. Royal Soc. A81 (1908) 141
1928: GEIGER COUNTER
SINGLE ELECTRON SENSITIVITY
H. Geiger and W. Müller, Phys. Zeits. 29 (1928) 839
1968: MULTIWIRE PROPORTIONAL CHAMBER
G. Charpak, Proc. Int. Symp. Nuclear Electronics (Versailles 10-13 Sept 1968)
Nobel Prize in Chemistry in 1908
Walther Bothe
Nobel Prize in 1954 for the “coincidence method”
Hans Geiger
Ernst Rutherford
Nobel Prize in 1992
George Charpak
Fabio Sauli
Jean-Calude Santiard

## Slide 17
Gaseous photon detectors use
PHOTOELECTRIC ABSORPTION :
gas photoionization photoelectric effect
gas volume: photosensor (TMAE or TEA) gas volume: CH4
+ carrier (CH4 or C2H6)
Cherenkov photon
photoelectron
E
Townsend
avalanche
anode wires cathode pad plane
Cherenkov
photon
Townsend
avalanche
thin layer (300 - 500 nm) of
CsI on the cathode pad plane
Albert Einstein
the past and the present
Tom Ypsilantis

## Slide 18
OMEGA
DELPHI
TMAE(Tetrakis-Dimethylamine-Ethylene)
TEA (Tri-Ethyl-Amine)
SLD - CRID
CLEO III
E605
RICH with gaseous PD’s
the first generation: photoconverting vapours

## Slide 19
Thanks to RD26
François Piuz
1992, F. Piuz et al. Development of large area advanced fast-RICH detector for particle identification at LHC operated with heavy ions
  TO ACHIEVE HIGH CsI QE:
  Substrate preparation:
  Cu clad PCB coated by Ni (7 µm) and Au(0.5 µm), surface cleaning in ultrasonic bath, outgassing at 60 oC for 1 day
  Slow deposition of 300 nm CsI film:
  1 nm/s (by thermal evaporation or e--gun) at a vacuum
  of ~ 10-7 mbar, monitoring of residual gas composition
  Thermal treatment:
  after deposition at 60 oC for 8 h
  Careful Handling:
  measurement of PC response, encapsulation under dry Ar, mounting by glove-box.
The best quartz cuts here
A. Di Mauro, NIM A 525 (2004) 173.
Schematic structure of the COMPASS Photon Detector:

## Slide 20
TIC, NA44
COMPASS
RICH-1
JLAB-HALL A
ALICE-HMPID
STAR
HADES
A solid state photocathode exposed to a gaseous atmosphere in an effective PD: a success !
RICH with gaseous PD’s
the second generation: MWPC’s + CsI

## Slide 21
COMPASS: 8 MWPC’s with CsI
built in 1999 – 2000,
after prototypes tests
(RD26 development )

## Slide 22
The CsI photocathodes

## Slide 23
Good performance in low gain configuration
photons / ring (b ≈ 1, complete ring in acceptance) : 14
sq-ph (b ≈ 1) : 1.2 mrad
sring (b ≈ 1) : 0.6 mrad
2s p - K separation @ 43 GeV/c
PID efficiency ~ 95% for q Ch > 30 mrad
except for the very forward region
After a long fight for increasing electrical stability at high m.i.p. rates and systematic studies at the CERN GIF we came to the same conclusion as Ypsilantis and Seguinot:
J. Seguinot et al., NIM A 371 (1996), 64:
CsI-MWPC with 0.5 mm gap to minimize ion collection time, fast front-end electronics (20 ns int. time):
stable operation is not possible at 105 gain because of photon feedback, space charge and sparks

## Slide 24
  MWPCs with CsI photocathodes in COMPASS:
  beam off: stable operation up to > 2300 V
  beam on: stable operation only up to ~2000 V
  (in spill ph. flux: 0 - 50 kHz/cm2 , mip flux: ~1 kHz/cm2)
  Whenever a severe discharge happens, recovery takes ~1 day.
  Photocathode aging:
  - our information from accidental contamination
  - very detailed study by Alice team
effective gain ~ 104
pe detection efficiency ~ 70%
cluster amplitude distribution:
limits of MWPC’s with CsI in COMPASS

## Slide 25: the central region before 2006
THE EXPERIMENTAL ENVIRONMENT
huge uncorrelated background related
to the memory of the MWPCs + read-out
overlap of
event images
m beam
1 mC/cm2
0.2 mC/cm2
Accelerated ageing test H. Hoedlmoser et al., NIM A 574 (2007) 28.

## Slide 26
12 outer CsI cathodes: change electronics (use APV25-S1)
4 central CsI cathodes : remove and insert frames with MAPMTs and lense telescopes
Same mechanics as CsI photo-cathode frame
upgrade of RICH-1 with MAPMT’s in the central region (2006)
photons
MAPMT
concentrator
field lens

## Slide 27
MAPMT’s have:
  wide wavelength range
  time resolution < 1 nsec
  short detection system memory (MAPMT + read-out)
  adequate for high rate operation
  robustness
  high efficiency for single photon detection
photons
MAPMT
concentrator
field lens
challenges:
    large ratio of the collection and photocathode
    areas with minimal image distortion
     ratio = 7.3  critical LENS SYSTEM design
    UV range  fused silica LENSES
    couple to a read-out system able to guarantee
    efficiency, high rate operation and to preserve
    time resolution
- C4F10 refractive index
- CsI sensitivity range
- MAPMT’s range
The difference

## Slide 28: THE LENSES
material:
fused silica, Corning 7980,
concentrator
aspheric
surface
field lens
complex and delicate
mechanical machining
Fused Silica
Borosilicate glass
Polymer lenses
200 400 600 l(nm)
fraction of photons detected
0 0.5 1
-if no reflection
with monolayer of MgF2
w/o antireflective layer
+8.4% photons
with MgF2
Convolution of Cherenkov light and effective QE
spherical s.
planar s.
aspherical s.
ZEMAX optimization:

## Slide 30: MAPMT: HAMAMATSU R7600-03-M16
  16 anodes
  UV extended glass
recall:
effective QE including
window losses
(collection efficiency not included)
FE cards plugged
directly here
protects against
B ≤ 200 G
and guarantees
good alignment
home made voltage divider
Quantum efficiency (%)

## Slide 32: MAPMT GAIN AT HIGH RATE
mean signal amplitude versus rate/pixel
pulsed light source synchronous to trigger +
random background from lamp
measured for single photoelectron
Working HV
operate with single photoelectron
rates up to 5MHz/pixel
CROSS-TALK RATE
10 fC threshold
cross-talk rate < 0.1 %
AND
cross-talk rate

## Slide 34: The Upper Detector from inside

## Slide 35: The central part of the lower detector

## Slide 36
number of photons and resolutions
estimated photoelectron detection time resolution: ~320 ps

## Slide 37
time resolution is useful for correctly assigning hits to rings

## Slide 38
PID from the likelihood function

## Slide 39
M (GeV/c2)
2004 data

## Slide 40: Improved PID performances
M (GeV/c2)
2004 data
2006 data

## Slide 41
Identification and misidentification probability

## Slide 42
Purity of K samples

## Slide 43
RICH PID information
in the Do analysis
without RICH information
with RICH information
COMPASS 2006 Do peak

## Slide 44
6 consecutive years of COMPASS data taking
up to 15 days of data taking per sample
identical cuts applied to the reconstructed particle trajectories (track quality)
Study of long term CsI QE variations
    Principle:
    Extract the mean number of detected photons per particle from the data collected during six years of COMPASS data taking
RATES IN THE EXTERNAL DETECTORS during SPS spills:
Photoelectrons < 10 Hz / cm2
MIPs < 10 Hz / cm2
 Integrated charge over 6 years < 10 mC/cm2
MAPMTs
M. Alexeev et al, 2014 JINST 9 P01006

## Slide 45
only identified p’s
only rings fully contained in a single cathode
count Nph (detected photons) of each ring
(background cannot be disentangled at this stage)
1 mrad wide qCh bins  N = < Nph >
Cherenkov photons : Poisson distribution
 detected photons : Poisson distribution
at least 1 detected photon
measured N is biased, corrected
measured: m’
m solving numerically the equation
FIT THE DISTRIBUTION:
Data selection, correction and fit
corrected
Frank and Tamm distribution
Background (flat distribution assumed)

## Slide 46
distributions
and fits (>25 mrad)
2006 data
c2 theoretical
NDF = 18
Fit results stable versus:
fit range variations
different ring selection:
at least 2, 3 photons
estimated systematic error: 0.7 x sstat
use N(qCh = 55.2 mrad)
for extrapolation
Fit quality, consistency and stability

## Slide 47
N(qCh = 55.2 mrad)
vs year
(statistical errors)
Frank and Tamm
background
Too few photons:
not used in the following
MEAN OVER 11 CATHODES
(statistical & systematic errors)
results

## Slide 48
<N> vs year is compatible
with no CsI QE variation
max CsI QE variation
rate : 2.3 % / year
[1 “COMPASS year” :
~6 months of data taking]
For the 3 most critical cathodes:
max CsI QE variation rate : 5.2 % / year
Estimated systematic error of the measurement: 2 % /year
Errors enlarged to get 50% probability for the linear fit
<N> corrected for
lower HV (-20V)
CsI photocathodes can preserve QE over years
The CsI QE decrease is modest

## Slide 49
COMPASS II PID requirements
Exclusive meson production channels have low cross-section
Precision measurements require not just high efficiency but also very stable response
MWPC + CsI operate at low gain  depend on p, T, threshold and background stability
but we need precise comparison of data with different background levels
Reduction of systematics from photon detectors  larger gain and faster signals
PMTs not adequate because of large angular acceptance  only small demagnification
factor of optical system allowed (large distortions); 5 m2 of PMTs not affordable.
MPGD-based Photon Detectors are the best option
A dedicated R&D project to develop THGEM-based PDs started 6 years ago and
rececently achieved positive conclusions
The R&D status and progress will be presented by Stefano Levorato on Friday
We have decided to replace COMPASS RICH-1 MWPC’s with the new detectors

## Slide 50: 2016 COMPASS RICH-1 upgrade
radiator:
C4F10
5 m
6 m
3 m
MWPC’s + CsI
UV mirror
wall
Al vessel
radiator gas: C4F10
PMTs
beam pipe

## Slide 51: 2016 COMPASS RICH-1 upgrade
radiator:
C4F10
5 m
6 m
3 m
MWPC’s + CsI
UV mirror
wall
Al vessel
radiator gas: C4F10
PMTs
beam pipe
THGEMs + CsI
Foreseen for 2016-2017

## Slide 52: New PD’s

## Slide 53: The THGEM+Micromegas version

## Slide 54: The THGEM+Micromegas version

## Slide 55: The THGEM+Micromegas version

## Slide 56: The THGEM+Micromegas version

## Slide 57: The THGEM+Micromegas version

## Slide 58: The THGEM+Micromegas version

## Slide 59: spares

## Slide 60: The keys of the success
A strong physics case
An outstanding project leader
A dedicated, highly motivated team
A constant support from the Institutes and the Experiment
The enthusiastic contribution from many colleagues:

## Slide 61: To work safely inside our “confined space”
  COMPASS RICH is a CONFINED SPACE: authorized people
  only can enter .
  - authorization requires a formation course and a medical
  certification: for the first time CERN asked for the latter
  to be done by the institute.
  - a scaffolding had to be mounted inside the RICH
  (the old one does not conform to the new rules).
  We managed to provide:
  1) formation: general confined space course from CERN
  2) formation: specific course on risks inside COMPASS RICH
  3) definition and agreement on the medical protocol
  4) medical exams and production of medical certificates
  4) detailed definition of the activity and formalization of the specific procedures.
  5) opening of the RICH with Fire Brigades, GLIMOS, Supervisor, TSO, CERN confined space responsible, etc.
  6) authorization to enter by radiation protection personnel, formed, checked and authorized for entrance
  7) special formation course and authorization for us to mount a borrowed scaffolding
  (it can only be mounted by authorized personnel, but they were not authorized for confined space …)
  8) mounting of the scaffolding by ourselves
  6) formation and authorization to enter for the responsible of the scaffolding to check our mounting and
  authorize using it
  7) … 8) … 9) … 10) …
  EVERYBODY (CERN Medical Service, TIS, GLIMOS, …) have been extraordinarily collaborative…

## Slide 62: Few months after the end of the run
highest photon flux region
accumulated charge:~ 1 mC/pad
wires
accidental exposure to air of one CsI cathode

## Slide 63: CsI surface at microscope (x 1000)
10 mm
“white strip”
normal

## Slide 64: SCHEDULE OF ASSEMBLING
Preliminary studies up to October 2004
Project design November 2004 – March 2005
Material procurement and constructions April 2005 - March 2006
Assembly April-May 2006
Ready for beam June 2006

## Slide 65: When the detector was ready …
With the MAPMT’s and electronics

## Slide 66: We moved out of the assembling area
It was May 18, 2006. A beautiful sunny day in Geneva.
At 11:45 the detector was ready for craning.
Suddenly a bang was heard.

## Slide 67
In few seconds the protections were removed and that’s what was seen:

## Slide 68: Immediate reaction
The repair started on the same day
Spares of all pieces, including the large quartz windows were available
The accident was carefully studied and understood in detail (20 mbar overpressure)
One month later, in time for the start of the run, the repaired detector was installed

## Slide 69: OPTICS QUALITY CONTROL WITH THE HARTMANN METHOD
image centroide
Theoretical
reference
He-Na laser
632 nm
optical system
under test
Lens focus
Detected
Image
(CCD camera)
Hartmann plate
for parallel light
1. the principle
2. the images
3. the analysis
tolerance
(= center points +/- 0.1 mm)
576 TELESCOPES:
A) ~70% within 50 µm tolerance
B) ~20% within 100 µm tolerance
C) ~10% within 150 µm tolerances

## Slide 70: MAPMT Quality Control
measured @ 360 nm
PROTOCOL – 2 h / MAPMT
Visual Inspection (Pixel grid o.k.)
Noise rates and dark current
Scope Image stored
Signal shape, uniformity, gain
  measuring ADC distribution @ several Voltages
Quantum efficiency
  measurement with blue LED and UV LED
Individual ADC
spectra for each
channel, voltage,
wavelenght
gain vs HV for each
MAPMT anode
out of 620 MAPMTs
less than 10 MAPMTs not fully satisfactory, mainly due to the dark current requirement:
I dark < 2 nA/ch after ½ h in dark

## Slide 71
with without PID
RICH PID information in Λ analysis
Λ  p π-
Λ  p π+
with without PID
purity increased by 6, loss < 3%
purity increased by 7, loss < 3%
without with p identification

## Slide 72: FIT CHECKS
Rings with al least
1 2 3 photons
Fit ranges:
25 – 45 mrad (25 – 40 mard)
20 – 40 mrad (20 – 35 mard)
15 – 35 mrad (15 – 30 mard)

## Slide 73: COMPARING THE 6 DATA SETS
POTENTIAL SOURCES OF SYSTEMATIC EFFECTS
different beams (m, h) and beam momentum
  different background and secondary multiplicities
   signal and background contributions are separated in the analysis
HV fixed, -20V (over 2kV) in 2010, 2011: small effect ~ 2.3% N decrease
differences in parameters:
  T, P, electronics threshold
   systematic effect estimated
procedure self-correcting for the
variation of the refractive index
(P, T, residual N2 content)
  n-1 = (1422 - 1537) * 10-6
  gas transparency:
   negligible variations
  (constant monitoring)