## Slide 1
The coordinate-tracking setup based on
the drift chambers for ultrahigh-energy
cosmic ray investigations
E.A.Zadeba, N.V. Ampilogov, N.S. Barbashina, A.A. Borisov,
A.G. Bogdanov, D.V. Chernov, S.S. Khohlov, R.P. Kokoulin,
A.S. Kozhin, K.G. Kompaniets, V.V. Ovchinnikov, R.M.
Fakhrutdinov, A.A. Petrukhin, V.V. Shutenko, I.I.Yashin.
BINP, Novosibirsk, 2014
National Research Nuclear
University MEPhI
Institute for High Energy Physics
Instrumentation for Colliding Beam Physics INSTR14

## Slide 2: Neutrino experiment at accelerator U-70

## Slide 3: Drift chamber
Spatial resolution ~ 1 mm
Angle resolution ~ 30 mrad
Two track resolution ~ 5-6 mm
Gas mixture: 94% Ar + 6% CO2
Max drift time < 6 µs
Drift velocity – 0,04 mm/ns
Electric field – 450 V/cm

## Slide 4: Structure of the chamber
Wire | Diameter, µm | Potential, kV
Signal | 64 | 2.2
Dummy | 200 | 2.2
Cathode | 200 | 0
Field forming | 200 | -12

## Slide 6: Cherenkov Water Detector NEVOD
Water volume of 2000 m3
9×9×26 m
91 quasi-spherical module
546 photomultipliers

## Slide 8: Experimental complex NEVOD-DECOR
Total area of 4 super-modules of DÉCOR ~ 35 m2
This is less than 15% of side area of CWD
Spatial resolution ~ 0.8 cm
Angle resolution ~ 1°
Two track resolution ~ 3 cm

## Slide 9: Experimental complex NEVOD-DECOR
Total area of 4 super-modules of DÉCOR ~ 35 m2
This is less than 15% of side area of CWD
Spatial resolution ~ 0.8 cm
Angle resolution ~ 1°
Two track resolution ~ 3 cm

## Slide 10: Project of coordinate detector

## Slide 11: Project of coordinate detector

## Slide 12: Project of coordinate detector

## Slide 13: Project of coordinate detector

## Slide 14: Project of coordinate detector

## Slide 15: Project of coordinate detector
Total sensitive area of detector (with 264 chambers) is about 270 m2
Consumption of gas is 10 liters of CO2 and 150 of Ar per hour

## Slide 16: Stages of project development
Primary test for pressure leak and integrity of wires
  Study of the basic characteristics of the chamber with a coordinate-tracking detector URAGAN
Development of hodoscope-like test bench
  Working out the methods of reconstruction of tracks in several coordinate planes
  Serial testing of the drift chambers and other detectors
Development of the TREK prototype for a joint operation with Cherenkov water detector

## Slide 17: Test bench for drift chambers, based on coordinate-tracking detector URAGAN
Efficiency
The accuracy of reconstruction
Drift velocity
Development of reconstruction method

## Slide 18: Hodoscope test bench for drift chambers

## Slide 19: Hodoscope facility for drift chambers
7 chambers in X и Y planes
Area of X и Y-plane – 12,7 m2
Max zenith angle - 73°
Coordinate resolution ~ 1 mm

## Slide 20: Prototype of TREK
Cluster area
– 16 m2
DECOR Short
– 17,5 m2

## Slide 21: Summary
Project of large-scale coordinate-tracking setup is now under development
Drift chambers from neutrino experiment of U-70 were successfully removed
Most part of drift chambers passed primary test for leaks and wire integrity
The possibility of joint work of EC NEVOD cosmic ray detectors and IHEP drift chambers was proved

## Slide 22: Thank you!