## Slide 1: CMS Alignment and Calibration
Yuriy Pakhotin
on behalf of CMS Collaboration

## Slide 2
CMS Detector at LHC
(88%)
LHC: proton-proton collider
(87%)
2011, TeV
2012, TeV
*No results from Heavy-ions collisions in this talk

## Slide 3
Higgs Boson: from original idea to observation
Higgs boson observation: July 4th, 2012
  Reports from CMS and ATLAS on special event at CERN
  http://indico.cern.ch/conferenceDisplay.py?confId=197461
It took almost 50 years to find Higgs
1964

## Slide 4
No discoveries possible without perfectly working detector
Smooth road to the discoveries essentially depends on calibration and alignment of the detector sub-systems internally and with respect to each other
Detector Calibration and Alignment
Sorry, not today
In spotlight of this talk!

## Slide 5
CMS Detector “Onion” Structure
2008 JINST 3 S08004
Total weight: 12,500 t
Diameter: 15 m
Overall Length: 22 m
Magnetic field: 4 Tesla
CMS is a complex detector:
Largest silicon tracker (~76M channels)
Homogeneous ECAL (76k crystalls)
Multilayers muon system (25k )
Largest superconducting magnet (B=4 T)
Muon system:
momentum resolution:
acceptance
Calorimetry:
  Hadron |η|<5.0, δE/E ~ 100% / √E + 5%
  Electromagnetic |η|<3.0, δE/E ~ 2.8% / √E + 0.3%

## Slide 6
Searches for new physics demand excellent knowledge of detector in terms of resolution
Near-detector calibration constants (pedestals, gains, etc.) are determined online
Rapidly changing detector conditions derived synchronously with data-taking and promptly used in first processing of data
  derived within ~24-48 hours after data collection
  important for fast physics analyses
Stable and improved conditions determined with state-of-the-art event-based alignment algorithms utilizing data sample accumulated over a longer range of time and used for data re-processing
  usually derived within ~1 month after data collection
  internal dependencies between alignment and calibration of different subsystems are accounted
Large data rate requires robust computing framework to handle alignment and calibration workflows utilizing special data formats to reduce bandwidth and disk space (AlCaReco)
Alignment and Calibration Strategy

## Slide 7
Two main alignment and calibration frames: prompt and offline
Alignment and Calibration Workflow
Prompt Alignment and Calibration
Offline Alignment and Calibration
Data Streams
Data-acquisition
Data Flow
Prompt Loop
Data
Re-reco

## Slide 8
Low latency workflows run immediately after the data-taking:
  Beam-spot position: measured frequently (every Luminosity Section)
  ECAL response corrections: frequently measured with laser pulses
Monitor conditions (update if necessary):
  Tracker problematic channels: HV trips/noise
  Calorimeter problematic channels: mask hot channels
  Pixel alignment: monitor movements of large structures using tracks
Use delay between express and prompt reconstruction to include derived conditions in first data processing
Prompt Alignment and Calibration

## Slide 9
A value is measured every Luminosity Section (23 s)
  use tracks from express stream
Position of the beam-spot in transverse plain (, ) and slopes determined from fit using reconstructed minimum bias tracks
Beam width ( and ), length () and position () come from fit to primary vertices
The calibration strongly dependent on alignment of Pixel detector
  Beam-spot is recomputed offline every time Pixel alignment is updated
Calibrate Beam-spot Position

## Slide 10
Cylindrically symmetrical Pixel detector is physically separated into two half barrels
Corrections for relative displacements along between the barrels are time-dependent
Monitor longitudinal separation (within mechanical tolerance) using unbiased track-to-vertex residuals
  done for every run ( events) using express strem
Time dependence of pixel structure alignment accounts for separation as a function of time
  b-tagging algorithms insensitive to remaining 10 m effect
Monitor Movements of Pixel Large Structures

## Slide 11
ECAL crystals temporary change transparency due to irradiation
  less significant in barrel, more pronounced in endcaps (where photo-detectors get conditioned by strong irradiation)
Damage/recovery cycles monitored by laser pulses (447 nm, 100 Hz in LHC abort gaps) and photo-detectors measuring the response variation to the laser light
  continuous monitoring, the whole ECAL measured in 40 min
  use dedicated stream at trigger
Corrections derived within 48 h and applied to prompt reconstruction
Monitoring the ECAL Response
Stable mass resolution

## Slide 12
All subsystems are aligned and calibrated offline
Offline Alignment and Calibration

## Slide 13
Tilts of the Tracker relative to magnetic field (flux along global ) could result in biases of the reconstructed track parameters
  need to be corrected
The global Tracker orientation is described by the angles and that correspond to rotation around global and axis of the CMS
Goodness of track fit scans for various tilt angles
  mrad, mrad
Tracker Orientation w.r.t. -field
Goodness of tracking fit

## Slide 14
The track-based alignment with MillePedeII minimization algorithm expected to provide precision
The CMS Tracker is a complex system:
  24k sensors in total
  free parameters per sensor (a sensor depends on other sensors)
    5(6) rigid body + 3 bow parameters for each sensor
Example: the 2011 alignment campaign with 1 fb-1 of reconstructed data
  inputs: 15M loosely selected isolated muon tracks
  3M low momentum tracks
  3.6M cosmic ray tracks
  375k muon track pairs from
  Z-mass measurement as a constraint
  Fitting sensor bows and kinks
  Time dependent (9 intervals) rigid body
  alignment for large pixel structures
Enormous computing task!
Precision estimated from the RMS of the Distribution of the Medians of the Residuals for each module
  more robust against Multiple Scattering
Tracker Alignment with Tracks

## Slide 15
Hardware based: measures positions of all chambers with respect to a floating network of rigid reference structures ( and mm)
  provides physically bound constraints on track-based alignment
Track based: minimizing the residuals which are the differences between measured (with segments) and predicted (propagated from Tracker) position of the muon in the chamber (m)
  more details in poster session
Combination (and comparison) of the methods
Muon System Alignment
Muon segment
from hits
Muon track
from tracker
muon from collision
“reference”
“target”

## Slide 16
Beyond 200 GeV, the muon system can contribute significantly to overall momentum resolution due to large lever arm
Precise muon alignment becomes essential for searches with high muons (e.g., )
Why the Muon System Misaligned?
  Deformations due to gravity force (~10 mm)
  Barrel shrinks & endcaps bend due to magnetic force (~10 mm)
  Repositioning after detector open/close operations (~1 mm)
  Imperfect positioning during installation (sub-mm)
  Temperature effects (sub-mm)
Why the Muon Alignment Important?
Muon system only
Inner tracker only
Full system
TeV
, GeV

## Slide 17
Inter-calibration of crystals located within the same ring:
  -symmetry of the energy flow trough the ECAL crystal (- days)
  invariant mass peak ( months)
  : high energy electrons from and decays (once in a year)
Key feature: dedicated streams at HLT with reduced event content
  kHz of ZeroBias events for -symmetry and a total of kHz for
Combination: weighted average of the 3 methods
The calibration determines energy scale and resolution
Offline ECAL Calibration

## Slide 18
All offline alignment and calibration constants are thoroughly validated before injection for data reprocessing
  “standard candle” process used by many system
Validation
Muon System
ECAL
Tracker

## Slide 19
All constants stored in SQL Data Base for global access by data processing computing jobs from all over the World
  All CMS Tiers must use the same conditions
Set of matching constants is identified via “tag”
  complete and consistent as required for data processing
  simple access for non-expert users (undergraduates and distinguished professors)
  experts can customize used constants
Alignment and Calibration Constants Storage
Tracker
Alignment
Muon
Alignment
ECAL
Calibration
System XYZ
Alignment
TkAl_v1
TkAl_v2
MuAl_ver1
MuAl_ver2
MuAl_ver3
ECAL_1
^&^&^&
*%#$@!
GR_P_V41
Tags:
START53_V7A

## Slide 20
The CMS alignment and calibration infrastructure proved to be efficient and effective for a fast analysis turn-around during data taking in 2011 and 2012
The prompt alignment and calibration mechanism:
  Designed for low latency workflow run smoothly during Run1
  Better quality of physics reconstructed objects already during very first processing of data
The offline calibration and alignment procedure:
  Increasing time/space granularity of the calibrations and thus precision
  Delivering to reconstruction the best knowledge of detector performance based on state-of-the-art algorithms
  Account for inter-dependencies among the different systems and workflows
Calibration and alignment has been crucial step towards the successful physics program of CMS during 2010-- 2012
Revision of main workflow is under study
  Goal is to keep the high standard
Looking forward to Run2 in 2015 and possible discoveries!
Summary

## Slide 21
Back-up Slides

## Slide 22
Pixel detector: 66M channels
  pixel size
  3 barrel layers, endcap wheels
  span to beam cm
Strip detector: 10M channels
  10 layers and of silicon
  largest silicon tracker!
  span to beam cm
CMS Inner Tracker
Barrel
Endcap wheel

## Slide 23
Muon residual is difference between measured (with hits) and predicted (i.e. propagated from Tracker) position of the muon in the chamber
Residuals calculated in chamber’s local frame
  hit (layers) based muon re-fit is used
  local residual x = track local x – hit local x
  scattering in iron  width of residual distribution
  chamber misalignment  non-zero mean of distribution
Residuals in Track-based Muon Alignment