## Slide 1: Time-Projection-Chamber for MPD NICA Project
Stepan Vereschagin
On behalf of the TPC team:
A.Averyanov, A.Bajajin, V.Chepurnov, S.Chernenko,
G.Cheremukhina, O.Fateev, A.Korotkova, F.Levchanovskiy,
J.Lukstins, S.Razin, A.Rybakov, S.Vereschagin, Yu.Zanevsky,
S.Zaporozhets, V.Zruyev
TPC/MPD Collaboration
Laboratory of High Energy Physics, JINR, Dubna
Novosibirsk, 2014

## Slide 2: CONTENS
TPC design overview
Field cage and central cathode plane
TPC readout chamber (ROC)
Front-End electronics (FEE)
TPC laser calibration
Gas system
Cooling system
Conclusion

## Slide 3: General view of the MultiPurpose Detector (MPD) NICA project
SC Coil - superconductor solenoid
IT - inner detector
ECT - straw-tube tracker
TPC - time-projection chamber
TOF - time-of-ﬂight stop counters
FD - The fast forward detectors
ZDC - zero degree calorimeter
BBC - beam-beam counter

## Slide 4: TPC design overview
12x2 Readout
chambers
HV-electrode
Field cage
beam
beam
E
The overall acceptance on │‌η│~ 1.2
The momentum resolution ~ 3% in pt interval from 0.1 to 1 GeV/c
Two-track resolution ~ 1 cm.
Charged particle multiplicity ~ 1000 in a central collisions
Hadron and lepton identification by dE/dx measurements with resolution better than 8%
Physics requirements:

## Slide 5: Main parameters of the TPC
Length of the TPC | 340 cm
Outer radius of cylinder | 140 cm
Inner radius of cylinder | 27 cm
Length of the drift volume | 170cm (of each half)
Magnetic field strength | 0.5 Tesla
Drift gas | 90% Ar+10% CH4
Temperature stability | 0.5°C
Gas amplification factor | ~ 104
Number of readout chambers | 24 (12 per end plate)
Pad size | 5x12mm2 and 5x18mm2
Number of pads | 95 232
Pad raw numbers | 53
Maximal trigger rate | ~5 kHz
dE/dx | better than 8%
∆p/p | ~ 3% in 0.1< pt<1 GeV/c

## Slide 6: The front view of the TPC
Four cylinders (green circles: C1 - C4) are required to make the complete field-cage structure.
All four TPC cylinders are under construction in Russian Industry as monolithic Kevlar composite constructions. Kevlar thickness is 4 mm.
Such an approach allows one to minimize problems with gluing of field cage parts and fragments.
Moreover, we suppose to mount field cages, central electrode and end plates as independent precisely adjusted constructions which will be inserted between Kevlar сylinders and fixed together mechanically and with epoxy.

## Slide 7: Construction of TPC cylinders
Material : Kevlar
Thickness: 4 mm
Length: 3.4 m
Diameter: 2.8 m
Deformation in operational position is less than 100 mkm

## Slide 8: Field cage and central cathode plane
TPC prototype under constraction
TPC prototype field cage

## Slide 9: Field cage
The field distortions in the drift volume defined by mylar strip system a) precisely placed strips b) one strip is shifted by 50μm
The distortions are down to 10-4 at ~23mm from the strip surface inward drift space. The positioning precision of the strips into nominal place has to be not worst than 50μm.
✔Along the line parallel the strip surface(orange line)
✔Inward the drift space (violet line)
The non uniformity of the electric field inside the sensitive TPC volume has to be not more than 10-4 relative to nominal value (140V/cm P10 gas mixture)
The dependence of the size of the worst region with the field distortion more than 10-4

## Slide 10: Readout chamber
Insulation plate
Pad plane
Structure of readout chamber:
- three wire planes
- pad plane
- insulation plate
- trapezoidal aluminum frame
Wires structure
- anode wire pitch 3 mm
- cathode wire pitch 1,5 mm
- gate wire pitch 1 mm
- wires gap 3 mm
Pad structure
pad raw number 53
rectangle shape
- small pads 5×12 mm2
- large pads 5×18 mm2
Al-body

## Slide 11: TPC readout chamber: Al body
The aluminum frame provides the overall mechanical stability of the readout chamber. Its stability against deformation caused by wire stretching has to provide as minimal as possible overall deformation less than the expected wire sag caused by electrostatic forces.
The frame is reinforced by stiffening rib
The deformations do not exceed 27 mkm
at the total wire tension ~ 800 N and
over pressure inside TPC up to 5 mBar
Finite element calculation of the deformation of the readout chamber caused by the wire tension and over pressure inside TPC

## Slide 12: Front-End Electronics
Signal to noise ratio, S/N - 30
NOISE < 1000e- (С=10-20 pF)
Dynamic Range - 1000
Zero suppression
Buffer (4 / 8 events)
Front-End Electronics prototype (USB2.0)
3d-model of the new Front-End Electronics
PASA
PASA
ALTRO
ALTRO
ALTERA
FPGA
Microsemi
FPGA

## Slide 13: Block diagram of FEE base

## Slide 14: FEE Testing

## Slide 15: TPC testing
Prototype 1 under preparing
to test with UV laser.
General view of the laser
beams inside TPC.
UV laser tracks reconstructed in Prototype 1.

## Slide 16: TPC Laser Calibration System
There are 224 laser beams whole TPCin
Mirrors reflect
beam at 900
Laser NL313-10
Semitransparent
mirror
Scheme of high power laser beam splitting into 112 “tracks” of 1 mm diameter.
In order to minimize the error in the absolute position measurement by TPC, it is necessary to take into account both static and time-dependent distortions in the drift path of the ionization cloud. A calibration system that can reproduce fiducial tracks is needed to monitor the TPC performance. This calibration system will be based on the UV laser.

## Slide 17: TPC gas system
Schematic view of the TPC gas system structure
Requirements
90%Ar+10%CH4
The drift volume is 18500 liters,
the insulating gaps – 4800 liters
Hermetically closed-loop gas circulation system
Dryer and purification in return line
Continuous monitoring of gas gain and drift velocity – gas chromatograph
Gas mixture temperature control - 0.5 K
Internal TPC pressure – 2 mbar
Recirculation flow - 3.8 m3 /h
CO
2
Ar
CH
4
N
2
TPC
Purifier
CO
2
Absorber
Buffer
Insulating gas
Gas quality
monitor
Exhaust system
Vent
Compressor
Insulating gap
Drift volume
Gas supply
Mixer

## Slide 18: TPC Cooling Scheme Preliminary estimation
Outer thermal screen
Front End Cards cooling
inner thermal screen
Resistor rods cooling
Bus bar cooling
Cover cooling
TPC gas volume, ∆T<0.50C
FEE/ROC dissipation < 400 W
Resistor rods 2 x 8 W
Bus bar < 500 W

## Slide 19: TPC cooling system
Flow rate:
• FEEC: 24 x 1m3/h
• ROC Covers: 24 x 0.2 m3/h
• Thermal screen: 24 x 0.5 m3/h
Total flow: 40 m3/h
Total heat to be removed: up to 10kW
Total Volume of water in the installation: 600L
Installed Electrical Power:
• Pump: 11kVA
• Heaters: 26kVA
Total Power: 37kVA
Number of Circuits:
• FEEC: 12+12
• ROC Covers: 2+2
• Therm screen: 12+6
• Resistor rods: 2+4
Total: 52
Reservoir
Temperature Sensors
Heat Exchanger
at Exchanger
Circulator Pump
Shut off valve
Heater
TPC
pressure in cooling loops is kept below atmospheric pressure

## Slide 20: Temperature Monitoring
Sensors: blue – on the field cage, red on the chambers
Location | Outer Field cage | Inner Field cage | ROC modules
Number of the sensors | 72 | 36 | 72

## Slide 21: Conclusion
Design of main parts of TPC are performed.
Three of fours TPC cylinders are constructed.
Technological Prototype TPC was designed, constructed and tested with laser beam and cosmic.
Readout Chamber (RoC) is designed and full size prototype is under construction.
The prototypes of FEE are constructed and tested.
Software is under developing.
Laser calibration system is designed.
Gas and Cooling systems are under designing.

## Slide 22
Thank you for attention!
and welcome to collaboration.

## Slide 23: ENERGY LOSS
The energy loss distribution in the MPD TPC
D
H3
He3
He4
P
P
K
π
e
PID: Ionization loss (dE/dx)
Separation:
e/h – 1.3..3 GeV/c
π/K – 0.1..0.6 GeV/c
K/p – 0.1..1.2 GeV/c
TPC FEE input full scale amplifier ~ 200 fC
It is ~ 30-40 MIP energy loss
QGSM Au+Au central collision
9 GeV, b=1fm

## Slide 24: Main parameters of the TPCs
Dimension | STAR TPC | ALICE TPC | MPD TPC
Length of the TPC | 420 cm | 500 cm | 400 cm
Outer Diameter of Vessel | 400 cm | 500 cm | 280 cm
Inner Diameter of Vessel | 100 cm | 170 cm | 54 cm
Cathode Potential | 28 kV | 100 kV | 28 kV
Drift Gas | Ar + CH4 (90:10) | Ne + CO2 + N2 [85.7 : 9.5 : 4.8] | Ar + CH4 (90:10)
Drift Velocity | 5.45 cm/µs | 2.65 cm/µs | 5.45 cm/µs
Number of Readout Sectors | 12×2 = 24 | 2×2×18 = 72 | 12×2 = 24
Number of Pads | 136 608 | 557 568 | 95 232
Pad Rows | 13 – inner subsector 32 – outer subsector | 32 – inner chamber 64 – outer chamber | 53
Pad Size | 2.85×11.5 mm2 – inner subsector 6.2×19.5 mm2 - outer subsector | 6×10 and 6×15 mm2 | 5×12 mm2 and 5×18 mm2
Magnetic Field | 0.25 T, 0.5 T | 0.5 T | 0.5 T
Electronics | ALTRO based | ALTRO based | ALTRO based
dE/dx resolution | 7.0% | 5.0% | 8.0%

## Slide 25: ALICE TPC FEE
FEC in Cu
sandwich
6 cables
per FEC
128 ch/FEC