## Slide 1
Bocheng Jiang on Behalf of the SSRF Accelerator Team
Jun 25-28 2018 Novosibirsk, Russia
SSRF storage ring improvement in beam line phase II project

## Slide 2: Contents
Introduction of SSRF
Introduction of beam line Phase II project
Storage ring upgrades
  Lattice upgrade
  Cryogenic system
  3rd harmonic cavity
  Insertion devices

## Slide 3: Introduction of SSRF
Shanghai Synchrotron Radiation Facility is
a 3rd generation light source in main land China. Located in Zhangjiang High tech-park, Pudong, Shanghai.
Based on a 3.5GeV electron storage ring with emittance 4 nm rad.

## Slide 4: SSRF Complex
DBA lattice
7 beam lines on Phase I project
6 users’ beam lines

## Slide 5
2004 ground breaking。（250Million USD）
2007 finished installation and commissioning started.
2009 open to users.
2012 Achieve op up operation (200mA->260mA).
2013 Fast orbit feedback, orbit stability sub micron.
2016 beam line phase II project started.
Introduction of SSRF

## Slide 6
Operation status
Chart: 
| 2009～2010 | 2010～2011 | 2011～2012 | 2012～2013 | 2013～2014 | 2014～2015 | 2015～2016 | 2016～2017
Availability(%) | 96 | 96.1 | 98.5 | 97.1 | 98.7 | 98.3 | 97.9 | 97.2
MTBF(hrs) | 36.3 | 43.7 | 72.8 | 54.7 | 79.4 | 90 | 46.5 | 62.1
MDT(hrs) | 1.55 | 1.8 | 1.15 | 1.65 | 1.05 | 1.76 | 1.03 | 1.84

## Slide 7
海南3
黑龙江5
吉林6
辽宁8
山东11
福建7
湖北13
湖南6
内蒙古3
甘肃4
青海3
四川11
云南3
新疆3
江苏33
山西5
宁夏
河南4
陕西7
安徽11
贵州2
江西4
台湾2
广西3
广东13
International：
singapore3
Australia2
S Korea17
Japan5
Sweden1
Denmark1
Canada2
U.S.5
Portugesa1
Tailand1
Russia1
France2
New Zealand1
Saudi Arabia1
German 1
⊙重庆3
⊙北京73
⊙天津10
河北3
⊙香港5
澳门 ⊙
⊙上海77
浙江14
10多个研究领域
Introduction of SSRF

## Slide 8: Introduction of beam line Phase II project
Project contents
16条光束线站
16 beamlines
Storage ring upgrade
Supplementary lab
Beamline tech lab
Buildings
Energy, environment, material, physics, chemistry, biology
Lattice modification, 3rd harmonic cavity, Cryogenic system, Insertion devices.
Sample preparation lab for material, In situ environment lab, Chemistry & environment lab，biology & medical lab， Data center。
Optical tech lab, Machinery & Vacuum lab, Electric &control lab, X-ray diagnostic lab
Experimental hall、Supplementary lab building、Data center.
Total budget: ~250M USD,
From 2016~2022

## Slide 9: Introduction of beam line Phase II project
Experimental hall
Experimental hall
Experimental hall
Supplementary lab
Data center

## Slide 10: Introduction of beam line Phase II project
Disciplines | Beamline | Science goals
Energy science | E-line | energy conversion and control
 | D-Line | Structure of non-equilibrium systems
 | Radioactive materials | Radioactive material
 | Hard X-Ray Spectroscopy | Catalysis
Environ. Science | Hard X-ray Nanoprobe | Nano technology, cell, environ. components
 | Medium-energy Spectroscopy | environmental pollutants
 | 3D Nano Imaging | nano imaging
Material Science | Magnetic Dichroism | magnetic and electronic properties
 | Laue microdiffraction | local microstructure and defects
 | Surface diffraction | microstructure of surfaces and interfaces
 | Laser Electron Gamma Source | nuclear astrophysics/structure
Life Science | P2 Protein Crystallography | Moderate-risk infectious viruses
 | Membrane Protein | Membrane protein
Industry Applications | Ultra Hard X-ray Applications | engineering materials and rocks
 | Time-resolved USAXS | self-assembly and fiber-spinning
 | Fast X-ray imaging | Fast process imaging

## Slide 11: SSRF Beamlines layout

## Slide 12: Introduction of beam line Phase II project
As a part of Phase II beamline project, accelerator get an upgrade plan to satisfy users’ requirement. The major principle is as follows:
Lattice adjustment to accommodate more insertion devices.
Provide various kinds of radiation sources. (SW, SuperB, EPU)
Provide more operation modes. (Such as hybrid filling mode)
Increase the reliability of the machine.
The major upgraded systems during Phase-II project:
Proposed upgrade system | Purpose
Super-Bend lattice | Provide more straight sections, Increase the flux of the hard X-ray
New Cryogenic system | An online spare of the primary cryogenic system, increase the machine reliability, Provide liquid helium to 3rd harmonic cavity
Third harmonic cavity | Increase the current threshold of single bunch, increase the beam lifetime.
New IDs | Satisfy the users’ requirements for new beam lines.

## Slide 13: Storage ring upgrades
Lattice upgrade
C03, C13 replace 1.8m bend with 1m SuperBend
Creating 1.9m short straight section
Super Bend
ID11, ID16 long straight section add triplet create double mini beta function straight sections accommodate 2 IDs

## Slide 14: Storage ring upgrades
Lattice upgrade

## Slide 15: Storage ring upgrades
Parameter | Unit | Current | Upgrade
Energy | GeV | 3.5 | 3.5
C | m | 432 | 431.989
Tune |  | 22.22,11.29 | 22.222, 12.153
Emittance | nm rad | 3.9 | 4.22 (with SW)
Momentum compaction |  | 4.27e-4 | 4.2e-4
Energy spread |  | 9.8e-4 | 11.1e-4
Energy loss/turn | MeV | 1.44 | 1.7 (With SW）
Straight sections | m | 4×12, 16×6.5 | 4×12, 16×6.5, 2×1.9
Bunch length | mm | 3.8 | 4~8
Bend field | T | 1.27 | 1.27 2.29
Lattice upgrade

## Slide 16
ID11，ID16 upgrade had been finished and beam commissioning successfully.
Super Bends, combine sextupoles had been built
Vacuum system, Gird is in fabrication.
Storage ring upgrades
Lattice upgrade

## Slide 17
Refrigerator 650W/4.5K
60W@2K
LHe Dewar 2000L
Valve Boxes 4
Multi channel Transfer Line
Single channel Transfer Line
GHe Storage Tanks 2×100m3
O
MC
ORS
LN
2
Buffer
Main Dewar
Compressor Station & Tank Farm
Cold
Box
Mul
ti
-
channel
Transfer Line
Atm
N
2
phase
separator
V
L
P
P
300K return
S
T
Atm
HT
V
B
T
P
U
V
L
T
LP Tank
4.5K return from
cavities
300K
supply
80K return from
cavities
4.5K return from
dewar
80K return from
dewar
80K supply
4.5K supply
Atm
HT
VB
T
P
U
V
L
T
Atm
HT
VB
T
P
U
V
L
T
Atm
HT
VB
T
P
U
V
L
T
Buffer
Buffer
SRF Cavity
-
A
SRF Cavity
-
B
SRF Cavity
-
C
SRF Cavity
-
T
Atm
P
Storage ring upgrades
Cryogenic system
Operation mode:
1、Main cryo for 3 main RF cavity, Cryo-II for 3rd harmonic cavity @ 2K
2、Main Cryo or Cryo-II down, The other switched both for 3 main RF cavity & 3rd harmonic cavity @ 4K, with 3rd harmonic detuned.

## Slide 18
Current status
2 LHE tank had been installed
Foundation for Refrigerator is ready
Storage ring upgrades
Cryogenic system
Transfer Line had been installed

## Slide 19
Storage ring upgrades
3rd harmonic cavity
Passive super conducting cavity
2 Cells
Working at 2K, 1.5GHz
Harmonic rf voltage 1.4~1.8MV

## Slide 20
C05
For 3rd hamonic
3rd harmonic cavity
500MHZ Main RF cavity
Storage ring upgrades
3rd harmonic cavity
3rd harmonic cavity installed at ID05， occupy half of the straight section
Near main Rf cavity and Cryogenic hall

## Slide 21
ACB & 2K cold box
2K Multi-transfer line
Cryoplant
Harmonic
cryomodule
Main SRF modules & ValveBoxes
Test Cave
RF Hall
Storage ring upgrades
3rd harmonic cavity

## Slide 22
Lengthening effect
Longitudinal acceptance
Detuning
Tracking for transient loading
Long bunch train
Short bunch trains
Hybrid filling pattern
Storage ring upgrades
3rd harmonic cavity

## Slide 23
Storage ring upgrades
Insertion devices
In house built EPU ， IVU

## Slide 24
Storage ring upgrades
Insertion devices
CPMU
Beam test, 9th harmonic

## Slide 25: Super Conducting wigglers 4.2 Tesla, Periods 22.5, Period length 48mm
Prototype
3D design
Thermotat design
Superconducting wire coiling
Storage ring upgrades
Insertion devices

## Slide 26
Scheduale
Started2016年11月
Inspect
2022年11月
Building
Supplementary lab
Beam line
Accelerator
First batch installation
2018.12
2019.9
First batch beam line commissioning
2019.6
2nd bath beam line installation
2020.9
3rd batch beam line installation
2020.6
2021.9
2018.8
完成穿墙线基建
2018.12
竣工
2022年6月
Finished commission
2019.6
设备安装
试运行
Lattice upgrade
2018.12
3rd harmonic cavity
2020.6
2nd batch beam line commissioning
3rd batch beam line commissioning

## Slide 27
Thanks