## Slide 1: New Muonium Hyperfine Structure Measurement in J-PARC
K. Shimomura (KEK)
on behalf of the MuSEUM Collaboration
BINP, Novosibirsk

## Slide 2: What is Muonium ?
Muonium:
Bound state of a positive muon and an electron.
Hydrogen-like atom free from the finite size of the nucleon.
Most suitable for validation of bound state quantum electrodynamics (QED).
Theoretical and experimental precision of the hyperfine structure comparable.
Muon:
Elementary particle (lepton)
200 times heavier than an electron
Lifetime of 2.2 microseconds.
Notes: Hydrogen: limitation due to the internal structure of the proton
Positronium: limitation due to unknown non-logarithmic higher-order terms

## Slide 3
Not included QED weak hadronic correction
Fine Structure
explained by Dirac
Classical Lamb Shift
QED
Tomonaga, Shwinger,
Feynman
Mu Energy Diagram
From K. Jungmann

## Slide 4: Muonium Hyperfine Structure
Zeeman Splitting
n12+n34 = DnHFS
n12-n34 µ mm/mp µ mm/mp
m+
e-
m+
e-
DnHFS ≈ 4463 MHz
DnHFS: Mu Hyperfine Structure
Pure lepton
= point particle
Breit-Rabi diagram
Magnetic Field (T)
Notes: Microwave magnetic resonance technique

## Slide 5: Most Precise Test of Bound State QED
nHFS(exp) 4463.302 765 (53) MHz [12 ppb]
nHFS(theory) 4463.302 868 (271) MHz [61 ppb]
nHFS(QED) 4463.302 720 (253) (98) (3) MHz
(mm/me) (QED) (a)
nHFS(weak) -65 Hz
nHFS(had. v.p.) 232 (1) Hz
nHFS(had. h.o.) 5 (2) Hz
Experiment:
Theory:
Progress: PRA 86 (2012) 024501, PRL 112 (2014) 173004, PRD 89 (2014) 014034
QED calculation: Effort for 10 Hz accuracy in progress (by Eides et al.)
µµ/µp = 3.18334524(37) [120ppb]
mµ/me = 206.768277(24) [120ppb]
LAMPF Experiment (1999)
By Nomura
Notes: had. v.p. : hadronic vacuum polarisation
had. h.o : hadronic higher-order correction
Alpha: Fine structure constant – precision of alpha
Theorists are confident that muonium HFS can be calculated to 10 Hz, if needed (Eides,...)
Experimental value from Liu et al.

## Slide 6: Why Mu HFS measurement is so important?
g-2 E821(BNL) 0.5ppm 3.6s deviation
• Measurement of the deviation of muon spin direction (ws)
and muon momentum direction (wc) wa∝(g-2)/2=am
• The ratio to the proton NMR frequency is important!
mm/mp accuracy from direct measurement of 120 ppb.
q
⇒
am an independent precise muon mass measurement is required!
From g-2 storage ring
From Muonium HFS
W. Liu et al., Phys. Rev. Lett. 82 (1999) 711

## Slide 7: Related on proton radius puzzle
By Randolf Pohl’ s slide
0.8770 ±0.0045
0.8409 ±0.004
Muon atom spectroscopy
Electron scattering
Measurements of the proton radius:
Proton Zemach radius can be obtained comparison of muonium HFS and hydrogen HFS*.
*SJ. Brodsy et al., PRL.. 94, 022001 (2005),
Notes: The measured value of the proton rms charge radius from muonic hydrogen μ p is 10 times more accurate, but 4% smaller than the value from both hydrogen spectroscopy and elastic electron proton scattering.
There exists a 7.9σ discrepancy between electronic (ep atomic and ep scattering) and muonic extractions of the proton radius.

## Slide 8
Fig. 2 on PRL 104, 220406 (2010)
Fig. 6 on PRD90, 073004(2014).
a pseudo vector boson
a massive vector boson
S. G. Karshenboim et al., PRL 104, 220406 (2010), PRD82, 113013(2010).
PRA 84, 064502(2011) , PRD90, 073004(2014).
Exotic particle search

## Slide 9: Test of CPT and Lorentz Invariance
O.W. Greenberg, PRL 89 (2002) 231602
R. Blihm, V.A. Kosteleky, C.D. Lane, PRL 84 (2000) 1098
V.W. Hughs et al., PRL 87(2002) 111804
CPT broken Theory ⇒ Lorentz symmetry is broken
CPT violation search
Ex: Muon difference gµ+/ gµ– 10-8
gm-2/MuHFS precise measurement
Lorentz symmetry violating term in STE Lagrangian b
Corresponding MuHFS Dn12/34
These value might change in sidereal time (23h56m)
b3m/p=-dDn12=dDn34
~
LAMPF Exp. Figure of Merit
mm/MP～10-20
Plank scale sensitivity
V.A. Kostelecky, A.J. Vargas, PRD 92 (2015) 056002
Notes: MuHFS can contribute to a possible test of CPT and Lorentz violation incorporated in extensions to the standard model,
leading to potentially observable perturbative shifts in the ground state energy levels of muonium
[Old Ref. (top): O.W. Greenberg, Phys. Rev. Lett. 89 (2002) 231602]

## Slide 10: MuSEUM Experimental Layout

## Slide 11: J-PARC Muon Science Facility (MUSE)
H1 Area
Phase 2 (g-2/EDM, TmS)
DeeMe
MuSEUM
H-Line: for particle and atomic physics large scale experiments, “precison frontier”.
Higher intensity tunable (4 – 50 MeV) µ+ & µ– beam.
(Exp.: MuSEUM, Deeme, g-2, …)
Under construction
H1 Area
MLF Experimental Hall No. 1 (2018)
D-Line: Decay and Surface muon (µ+ & µ–)
Slow (50 keV) – fast (50 MeV) beam, general purpose.
Beamline in Operation

## Slide 12: Zero field measurement at D Line Important milestone for HF measurement-
Two additional components are required.
・Permalloy magnetic shield
・RF cavity for ZF

## Slide 13: Resonance Measurement Setup
Kr Gas Chamber
(RF Cavity inside)
Three layers of magnetic shield
Positron Counter
w/Al Absorber
Fiber Beam Profile Monitor
Muon Beam
200 mm

## Slide 14: Magnetic Shield and Field Probe
Assembled magnetic shield
without top boards
Magnetic field probe holder
and its moving system
700 mm
Fluxgate magnetic probe
35 mm x 35 mm x 35 mm

## Slide 15: Inside of the Gas Chamber
Pickup antenna
Input antenna
Tuning bar
Piezo positioner
81 mm
Expected Q-value is 10000, microwave power is up to 3 W
TM110 mode at 4.463 GHz, +-1 MHz tuning by a piezo positioner

## Slide 17: 1st MuSEUM Zero Field Experiment
2016. June. 3(24h)
Beam profile measurement
2016. June. 12-14(60h)
Muonium Resonance Search
Results
Good zero field condition (~100nT) was obtained.
Beam profile was successfully measured.
Enough RF power and cavity Q value were obtained
All detectors were working properly.
After several trial, Muonium HFS resonances was obtained!

## Slide 18: Time Dependent Spin Flip Signal
Near at Resonance
4463.1 MHz
RF frequency
1.0 Kr atm
27.4 MeV/c muon
Off-Resonance
RF frequency was far detuned
1.0 Kr atm
27.4 MeV/c muon
time (ns)
time (ns)
Signal (a.u.)
Signal (a.u.)
Signal = ON/OFF-1
Kanda thesis

## Slide 19: Resonance Lineshape
Muonium HFS resonance was observed
Fitted by Lorenzian and freq. center was 4463.1+-0.02 MHz
Expectation from precursor experiments is 4463.1 MHz
Frequency detuning (kHz)
Spin flip signal (%)
Kanda thesis

## Slide 20: 2nd MuSEUM Zero Field Experiment(2017)
Experimental Procedure
  Muonium formation in a Kr gas chamber
  Microwave spin flip
  Positron asymmetry
Kr gas chamber
Silicon detector
Magnetic shield
Sci. positron counter
RF cavity
(TM220)
decay positron
Polarized muon beam

## Slide 21: Positron Counter (2):
Silicon strip detector
Readout chips (SliT128A, 128 ch/chip)
Developed for J-PARC g−2/EDM experiment
Highly-segmented
High-rate capability
S/N ~ 21
Nishimura
Item | Specification
Sensor type | single-sided, p+ on n
Size | 98.77 mm × 98.77 mm
Active Area | 97.28 mm × 97.28 mm
Strip pitch | 0.19 mm
Strip length | 48.575 mm
No. of strips | 512 x 2 blocks
Thickness | 0.32 mm
Silicon Strip Detector
98.77 mm
98.77 mm

## Slide 22: Zero Field Measurements at D-Line
Muon Beam
Online Beam
Profile Monitor
Kr Gas
Chamber
Readout
Electronics
Magnetic Shield
Positron
Counters
TM220 mode
Larger cavity
More muon stop
Q-Value: 20,000 (calc.)
Experimental Setup
Upstream
Window
Downstream
Window
Residual Magnetic Field
New RF Cavity for Zero Field
~ 80nT
180 mm
RF Intensity
Dn = 4.463 GHz

## Slide 23: Results (1): Time Integral Method
Off Resonance
On Resonance
Time (ns)
Spin-flip Signal (%)
Previous ZF Experiment at LAMPF:
DnHFS = 4 463 302.2 ± 1.4 kHz (0.3 ppm)
– Scintillation Position Detector Data –
Systematic uncertainty: Estimation in progress
Conventional
Method
Statistical uncertainty:
2016 Feb. ~ 20 kHz (5ppm)
2017 Feb. ~ 4 kHz (1ppm)
2017 June ~ 2 kHz (0.5ppm)
2018 March ~ 1kHz, measured at 0.4, 0.55, 0.7 atm.
2018 June ~ 1kHz, measured at 0.3 atm Kr gas pressure.
Resonance Line Shape (2018 March)
Very Preliminary
Detuning Frequency (kHz)
New world record at ZF ???
Data analysis on going

## Slide 24: Results (2): Time Differential Method
0 ｋHz
100 ｋHz
200 ｋHz
400 ｋHz
Time (μs)
Signal
Possible advantages of this method:
Each detuning frequency data fitted individually.
Can determine DnHFS with only one frequency data.
Most sensitive detuning frequency is ~60 kHz.
Can improve statistical uncertainty by 3.2 times compared to the conventional method.
Can reduce systematics of RF power variation (free fitting parameter).
Need high-statistics data.
– Silicon Strip Detector Data –
Nishimura thesis
Statistics:
less data (smaller detector area)
Systematics (main):
RF power drift (200 Hz)
gas pressure extrapolation (66 Hz) (only one pressure data !)
Experiment (2017 June):
Simulation:
Preliminary
DnHFS = 4 463 302.2 kHz
± 3.1 ± 0.2 kHz
Notes: Main systematics in these data: RF power drifft (200 Hz), gas pressure extrapolation (66 Hz) (only one pressure !)

## Slide 25: 3rd MuSEUM Zero Field Experiment(2018)
2018 Mar 9th - 16th @ J-PARC D2-Line
Purpose : Measure the HFS value in vacuum by extrapolation
Measured with 0.4, 0.55 and 0.7 atm Kr gas pressure
uncertainty by extrapolation
Kr Gas Pressure [atm]
HFS frequency
0.3
1.0
Pressure gauge precision

## Slide 26: 3rd MuSEUM Zero Field Experiment(2018)
Kr gas pressure shift
  Resonance frequency is shifted due to collision of muonium & the Kr atom
  Gas pressure in the experiment in 2018 0.3, 0.4, 1.0 atm
  Spin flip resonance signal was obtained for each gas pressure
0.3 atm
0.4 atm
Ueno thesis

## Slide 27: 3rd MuSEUM Zero Field Experiment(2018)
Kr gas pressure shift
  Resonance frequency is shifted due to collision of muonium & the Kr atom
  Gas pressure in the experiment in 2018 0.3, 0.4,1.0 atm
  Spin flip resonance signal was obtained for each gas pressure
Recent analysis achieved 0.9kHz !
Preliminary
Ueno thesis

## Slide 28: Systematic Uncertainty
  Systematic can be as small as the previous experiment
Item | June 2017 | Prospects
Gas pressure fluctuation | 7 Hz | 7 Hz
Gas pressure extrapolation | 66 Hz | 7 Hz
Gas impurity | 0 Hz | 0 Hz
Static magnetic field | 0 Hz | 0 Hz
Microwave power drift （including muon beam profile） | 200 Hz | 1 Hz
Pileup event loss | 1 Hz | 1 Hz
Time Calibration | 1 Hz | 1 Hz
Total | 200 Hz | 10 Hz
Nishimura

## Slide 29: High field measurement at H Line
Two additional components are required.
・Permalloy magnetic shield
・RF cavity for ZF

## Slide 30: Improvement of statistics
d(Dn)
10.9 ppb
Statistics
4.4 ppb
Kr Density/Pressure
1.0 ppb
RF power
0.96 ppb
Muon stopping
d(mm/mp)
107 ppb
Statistics
Magnetic field
56 ppb
Kr Density/Pressure
11 ppb
RF power
9.6 ppb
Muon stopping
13 ppb
LAMPF Experiment
LAMPF: DC 107/s
total 1013
J-PARC/MUSE: Pulsed 1x108/s
H-Line total 2x1015
x200
Systematics
magnetic field accuracy & uniformity
pressure dependence (longer cavity lower pressure)
muon stopping distribution measurement
RF power stability
MuSEUM Improvements:
Statistics:
Systematics:

## Slide 31: MRI Magnet for High-Field Experiment
1.4 ppm p-p→0.27 ppm p-p (2017→2018)
64 Hz / 9.7 days
0.003 ppm /h
18 ppb→5.9 ppb (2017→2018)
  Spheroid : r=100 mm, z=300 mm
Second-hand 2.9 T MRI magnet
CW-NMR Field Monitoring System
Long Term Stability
Field Homogeneity (after shimming)
Sasaki, Yamaguchi , T. Tanaka

## Slide 32: RF Cavity for High Field Experiment
Tuning
Tuning
MWS simulation
3D CAD
Test Cavity
Q Value
Modes | Q (measured) | Q (simulation)
TM110 | 11,300 | 29,700
TM210 | 8,050 | 28,900
K.S. Tanaka, Seo

## Slide 33: Preliminary Systematic Error (HF)
 | Accuracy | n12 and n34 | d(DnHFS) | d(mm/mp)
Magnetic Field* | 30 ppb |  | 0.0 ppb | 15 ppb
RF power* | 0.2 % | 4 Hz | 0.8 ppb | 8 ppb
Kr gas temperature | 0.2 deg. | < 2 Hz | 0.4 ppb | 4 ppb
Kr gas pressure | 1 Pa | 1 Hz | 0.2 ppb | 0 ppb
H impurity | <50 ppm | 1 Hz | 0.5 ppb | 0 ppb
Quadratic dependence |  | 5 Hz | 1.0 ppb | 5 ppb
Muonium position (x,y) | 1 mm | 3 Hz | 0.6 ppb | 6 ppb
Muonium position (z) | 1 mm | < 1 Hz | 0.2 ppb | 2 ppb
Beamline | 10(e-4) | < 1 Hz | 0.2 ppb | 2 ppb
Detector pile-up | w/ absorber | 0.3 Hz | < 0.1 ppb | < 1 ppb
*should be re-estimated by latest progress and further MC simulation.
*should be re-estimated by latest progress of Time differential method.
Total systematic error of DnHFS~2 ppb, and mm/mp ~ 20 ppb
Notes: Our GOAL !!!

## Slide 34: Plan for Next Five Years
FY2019 High Field Measurement at S line (1.7T)
50 days? More accuracy than LAMPF
FY2020 Zero Field Measurement H line
50 days？ Less than 12ppb uncertainty
FY2021 High Field Measurement at H line (1.7T)
50 days 50 times statics
FY2022 High Field Measurement at H line (1.13T)
50 days 50 times statics
（magic field, rectangular cavity）
FY2023 High Field Measurement at H line (3T)
50 days 50 times statics
（Better condition for mm determination, rectangular cavity）

## Slide 35
M. Abe, Y. Fukao, Y. Ikedo, R. Kadono, N. Kawamura, A. Koda, T. Mibe, Y. Miyake,
K. Nagamine, S. Nishimura, T. Ogitsu, N. Saito, K. Sasaki, Y. Sato, K. Shimomura,
P. Strasser, A. Toyoda, K. Ueno, H. Yamaguchi, T. Yamazaki, A. Yamamoto, M. Yoshida
KEK
Y. Higashi, T. Higuchi, Y. Matsuda, T. Mizutani,
S. Seo, T. Tanaka, H. A. Torii, Y. Ueno, H. Yasuda
University of Tokyo
K. Kubo
ICU
M. Aoki, D. Tomono
Osaka University
E. Torikai
Univ. of Yamanashi
D. Kawall
U. of Massachusetts
Amherst
H. Iinuma
Ibaraki University
K. Kawagoe, J. Tojo, T. Yoshioka, T. Suehara,
T. Yamanaka, M. Matama, T. Ito, Y. Tsutsumi
Kyushu University
K. S. Tanaka
Tohoku University
H. M. Shimizu,
M. Kitaguchi
S. Fukumura
Nagoya University
K. Ishida, M. Iwasaki,
O. Kamigaito, S. Kanda
RIKEN
T. U. Ito
JAEA
S. Choi
Seoul National Univ.
MuSEUM Collaborators
(Muonium Spectroscopy Experiment Using Microwave)
K. M. Kojima
TRIUMF

## Slide 36: Summary and Next Step
Zero-field measurements at existing beamline (D-Line) in progress for engineering run of the apparatus.
Muonium HFS resonance clearly observed !
Soon new world record at zero field ! (data analysis in progress)
Several Analysis Methods are in progress (Old Muonium, Time differential)
Time-Differential Method promising to improve statistics and reduce RF power fluctuation systematics.
Need improvement of the RF power stability (systematics) !!!
4 Doctor thesis 5 Master thesis
New Precise muonium HFS measurements at high magnetic field will be carried out in a few years (H-Line).
Present expected systematic error estimated as
HFS ~ 2 ppb (~8Hz)
Magnetic moment (mm/mp) ~ 20 ppb
preliminary
Stay tuned !

## Slide 37
Backup Slides

## Slide 38: History of Mu HFS measurement
Old Mu Method
High Field
World Record
Zero Field
World Record
Magic Field
Spin Echo
K.S.Tanaka thesis

## Slide 39: How to improve the accuracy of mµ/me?
Comparison between theoretical and experimental value of Dn
＋higher order
where recoil term 800kHz (120ppm) and so on are included.
R∞＝10973731.568639(91)m-1(0.09ppt)
（Ｃｓ atomic beam interferometory）
a-1=137.03599958(52) (3.8ppb)
（from electron g-2）
mm/me=206.7682826(46) (22ppb), mm/mp=3.183345396(94) (24ppb)
This value is used for the determination of g-2.

## Slide 40: Determination of the Muon Mass
Muon mass (CODATA2016) determined by MuHFS (LAMPF 1999)
Mu 1S-2S
mSR
in Br2
MuHFS
Breit-Rabi
MuHFS
Dn(theory)
206.768 282 6 (46)
[22 ppb]
mm/me
mm/mp, am, mp/mB

## Slide 41
From K. Jungmann

## Slide 42
Los Alamos Experiment

## Slide 43
W. Liu et al., Phys. Rev. Lett. 82, 711 (1999).
Los Alamos Experiment

## Slide 44: Old Muonium Method
Delay time gate shows
more sharp resonance !
Simulation
Measurement

## Slide 45
Hydrogen-like atom | Experiment | Theory | (Dntheo - Dnexp)/Dnexp
Hydrogen | 0.2 ppt | 1.2 ppm | (-0.45 ± 1.2) ppm
Positronium | 3.3 ppm | 2.0 ppm | (15 ± 4) ppm
Muonium (Zero-Field) | 310 ppb | 61 ppb | (150 ± 320) ppb
Muonium (High-Field) | 12 ppb | 61 ppb | (23 ± 62) ppb
Precision of the hyperfine structure (HFS, Dn):

## Slide 46: Breit Rabi Diagram
m
e

## Slide 47: Gas Chamber and Gas Handling
425 mm length, 280 mm diameter, 100 μm Al beam window
Gas pressure is monitored by a capacitance gauge
Gas purity is measured by Q-Mass spectrometer

## Slide 48: Muon Beam Profile Monitor
100 mm
100 μm
Two layers of 100-µm fiber hodoscope (2x16ch).
3 x 3mm2 active area MPPC with 15-µm pixel pitch.
EASIROC readout
σ=20.8±1.5 mm
Horizontal position (mm)
σ=26.5±2.8 mm
Vertical position (mm)
Kanda, Ueno, Toyoda
Notes: MPPC: multi pixel photon counter

## Slide 49: Offline 3D Beam Profile Monitor
Actuator
Screw
Kr Gas
Chamber
Scintillator
Stage
Linear
Actuator
CCD
Muon beam width
Muon beam center
± 2 mm
± 2 mm
Ueno, Kanda, Toyoda, Ito

## Slide 50: Positron Counter (1):
240 mm
10 mm
3 mm
Plastic scintillator + MPPC + Kaliope readout circuit
32ch MPPC input
FPGA
Ethernet
Trigger input
ASIC
PROM
+5V(A), +1.8V
MPPC (Multi-Pixel Photon Counter)
1.3 mm x 1.3 mm active area
(Hamamatsu)
Segmented scintillation detector
Scintillation counter with SiPM readout
Unit cell: 10 mm × 10 mm × 3 mmt
Area: 240 mm × 240 mm
24x24 segments x 2 layers = 1152 ch
High-rate capability required
Pileup loss at 3 MHz/ch ~ 2%
576 ch/layer x 2 layers
Scintillation Position
Detector
Kanda, Kojima

## Slide 51: 3rd MuSEUM Zero Field Experiment
Kr gas pressure shift
  Resonance frequency is shifted due to collision of muonium & the Kr atom
  Gas pressure in the experiment in 2018 | 0.3, 0.4, 0.7 atm
  Spin flip resonance signal was obtained for each gas pressure
Analysis is ongoing
Preliminary
Time (μs)
Δ=100 kHz
0.7 atm
Nishimura

## Slide 52: RF Cavity & Gas Chamber
Gas Handling System
Pressure: 0.5 – 1.5 atm
Readout precision: several ppm
  (crystal gauge: 0.008% of full range)
Contamination: below 1ppm.
gas sampling before, during and after the experiment (several weeks).
Notes: - pressure range 0.5 - 1.5 atm; measurement precision: several ppm (crystal pressure gauge: 0.008% of full range)
- contamination: under 1 ppm (oxygen depolarize muonium)
- gas sampling before, during and after the experiment (several weeks of experiment).

## Slide 53: Systematic Error
Tanaka, Kanda, Ishida
Notes: Scheme of simulation tool: Evaluation of uncertainty by resonance-line simulations

## Slide 54: Mu Fraction

## Slide 55: Old Muonium in ZF field

## Slide 56: Time Integral Method
Resonance spectrum
Signal of all positrons
Resonance spectrum｜Lorentzian function
  Peak of Lorentzian is equal to Mu HFS frequency
  Mu HFS is determined by multiple frequency data
  Width and height of spectrum is changed by microwave power
  Δω / Detuning angular frequency
  |b| / Microwave magnetic field intensity
  λ / Spin relaxation rate
  γ / Muon decay rate
  P / Muon spin polarization

## Slide 57: Time Differential Method
Time dependence of signal
Detuning frequency dependence
Microwave power dependence
Time spectrum｜ Summation of cos
  contains more information
    Mu HFS frequency
    Microwave power
    Spin relaxation time
  can determine Mu HFS by only one detuning frequency data
Notes: 変動に強いことを言う

## Slide 58: Time Integral Signal (Simulation)
Simulation setup
  Measurement point | 10 points
  7.8×1010 muon/point
Fitting function for Time integral method
  Summation of Lorentzian function considering microwave power distribution felt by muonium
Simulation
Fitting

## Slide 59: Time Differential Signal （Simulation）
  Time differential signal | Same statistics as time integral method
  Time spectrum are changed by the detuning frequency
Fitting function
  Summation of cosine considering microwave power distribution felt by muonium
0 ｋHz
100 ｋHz
200 ｋHz
400 ｋHz
Time (μs)
Signal
Notes: HFS transition frequency can be determined by only one microwave frequency

## Slide 60: Time Differential Signal (Simulation)
時間微分信号
  積分信号の各周波数点に相当する統計量
  測定周波数による 時間スペクトルの 変化を確認
Fitting関数
  マイクロ波強度分布を 考慮したcos関数の 重ね合わせ
Simulation
0 ｋHz
100 ｋHz
200 ｋHz
400 ｋHz
Time (μs)
Signal
Mu HFS is obtained by only one
detuning frequency data
Notes: 変動に強い

## Slide 61: Multiple Time Differential Data
Mu HFS is determined by multiple results of time differential method
Simulation
Time Integral Method ｜0.41 kHz
Time Differential Method ｜0.34 kHz
15% improvement

## Slide 62: More Efficient Measurement
The most sensitive
detuning frequency
χ2 | 88.0/95
Δ | 59.9±0.13 kHz
Concentrating one frequency is the most efficient method
Time Integral Method ｜0.41 kHz
Time Differential Method ｜0.34 kHz
Time differential Method (Concentrate on Δ=60 kHz) ｜0.13 kHz
3.2 times improvement compared to the time integral method
Time (μs)

## Slide 63: Analysis by the Time Differential Method (2017)
Time differential muon spin resonance signal was observed
  Detuning frequency dependence is similar to the simulation results
  Same fitting function as the simulation
  Mu HFS was obtained from each detuning frequency data

## Slide 64: Mu HFS Measurement (2017)
Mu HFS was obtained from multiple data
  Obtained ΔνMu
  It is consistent to the previous experiments
  4 463 302.2 ± 3.1 kHz
Previous experiment
ZF | 4 463 302.2(14) kHz
HF| 4 463 302.765(50)(17) kHz
Phys. Lett. B59 (1975) 397-400 ， Phys. Rev. Lett. 82 (1999) 711-714