## Slide 1: BINP electron-positron facilities
Dmitry Shwartz
on behalf of
IC, VEPP-4M, VEPP-2000 teams
Feb 25, 2019
PhiPsi’19

## Slide 2: BINP accelerator complex layout
Injection Complex and beam transfer lines
VEPP-3
VEPP-4M
VEPP-2000
BEP
Damping
Ring
Linacs
Beamline to VEPP-2000
250 m
Beamline to VEPP-4M
130 m
IC Parameters (2016)
Beam Energy: 395 MeV
Storage rate e @ 12.5 Hz: 4.0·1010/s (70 mA/s)
Storage rate e+ @ 12.5 Hz: 4.0·109/s (7 mA/s)
Conversion System
Beam @ VEPP-3
Tour over BINP facilities today @ 18:00

## Slide 3: VEPP-4M complex
Energy | 0.925 ÷ 4.75 (5.3) |  |  |  | 
Circumference | 366 |  |  |  | m
N of bunches | 2e+ × 2e– (16e–) |  |  |  | 
Harmonic number | 222 |  |  |  | 
Betatron tunes, h/v | 8.54/7.57 |  |  |  | 
Coupling | 0.05% |  |  |  | 
Bunch length | 5 |  |  |  | cm
Beam Energy | 1.5 | 1.9 | 4.7 | 5.2 | GeV
Emittance | 16 | 25 | 167 | 200 | nm·rad
Energy Spread | 2.5 | 3.0 | 7.8 | 8.5 | ·10-4
Bunch Current | 1.6 | 3.5 | 25 | 25 | mA
Luminosity | 0.9 | 3.3 | 44 | 25 | 1030 cm-2·s-1
e+e– HEP at VEPP-4M with KEDR detector
SR at VEPP-3 (2 GeV)
SR at VEPP-4M (2÷4 GeV)
Nuclear physics at VEPP-3 with Deuteron facility
Test Beam Facility at VEPP-4M
Accelerator physics activity

## Slide 4: HEP @ VEPP-4M with KEDR
Universal magnetic detector KEDR
Electron-positron tagging system
Wide energy range 0.9÷6 GeV
Energy spread control
Precision beam energy calibration by resonance depolarization
First collider with beam energy monitoring by Compton backscattering
High energy luminosity run 2x(1.9÷Max energy) GeV
R scan 2x(2.3÷3.5) GeV (~ 10 bp-1)
ϒ-mesons study (~ 50 pb-1)
gamma-gamma physics (~ 200 pb-1)
2001-2017 low energy luminosity run 2x(0.9÷1.9) GeV
  J/, ’ , ”, (3770) meson masses
   lepton mass
  D0 mesons masses
  D± mesons masses
  Search for narrow resonances 1.85÷3.1 GeV
  R-scan 1.85÷3.1 GeV
  Ruds- and R- scan 3.12÷3.72 GeV
  J/  c
  -mesons, c, … parameters
RF system Upgrade
Power Supplies upgrade
Dedicated talks by T.Kharlamova, K.Todyshev
4 x GU-101A tetrode
2 MV → 4 MV
200 kW → 400 kW
100 mA @ 4.75 GeV
VEPP-3: ±15 kA ±40 V 600 kW
VEPP-4M: +7.5 kA +70 V 525 kW 4.75 → 5.2 (6.0) GeV

## Slide 5: Run 2017/18 highlights
In 2017 hadron cross section measurement from 2.3 to 3.5 GeV in two runs was started
At present first run has been finished ~ 6 pb–1
VEPP4-4M
KEDR runs
KEDR data
SR runs
shutdown
First luminosity @ ϒ(1S)
Luminosity
Bunches currents

## Slide 6: Deuteron @ VEPP-3
Tensor-polarized deuteron photodisintegration at the VEPP-3 storage ring
The two-body deuteron photodisintegration is one of the most studied process in nuclear physics. Tensor analyzing power T20 reaction will be measured in an unexplored region of the photon energy up to 1.5 GeV.
SR @ VEPP-3 – 1.2 or 2.0 GeV with 2 T shifter
SR @ VEPP-4M – 1.9 or 4.5 GeV with new 9-poles hybrid 2 T wiggler
VEPP-3
LIGA-technology and X-ray lithography.
Fast dynamic process.
Precise diffraction and anomalous scattering.
X-ray fluorescence analysis.
High pressure diffraction.
X-ray microscopy and micro-tomography.
Time resolved diffraction.
Time resolved luminescence.
Precise diffraction.
VEPP-4M
Metrology experiments.
Phase contrast microscopy, micro-tomography and hard X ray fluorescence.
Nanosecond spectroscopy of fast processes.
Material study under extremal conditions
Material study for thermonuclear applications
old
new (since 2017)
and SR program

## Slide 7: VEPP-2000 overview
Design parameters @ 1 GeV | 
Circumference | 24.388 m
Beam energy | 150  1000 MeV
N of bunches | 11
N of particles | 11011
Betatron tunes | 4.14 / 2.14
Beta* | 8.5 cm
BB parameter | 0.1
Luminosity | 11032 cm-2s-1
SND
CMD-3
Operating with IC#VEPP-5 since 2016
Round beams concept
Single-ring head-on collisions
13 T solenoids for FF
2.4 NC dipoles @ 1 GeV
CBS for energy control

## Slide 8: Experimental program
Precision measurement of
    exclusive approach, up to <1% for major modes
Study of hadronic final states:
Study of vector mesons and theirs excitations:
Comparison of cross-sections with spectral functions of -decays
Study of nucleon electromagnetic formfactor at threshold
Measurement of the cross-sections using ISR
Study of higher order QED processes
Target luminosity integral is 1 fb-1 per detecor
Dedicated talks by M.Achasov, F.Ignatov, E.Solodov

## Slide 9: Beam-beam limit @ lepton colliders
J.Seeman (1983)
Beam-beam parameter saturation, emittance (and beam size) growth
Final limit:
emittance blowup,
lifetime reduction,
flip-flop effect

## Slide 10: The concept of Round Colliding Beams
Head-on collisions!
Small and equal β-functions at IP:
Equal beam emittances:
Equal fractional parts of betatron tunes:
Axial symmetry of counter beam force + X-Y symmetry of transfer matrix IP2IP
Round beam
Mx = My
Lattice requirements:
F.M. Izrailev, G.M. Tumaikin, I.B. Vasserman. Preprint INP 79-74, Novosibirsk,(1979).
L.M. Barkov, et. al, Proc. HEACC’89, Tsukuba, Japan, p.1385.
S. Krishnagopal, R. Siemann, Proc. PAC’89, Chicago, p.836.
V.V. Danilov et al., EPAC’96, Barcelona, p.1149.
S. Henderson, et al., Proc. PAC’99, New York, p.410.
Additional integral of motion (angular momentum Mz = xy - xy)
Particle dynamics remains nonlinear, but becomes 1D

## Slide 11: Round Beams Options @ VEPP-2000
Flat to Round/Mobius or Long to Short change needs polarity switch in solenoids, realignment and new orbit correction.
Round beam due to coupling resonance?
The simplest practical solution!
Both simulations and experimental tests showed insufficient dynamic aperture for regular work in circular modes options.
Below 600 MeV “short” FF solenoids are available.
Solenoid main coils

## Slide 12: Beam size measurement via SR @ CCDs

## Slide 13: Machine tuning
Orbit correction & minimization of steerers currents using ORM techniques
Lattice correction via ORM SVD analysis ( < 5%)
Betatron coupling correction in arcs (min ~ 0.001)
Working point fine tuning & small shift below coupling diagonal
Sextupoles fine tuning (chromaticity slightly undercompensated)
Lifetrac by D.Shatilov, 2008
After correction
Before correction
Specific luminosity & linear lattice correction

## Slide 14: “Flip-flop” effect
E = 240 MeV,
Ibeam ~ 55 mA
0.17
0.2
0.25
0.17
0.2
0.17
0.2
Pickup spectrum of the coherent oscillations
Coherent beam-beam -mode interaction with machine nonlinear resonances?
TV
e+
e


regular
blown-up e
blown-up e+

## Slide 15: Flip-flop suppression with long bunch
URF= 35 kV
URF= 17 kV
Bunch lengthening & mw instability
Е= 392.5 МэВ
Single bunch length measurement with phi-dissector as a function of single beam current for different RF voltage @ 478 MeV.
Energy spread dependence, restored from beam transverse profile measurements.

## Slide 16: BeamShaker (Run 2017/18)
Typical values:
50-100 V, 300 ns, 50 s
(Trev = 81.4 ns)
Experimentally: permanent excitation of “strong” beam size prevent it from shrinkage to natural value during injection cycle of “weak” beam, or whatsoever. Very effective suppression of flip-flop meta-stable states.
In addition large emittance results in a lifetime enhancement.
Idea (I.Koop): kicked bunch oscillations decoheres very fast in the presence of counter beam’s strongly nonlinear field. Weak and frequent kicks should effectively increase the emittance, similarly to quantum excitation by wiggler.
At low energies emittance growth is available up to aperture restriction. That allow with the same beam-beam parameter (particles density) increase the beam current and luminosity.

## Slide 17: Shaking @ pickup
Pickup signal, without counter beam, 360 MeV
Pickup signal, with strong counter beam, 274 MeV
70 m
@ 274 MeV:
x = 250 m @ pickup
damp = 130 ms = 1.6×106 turns
100 turns
Periodically excited oscillations gives the line spectrum

## Slide 18: Luminosity and beam-beam parameter
392 MeV
2018
2013
- normalized beam current
- “beam-beam parameter”

## Slide 19: Data collection
CMD-3 luminosity, averaged over 10% of best runs
2017-2018 data
Below 500 MeV
Above 500 MeV
Highest luminosity achieved
Lpeak = 5×1031 cm2s1
@ 550 MeV
Variable * scaling law
With new IC
ongoing run

## Slide 20: Total luminosity integral
,

̍
NN
D*0
Lowest energy ever obtained in e+e− colliders


## Slide 21: Beam energy measurements: CBS system
E.V. Abakumova et al., PRL 110 2013 140402
Backscattered photons spectrum edge:

## Slide 22: Summary
New BINP injection complex routinely serves both colliders.
VEPP-4M has started the program at it’s high energy range with resonance depolarization system for precise energy control.
VEPP-2000 with new BINP injector and upgraded booster started data taking in all energy range of 200–1000 MeV with a luminosity increased in a factor of 2-5.
Round beams concept gives the luminosity enhancement @ VEPP‑2000.
Novel technique (“beamshaking”) for effective emittance control allow to suppress flip-flop effect and increase beams intensity at middle energies.
Ongoing run is devoted to energy range above 500 MeV with intent to achieve the target luminosity at 1 GeV.
Thank you for your attention

## Slide 23: backup

## Slide 24: Super-CT Project
Thermionic
Gun
Polarized e- Gun
e- Photogun
1 nC, 3 ps
ΔE/E ~ 0.5 %
(total charge)
e- 1 GeV + 1.5 Gev Linacs
AS – 16 + 24
Klystron – 8 + 12
Length – 72 m + 96 m
e- 1.5 GeV Linac
AS – 24
Klystrons – 12
Length – 96 m
e+ 1.5 GeV Linac
AS – 24
Klystrons – 12
Length – 96 m
Damping Ring
e+ 1 – 1.5 GeV
1 GeV Linac
AS – 16
Klystrons – 8
Length – 72 m
Debuncher
Compressor
Damping
Wiggler
IP
RF System
Damping
Wiggler
Damping
Wiggler
Damping
Wiggler
Siberian
Snake
Crab
Sext
Crab
Sext
RF photogun: beam charge is 1 nC, laser length is 266 nm, laser energy is up to 3 mJ, laser pulse length is not more 10 ps, metallic cathode, beam energy is at least 5 MeV, beam energy spread for
total charge is not more 0.5%, rms beam length is about 1 mm (3 ps)
Accelerating structure: TW, constant impedance (geometry), length is 3 m, quasi-constant electric field distribution, energy gain is 22 MeV/m, beam energy per structure is 66 MeV
Klystron: peak power is 50 MW, repetition rate is 50 Hz, pulse length is up to 5 μs
RF module: 1 klystron, 2 accelerating strictures, electric field amplitude is 27 MV/m, gap between structures is 1 m
Thermionic gun: pulse length is up to 10 ns, peak current is about 8 A
Total number of accelerating structures: 104
Klystron number: 52
Total length of the linacs: ~440 m
Drift channel for 1.5 GeV mode

## Slide 25: Coherent beam-beam spectrum
 = 0.21   = 0.17/IP
Here the Yokoya factor Y = 1, due to fast kick method of eigen modes excitation and due to short period analysis (studied @ VEPP-2M; simulated for VEPP-2000 by D.Shatilov)


 = 0.135,  = 0.345