## Slide 1: Status of the Forward RICH for PANDA
Sergey Kononov
Budker Institute of Nuclear Physics SB RAS
Novosibirsk State University
FRRC - SSC RF ITEP of NRC “Kurchatov Institute”
November 18, 2015
Work is funded by
MINISTRY OF EDUCATION AND SCIENCE OF THE RUSSIAN FEDERATION

## Slide 2: PANDA detector
Forward RICH
Disc DIRC
Barrel DIRC
PID

## Slide 3: Requirements to Forward RICH
PID in the Forward Spectrometer
|θx| < 10°, |θy| < 5°
1 m space along the beam
approximately 3 x 1 m transverse active size
Working momentum range for 3σ separation
  π /K: 3÷10 GeV/c
  μ/π: 0.5÷2 GeV/c possible
Physics cases application: processes with high charged hadrons multiplicity in the final states for high beam momenta

## Slide 4: Conceptual design
Baseline PD option
Hamamatsu H12700 MaPMT
flat panel,
8x8 anode pixels of 6mm size
87% active area ratio
Bialkali photocathode
Gain: 1.5∙106
Good single p.e. amp. resolution
Relatively cheap (≈€1700 / unit)
Robust
Long lifetime
Focusing aerogel radiator (non-homegenious)
No gaseous radiator
Flat mirrors
MaPMT readout (other options possible)

## Slide 5: Readout options
DPC
Tile FPGA
Module
FPGA
Data concentrator FPGA
MaPMT
H12700
FEE
PADIWA
TDC
TRB
Baseline option
H12700B price: 1700 € per tube (~1400 tubes in total)
option
DPC price: 3500 € per module (~800 modules in total)
Needs liquid cooling.

## Slide 6: Production of aerogel in Novosibirsk
Started in 1986 by the Boreskov Institute of Catalysis SB RAS in cooperation with the Budker Institute of Nuclear Physics SB RAS
Hydrophilic (absorbs moisture)
Refraction indices 1.006 – 1.08 (1.08-1.13 produced by sintering)
Block dimensions up to 200x200x50 mm3 (for n=1.03)
Remarkable optical quality has been achieved: Labs (400nm) = 5 – 7 m Lsc (400nm) = 4 – 6 cm (Clarity = 0.0043 – 0.0064 μm4/cm)
Used in the experiments:
  KEDR/VEPP-4M: n=1.05 (1000 l)
  SND/VEPP-2000: n=1.13 (5 l) + n=1.05 (5 l)
  LHCb RICH: n=1.03 (20 l)
  AMS-02/ISS RICH: n=1.05 (60 l)
  DIRAC-II/CERN PS: n=1.015 (26 l) + n=1.008 (13 l)
Absorption length

## Slide 7: KEDR ASHIPH counters: 1000 liters of aerogel
SND ASHIPH counters: n=1.13 (n=1.05)

## Slide 8: FARICH – Focusing Aerogel RICH
T.Iijima et al., NIM A548 (2005) 383 A.Yu.Barnyakov et al., NIM A553 (2005) 70
n=1.030 6.0mm
n=1.027 6.3mm
n=1.024 6.7mm
n=1.022 7.0mm
First sample of 4-layer aerogel by BIC
3-layer aerogel 115x115x41 mm3
Focusing aerogel improves proximity focusing design by reducing the contribution of radiator thickness into the Cherenkov angle resolution
Single ring option
Multi-ring option
Multi-layer monolith aerogels are produced by the Boreskov Institute of Catalysis in coop. with BINP since 2004. In 2012 we succeeded in production of continuous density gradient aerogels.
Notes: Идея ФАРИЧ появилась в 2004 г.
Точность измерения черенковского угла связана с точностью измерения скорости, а значит с качеством разделения частиц.

## Slide 9: FARICH projects and proposals
FARICH PID system for Super c-τ factory (BINP&BIC)
Particle ID : μ/π up to 1.7 GeV/с
~21m2 detector area (SiPM) ~106 pixels with 4 mm pitch
Belle II ARICH (Belle coll.)
Particle ID: π/K up to 4 GeV/c
Forward end-cap: ~3m2
Two (separate) layers of aerogel: n1= 1.045, n2= 1.055
Photon detector: HAPD (Hamamatsu)
PANDA Forward RICH (BINP&BIC)
Particle ID: π/K/p up to 10 GeV/с
3m2 detector area (MaPMTs or SiPMs)

## Slide 10: Electron and gamma beam test facility at BINP
Parameters of the e− beam | 
E [MeV] | 100÷3000
σE/E [%] | 1.8%@1GeV
Rate [s−1] | 50

## Slide 11: DPC is an Integrated “Intelligent” Sensor by Philips Digital Photon Counting
FPGA
Clock distribution
Data collection/concentration
TDC linearization
Saturation correction
Skew correction
Flash
FPGA firmware
Configuration
Inhibit memory maps
32.6 mm
DPC3200-22-44 – 3200 cells/pixel
DPC6400-22-44 – 6396 cells/pixel

## Slide 12: First test of DPC in RICH: PDPC-FARICH prototype @ CERN PS T10, June 2012
Main objective:
  Proof of concept: full Cherenkov ring detection with a DPC array
Details:
Operation temperature is −40°C to suppress dark count rate
  Dead time is 720 ns.
  DCR(+25°C) ≈ 10 Mcps/sensor single photon detection is not feasible!
  DCR(-40°C) ≈ 100 kcps/sensor inefficiency is 7% .
2 stage cooling: LAUDA process thermostat + Peltiers.
Dry N2 constant flow to avoid condensation.

## Slide 13: PDPC-FARICH: Particle ID evaluation
π /K: 7.6σ @ 4 GeV/c
μ/π: 5.3σ @ 1 GeV/c
2.3 times higher than SuperB FDIRC
1.4 times higher than Belle II ARICH
2.6 times less than in initial MC simulation
A.Yu. Barnyakov, et al., NIM A 732 (2013) 352
Ring distribution on radius
Aerogel to be optimized
DPC PDE lower than expected

## Slide 14: Upgrade of PDPC-FARICH prototype
Cold box for DPC photon detector. Aerogel is placed outside at room temperature and can be easily exchanged
Extend aerogel-PD distance to ~500 mm
Dark envelop box with moving stage for aerogel and mirror (under construction)
PMMA window
Test of upgraded DPC detector with e- beam in March 2015

## Slide 15: Proton irradiation of DPC at COSY August 1-4, 2014
Cold box with 2 DPC-3200-22-44 tiles
p beam
Protons with P=800 MeV/c (T=295 MeV)
Maximum fluence ~4·1011 p/cm2 accumulated in 9 steps
Tiles irradiated at −18°C
DCR scan of cells was done in beam stops
Total dose is measured by ionization chamber provided by COSY team
Beam profile was determined by data
M.Yu. Barnyakov et al., http://dx.doi.org/10.1016/j.nima.2015.10.098

## Slide 16: Dark count rate vs fluence
Single cell DCR averaged over one subpixel (32x25 cells). Different colors for different dies.
Proton fluence
4x1011 p/cm-2
NIEL-equivalent neutron fluence 3x1011 n1MeV/cm-2

## Slide 17: Leveraging DPC cell inhibit function to keep up efficiency
DCR of a die as a function of active cells
fraction for different proton fluences.
Relative photon detection efficiency as a function of active cell fraction taking into account dead time.
Optimal efficiency is a tradeoff between the fraction of active cells and DCR-induced dead time. The dead time for the current chip design is 720 ns.

## Slide 18: DPC PDE vs proton fluence
4∙109 n1MeV/cm2
2 times drop

## Slide 19: Expected rad. backgr. @ PANDA
FRICH location |  | [n1MeV/cm2/s] HR mode (2 ∙ 106 s-1 ) | DPC Lifetime[years]
 | Next to FT5,6 | 83 | 2.4
 | Next to FTOF | 73 | 2.7
 | Close to FT5,6. PD shifted by 10 cm up and down | 71 | 2.8
 | Close to FT5,6 PD shifted by 20 cm up and down. | 53 | 3.8
FRICH location |  |  | DPC Lifetime[years]
 | Next to FT5,6 | 83 | 2.4
 | Next to FTOF | 73 | 2.7
 | Close to FT5,6. PD shifted by 10 cm up and down | 71 | 2.8
 | Close to FT5,6 PD shifted by 20 cm up and down. | 53 | 3.8
Radiation background simulation in PandaRoot:
DPM generator
10 GeV/c beam momentum
Geant4 for secondary sim.
4 geometry options considered
Almost all particles considered and scaled by NIEL to 1MeV neutron fluence
Simplified detector description w/o frames, support, etc.
Neutron shielding may be considered
Highest flux comes from neutrons

## Slide 20: Forward RICH in PANDAroot
π/K-separation | up to ~10 GeV/c
Radiator | Focusing layered aerogel
Refractive indices | ~1.05
Radiator thickness | 4 cm
Placement | after FT5&6
Vertical angle | ±5°
Horizontal angle | ±10°
FT5
FT6
FRICH
TOF
ECAL
HCAL
Dipole magnet

## Slide 21: Simulated effects
Simulation
  Geometry description
    RICH position
    Aerogel (size, number of layers, refraction index)
    Mirror geometry (round, flat)
  Materials properties for Cherenkov photons
Digitization
  Pixelization
  Quantum efficiency of photodetector
  Photon detector noise
  Dead time of photodetector
  Photodetector time resolution
  Crosstalks (TO DO)
Reconstruction (simple mode)
  Hit preselection
  Fit θ(φ) dependence
PID (TO DO)
  Probability calculation
  PID selector implementation

## Slide 22: Optimizing mirror configuration
1 segment
2 segments
3 segments
4 segments
6 segments
10 segments
Round
Acceptance for Cherenkov photons is maximized, photon detector area is minimized. Mirror is curved in 1D.
PD width

## Slide 23: Optimal photon detector width
Cylindrical mirror
Parameter | 3 segments | Round
PD width, cm | 67.5 | 58.5
Mirror focusing | no | yes
Aerogel focusing | yes | no
Combinatorial background | yes | no
Cherenkov image shape on PD surface | broken elliptical | complicated
Number of parts | 3 | 1

## Slide 24: Multi-layer aerogel optimization
1.05 − δn
1.05 + δn
1.05 − δn
1.05
1.05 + δn
Two layers
Three layers

## Slide 25: Multi-layer aerogel: optimal refractive index spread
Two layers
Three layers
n = 1.05
δnopt = 1.03·10-3
δnmin = 0.76·10-3
δnmax = 1.36·10-3
n = 1.05
δnopt = 1.23 ·10-3
δnmin = 0.96 ·10-3
δnmax = 1.47·10-3
Configuration with three segments mirror and three layer aerogel is used further on

## Slide 26: Events simulation and reconstruction
X, cm
X, cm
X, cm
Y, cm
Y, cm
Y, cm
φC, rad
θC, rad
Possible reconstruction methods:
2D pattern recognition on photon detector surface
track hits to the origin and reconstruct Cherenkov angles (θc, φc)
θC = acos(1/n)

## Slide 27: Reconstructing Cherenkov photon direction angles
θc, rad
φc, rad
θc = f( φc; β, n, α )
φc − azimuthal angle
β − velocity of the charge particle
n − refraction index of the aerogel
α − polar angle of the charge particle
Event data fit
μ
p = 10 GeV/c
β = 0.99994
βFIT = 0.99912

## Slide 28: π/K-separation: first result
2 GeV/c
4 GeV/c
6 GeV/c
8 GeV/c
10 GeV/c
K
K
K
K
K
π
π
π
π
π

## Slide 29: Conclusion
Forward RICH R&D is in a good shape
Two readout options (MaPMT, DPC) are considered
DPC radiation hardness study has been carried out
Full PandaRoot simulation of FRICH is under development. First results on PID performance of FRICH are obtained.
Plans for 2015-2016
DPC characterization
MaPMT H12700 characterization with PADIWA&TRB3 FEE
Mirror optical measurements
Submit FRICH full sim. to PandaRoot
Mechanical design
Prototype beam tests

## Slide 30: Backup slides

## Slide 31: Use cases of PANDA Forward RICH 2010
Covered solid angle: |θx| < 10°, |θy| < 5°
Identification of high momentum (>3GeV/c) kaons in presence of a large pionic background
Separation of other charged particles: μ/π, e/π, K/p
In spite of the small covered solid angle production processes at high beam momentum with a large multiplicity are likely to give particles in the Forward RICH.
Example: hybrid () search at 15 GeV/c
Fast MC simulation shows:
46% of events are reconstructed only due to the RICH. That means 86% statistics gain due to the RICH.
Distribution of pions and kaons

## Slide 32: SiPM detectors and electronics
32 CPTA MRS APDs pixel size 2.1x2.1mm2
60 CPTA MRS APDs
pixel diam. 1.28 mm
CAEN V1190B multihit TDC board
Custom 16ch amplifier-disc. boards
ALICE TOF NINO-based board
+
+

## Slide 33: Single pixel approach for aerogel characterization
Given a tracking system and enough particle statistics, a single PD pixel is enough to build the distribution of Cherenkov photons on Rch (θch).
Many pixels can be combined to improve accuracy and align the tracking system with the PD pixels
Sum of all pixels w.r.t. track position

## Slide 34: Beam test 2011 results
σr=1.1 mm – in rough agreement with MC simulation ‹Np.e. › = 13 – 2 times less than expected
4-layer aerogel (t=3cm) vs single layer aerogel (t=2cm)
Focusing effect has been observed.
σr vs channel
Np.e. vs channel
σr =1.1 mm
σr =2.1 mm

## Slide 35: PDPC-FARICH setup
Square DPC array 20x20 cm2
DPC3200-22 sensors
3200 cells per pixel of 3.2x3.9 mm2
3x3 modules = 6x6 tiles = 24x24 sensors = 48x48 pixels
576 timing channels
2304 amplitude channels (pixels)
3 levels of FPGA readout: tiles, modules, data collection board.
4-layer aerogel
nmax = 1.046
Thickness 37.5 mm
Focal distance 200 mm
Test conditions
Beam content: e+, μ+, π+, K+, p
Momentum: 1–6 GeV/c
Trigger: 2 sc counters 1.5x1.5 cm2 in coincidence separated by 3 m
No external tracking, particle ID, precise timing of trigger

## Slide 36: PDPC-FARICH: timing resolution and number of photoelectrons
σnarrow = 48ps
for single photons
Hit time w.r.t. fitted event time, ns
‹Np.e. › = 12 (accounted for optical crosstalks)
1.7 times lower than expected
Number of hits