## Slide 1
Simulations of physics background in Super c-tau factory detector
L.Shekhtman
Budker INP, Novosibirsk State University

## Slide 2
Main specifications:
2E = 3 ÷ 6 GeV
Crab waist collision
Peak luminosity 1035 cm-2s-1
Longitudinal polarization of electron beam
Novosibirsk Super Charm-Tau Factory

## Slide 3
Main luminosity background sources:
Two-photon processes e+e-  g*g*e+e-e+e- (Ee+e->2MeV) - 2.9mb (at 3 GeV per beam), DIAG36
Radiative Bha-Bha e+e- e+e-g(ng) (q>5mrad), Eg>1MeV) - 1.2mb (at 3 GeV per beam), BHWIDE
Average number of particles with q>5mrad – ~1.9 per event (primary electrons and positrons in two-photon processes were removed from the source)
With 1035 cm-2s-1 - ~4x108 background events per second
If frequency of bunch crossings is 2x108 - ~2 events per crossing, ~4 background particles with q>5mrad

## Slide 4
General conditions of the simulation:
Magnetic field was calculated by A.Bragin for “standard” coil, 1.5T in central part (as in old simulation)
In order to turn the source particles in accordance with the crossed VP, they were transferred to the system with βx≈-0.03.
Simulation of background particles fluxes is performed with FLUKA package with FLAIR interface (http://www.fluka.org)
Particles transport threshold is set to 0.1 MeV for all particles except of electrons-positrons and photons: 10 MeV in concrete walls (electrons and photons), 1 MeV (0.1MeV for photons) in other regions, production threshold in the walls is 10 MeV (electrons and photons).

## Slide 5
Crossed vacuum pipe
Tilted view with cut
Z-X cross-section

## Slide 6
Expanded view of the interaction region of VP
Final focus
Crossed vacuum pipe

## Slide 7
General view of the model

## Slide 8
Comparison of “all particles” Z-X (-5cm <Y<5cm) and Z-R maps (2π>φ>0)
Maps of all particles fluence in units of track length per cubic cm per second
Statistics – 2x106 source particles (10 runs, 200000 source particles each)

## Slide 9
Comparison of Z-X map and Z-R map of e+e- fluence

## Slide 10
Electrons & positrons (TPC)
Z, cm
1/cm2s
R, cm
e+e- fluence (Z-R map), comparison of new and old simulations
2x106 source particles
2x105 source particles

## Slide 11
Spectra in Inner Tracker volume
Z-X map of photon fluence

## Slide 12
Electrons and positrons in the region of IT

## Slide 13
Comparison of new and old simulations
New simulation
Old simulation

## Slide 14
Absorbed dose in Gy/year

## Slide 15
1-MeV neutron equivalent fluence for Si in n/cm2year

## Slide 16
Conclusions
Crossed geometry of VP and final focus assembly according to the available
drawing are realized in FLUKA
Results of simulations with new geometry are very similar to old ones
Charge particles rate in the region of Inner Tracker 105 – 103 cm-2s-1. This result is used for further studies of the TPC option (ion space charge impact)
1 MeV n-equivalent fluence for Si is below 1011 n/cm2y
Absorbed dose is below 100 Gy/y (rad-tolerant electronics needed)

## Slide 17
Backup slides

## Slide 18
Z, mm
R, mm
Energy deposition in TPC after 2000 bunch crossings

## Slide 19
Cross sections dependances