## Slide 1: ECL DAQ status
Vladimir ZHULANOV, Budker INP
06.09.2016

## Slide 2: Outline
Electronics status
ECL data format
ShaperDSP access & initialization

## Slide 3: ECL electronics
ShaperDSP
ShaperDSP
ECLCollector
ShaperDSP
FTSW
COPPER
TTD
belle2link
HSLB
HSLB
TTRX
Electronics for all 52 crates has been installed and connected to DAQ
PreAmps only for barrel part are connected
Stable DAQ operation with random TR=30 kHz. And continuous stable work during >20 hours
12 ShaperDSPb
Modules
52 X

## Slide 5: ECL Data format – overall structure
EclCollector header
ShaperDSP#1 data
ShaperDSP#2 data
ShaperDSP#3 data
…
ShaperDSP#12 data
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
reserved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | SHAPER_DSP_DATA_MASK |  |  |  |  |  |  |  |  |  |  | 
ADC_DATA_ENCODED flag
b12=1: ADC data encoded
b12=0: ADC data in raw format
SHAPER_DSP_DATA_MASK
b11=1: ShaperDSP#12 data presented b11=0: ShaperDSP#12 data omitted
b10=1: ShaperDSP#11 data presented
b10=0: ShaperDSP#11 data omitted
…
b0=1: ShaperDSP#1 data presented
b0=0: ShaperDSP#1 data omitted
ShaperDSP data presented
only for those ShapersDSPs
marked in corresponding
position here
Overall packet structure
EclCollector header
ShaperDSP data format see in the next slide

## Slide 6: ECL Data format – ShaperDSP data
 | b31…b24 | b23…b16 | b15…b8 | b7…b0
0 | PCK_ID (debug reasons) | 0x10 (magic number) | b[15..0] – PCKT_LEN ShaperDSP packet length | 
1 | b[28…24] – ADC_NUM Channels # with raw ADC data presented = weight (number of ‘1’s) of the ADC_MASK | b[22…16] – SAMPLES_NUM | b[12…8] – DSP_NUM Channels # with DSP data presented = weight (number of ‘1’s) of the DSP_MASK | b[7…0] – TRG_PHASE Trigger phase within ADC conversion period. Δt = 4 ns
2 | b[31..16] – DSP_MASK Reconstructed (DSP) data present only for those channels marked in this mask |  | b[15..0] – TRG_TAG Trigger TAG | 
3 | reserved |  | b[31..16] – ADC_MASK ADC data present only for those channels marked in this mask | 
4 … | DSP data: DSP_NUM words |  |  | 
… | ADC data: ADC_NUM x SAMPLES_NUM if encoding not enabled, much less otherwise |  |  | 
DSP data for 1 channel:
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
b[31…30] |  | b[29..18] – reconstructed TIME, signed integer , LSB = 0.5 ns |  |  |  |  |  |  |  |  |  |  |  | b[17..0] – reconstructed AMPLITUDE, 1 LSB = ~50 keV unsigned integer with offset -128 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
b[31…30] |  |  |  |  |  |  |  |  |  |  |  |  |  | b[17..0] – reconstructed AMPLITUDE, 1 LSB = ~50 keV unsigned integer with offset -128 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ShaperDSP data
Quality flags: 0 – Calculation OK, good
1,2 – Calculation errors
3 – Calculation OK, bad

## Slide 7: ECL Data format – ShaperDSP data – raw format
b[31…18] | b[17…0]
reserved | Ch#1, Sample #0
reserved | Ch#1, Sample #1
reserved | …
reserved | Ch#1, Sample #N
reserved | Ch#2, Sample #0
reserved | Ch#2, Sample #1
reserved | …
Ch#1 SAMPLES_NUM
samples
ADC_NUM x SAMPLES_NUM
samples
Very ineffective way of encoding!
14 bits of 32 are not used
Usually ADC values are within narrow region around baseline
ADC data encoding see next slide

## Slide 8
min = 2245
max = 2750
diff = 505
9 bits enough to encode any offset
relative to the common base line.
Even less bits for smaller pulses!
word# | contents |  |  |  | 
0 | b[31…23] 7 | b[22…18] WIDTH 9 |  | b[17…0] BASELINE 2245 | 
1 | ... |  | b[17…9] 27 |  | b[8…0] 22
… | … |  |  |  | 
Sample #0 = 2252 = 2245 + 7
Sample #1 = 2267 = 2245 + 22
Sample #2 = 2272 = 2245 + 27
…
BASELIND, WIDTH and OFFSETS
are encoded in common bitstream

## Slide 9: Event data size estimations
Event data size = 1 (EclCollector header) +
= 4 (ShaperDSP header) + DSP_NUM + ADC_NUM * SAMPLES_NUM
1 word for every hit channel 16 words * occupancy (<30%)
496 words = 16 channels * 31 samples (no encoding)
For regular runs
appended only to
1/100 events or less
Thus, for occupancy 30% and 1/100 ratio of events with raw ADC data we have average event size:
S = 1 + 12 * (4 + 16*0.3 + 140 * 1/100) = 1 + 12 * (4+4.8+1.4) ~= 123 words. MIN/MAX = 49/3841 words
49 out of 123 words are headers!!!
We should think on how much of this we can strip and where (on EclCollector?/ on Copper?)
Looking at the headers I see that this number (49) can be reduced to 14,
so the average Event size can be reduced to 88 words.
140 words ~= 16 channels * 8.7 words (av. # of words with encoding)

## Slide 10: Access to ShaperDSPs
IN
BUF # 1
OUT
BUF # 1
ShaperDSP #1
IN
BUF # 2
OUT
BUF # 2
ShaperDSP #2
IN
BUF # 12
OUT
BUF # 12
ShaperDSP #12
…
Custom
ETH I/F
Ethernet
EclCollector FPGA
In the very first version (no belle2link) we
used Ethernet interface with low level access:
no packet decoding on Collector side
Original design

## Slide 11
IN
BUF # 1
OUT
BUF # 1
ShaperDSP #1
IN
BUF # 2
OUT
BUF # 2
ShaperDSP #2
IN
BUF # 12
OUT
BUF # 12
ShaperDSP #12
…
Embedded CPU
Ethernet
EclCollector FPGA
In the intermediate version
the data merger was implemented
decoding packets from Shapers moved from remote PC to embedded CPU
Drawback: No read from shapers while Event data merger is active  no Shapers monitoring during RUN
Intermediate design
Event data merger
Belle2link

## Slide 12
IN
BUF # 1
OUT
BUF # 1
ShaperDSP #1
IN
BUF # 2
OUT
BUF # 2
ShaperDSP #2
IN
BUF # 12
OUT
BUF # 12
ShaperDSP #12
…
Embedded CPU
Ethernet
EclCollector FPGA
In the current version
Packets for Read ShaperDSP registers/memories is implemented in Merger’s logic
Full access to ShaperDSP internals during RUNs
Advanced (current) design
Event data merger
+ all packets decoder
Belle2link
Decoded data

## Slide 13: ECL initialization using only b2link
reghs -a fee32 0x00B0 0xA7000000 # set Flash-memory address
reghs -a fee32 0x00B2 0xFFF # set active ShaperDSP mask
reghs -a fee32 0x00B8 1 # init downloading ShaperDSP firmware
set er_code = 1 # wait completion of operation
while( $er_code != 00000000 )
set er_code = `reghs -a fee32 0x00B8 | awk '{split($0,array," "); print array[3]}'`
end
set er_code = `reghs -a fee32 0x00B9 | awk '{split($0,array," "); print array[3]}'`
echo $er_code # print operation status: 00000000 - OK
Download ShaperDSP firmware
reghs -a fee32 0x00B0 0xAA000000 # set Flash-memory address
reghs -a fee32 0x00B2 0x002 # set active ShaperDSP mask
reghs -a fee32 0x00B8 2 # init downloading ShaperDSP coeficients
set er_code = 1 # wait completion of operation
while( $er_code != 00000000 )
set er_code = `reghs -$SLOT fee32 0x00B8 | awk '{split($0,array," "); print array[3]}'`
end
set er_code = `reghs -$SLOT fee32 0x00B9 | awk '{split($0,array," "); print array[3]}'`
echo $er_code # print operation status: 00000000 - OK
Download ShaperDSP coeficients
set REG_NUM = 0303 # set ShaperDSP register number
set REG_WDATA = 0BB8 # set ShaperDSP register date to be written
reghs -a fee32 0x00B0 0x${REG_NUM}${REG_WDATA}
reghs -a fee32 0x00B2 0x${SH_MASK} # set active ShaperDSP mask
reghs -a fee32 0x00B8 0x4 # init write ShaperDSP register
set er_code = 1 # wait completion of operation
while( $er_code != 00000000 )
set er_code = `reghs -$SLOT fee32 0x00B8 | awk '{split($0,array," "); print array[3]}'`
end
set er_code = `reghs -$SLOT fee32 0x00B9 | awk '{split($0,array," "); print array[3]}'`
echo $er_code # print operation status: 00000000 - OK
Write ShaperDSP registers
Operation recently done only with Ethernet interface can be done now with b2link

## Slide 14: Conclusion
ECL DAQ works smoothly with all 52 EclCollectors connected but in process of continuous improvements
Initialization and verification modules in CBASF TBD
Strip excessive header information

## Slide 15
Thank you

## Slide 16: Calibration 0.7 ns instability
Time shift of the calibration pulse after EclCollector reset
192 channels served by 1 EclCollector
= single calibration pulse generator

## Slide 17
DAC
DATA
DATA CLOCK
CONV
jitter-free clock
FPGA
phase between “data clock”
and “CONV” signals can drift
up to 1 DAC conversion period
DAC has 4 sample pipeline and smart logic
to provide the continuous conversion with
no strict requirements for input data interface.
After reset this logic falls to unpredicted state
unpredicted extra test pulse delay of 0.7 ns
Disabling the logic for auto data-capture
solved the instability problem
Test
pulse

## Slide 18
No time shift after Update

## Slide 19: HIT threshold – original design
Original HIT threshold: If average of two samples at peak is less than set threshold then the processing of this channel is skipped
 Process only channels with hits
Drawback : due to baseline drift we had to set this threshold too low
 effectively no threshold

## Slide 20: HIT threshold – differential design
Differential HIT threshold: average of two samples and peak
and average of 4 samples at baseline
are compared to the set threshold
 Immune to baseline drifts
Diff threshold

## Slide 21: Minor updates
b2tt part in EclCollector updated to v0.48
No spurious LINK state for not connected Shaper interfaces
ShaperDSP coefficients verification
Access to ShaperDSP internals through belle2link  All initialization (except uploading data to flash-memory) can be performed using only belle2link