## Slide 1
Antihydrogen experiments: addressing the challenges of ultra-low temperatures
Sebastian Gerber1 , on behalf of the AEgIS collaboration2
INSTR-17 conference, 27th February - 3rd March 2017
1 CERN, Route de Meyrin 385, 1217 Meyrin, CH
2 http://cern.ch/aegis

## Slide 2
Collaboration

## Slide 3
Currently no experimental WEP test available for antimatter with high precision
normal matter Dg/g:
normal matter WEP:
Hypotheses of gravitational interaction
of matter with antimatter:
normal gravity, supported by EP
graviphoton/graviscalar in quantum gravity theory,
interaction with slightly different magnitude.
Kaluza Metric:
 Neutral antimatter () suitable to reach high precision
Currently hampered by absence of directionally emitted or trapped production in sufficient quantity
Physics goal of AEgIS: measurement of gravitational interaction between matter and antimatter, spectroscopy,…
L. L. Williams, J. of Gravity 6, 901870 (2015)
H. Mueller et al., Nature 463, 926 (2010)
S. Baessler et al., Phys. Rev. Lett. 83, 3583 (1999)
N. Ramsey et al., Quant. Electrodynamics, 673, (1990)
Motivation

## Slide 4
Method
formation via resonant charge exchange
Advantages:
  Pulsed production (time of flight)
    laser-excitation to Ps*
  Colder potentially than via mixing
  defined by + momentum of Ps*
Aghion, S. et al., Nat. Commun. 5:4538 (2014).
AEgIS proposal: http://cdsweb.cern.ch/record/1037532
M. Oberthaler et al., Phys. Rev. A, 54, 3165 (1996)
S. Aghion et al., Nat. Commun. 5, 4538 (2014)
  Measure g for in Moiré deflectometer
  Falling height:
  Requires velocity information of and t0
  Requires high detector resolution
,
L
L
Notes: We intend to form Hbar via resonant change exchange of Rydberg Ps with the following steps, also readable in the Aegis proposal online.
Beer Lambert’s law. Specific depth defined by the cross section, the plasma density and the interaction length.
About 10^-10 cm^2 via Monte Carlo simulations, group intern
e.g. 𝑣_(𝐻 ̅^∗ )=500 m/s, 𝐿 =1 m
-Production of positrons (e+) through a 22Na source and accumulator;
- Capture and accumulation of p from the AD in a cylindrical Penning trap;
- Sympathetic cooling of the p with electrons and/or to sub-K temperatures with anion species
- Production of Ps by bombardment of a cryogenic nanoporous material with an intense e+ pulse;
- Excitation of the Ps to a Rydberg state with principal quantum number n = 25 35;
Pulsed formation of H by resonant charge exchange between Rydberg Ps and cold p ;
- Pulsed formation of an H beam by remaining Ps recoil or Stark acceleration with inhomogeneous electric fields;
- Determination of g in a moire deflectometer coupled with a position-sensitive detector or a tiltable deflectometer with a counting detector.
- Measurement of the HFS of antihydrogen in a microwave flipping cavity coupled with ananalyzing multipolar magnet.

## Slide 5
Crucial step towards the direct detection of the gravitational
acceleration of antihydrogen with the AEgIS experiment Δz = gτ2
P. Scampoli et al., J. Instr. 9, C01061 (2014)
Visibility of 71%; mean force of ~530 aN
(Compatible with a Lorentz force from 1 mT or 30 V/cm)
S. Aghion et al., Nat. Commun. 5, 4538 (2014)
…Moiré deflectometer to measure deflection
of beam (~100 keV) provided by CERN AD facility
Proof of principle with ...
Crucial step towards direct detection of the gravitational
acceleration of antihydrogen with the AEgIS experiment Δz = g t2
Emulsion detector with vertex resolution ~2 mm
9.8 um upwards shift
Annihilation vertex positions of 241 :
0.9 (stat.) 6.4 (syst.) mm
Shift between light and :
Notes: Detector=2.5 cm,
12 um slit width, 40 um periodicity.
Goal: distinguish between annihilation on detector and on interferometer grating:

## Slide 6
Crucial step towards the direct detection of the gravitational
acceleration of antihydrogen with the AEgIS experiment Δz = gτ2
P. Scampoli et al., J. Instr. 9, C01061 (2014)
Visibility of 71%; mean force of ~530 aN
(Compatible with a Lorentz force from 1 mT or 30 V/cm)
S. Aghion et al., Nat. Commun. 5, 4538 (2014)
…Moiré deflectometer to measure deflection
of beam (~100 keV) provided by CERN AD facility
Proof of principle with ...
Crucial step towards direct detection of the gravitational
acceleration of antihydrogen with AEgIS experiment Δz = g t2
9.8 um upwards shift
Annihilation vertex positions of 241 :
0.9 (stat.) 6.4 (syst.) mm
Shift between light and :
Challenges:
1) Position sensitive detector that can distinguish annihilations from secondaries.
2) Production of cold required for precision measurements on g.
Emulsion detector with vertex resolution ~2 mm
Notes: Detector=2.5 cm,
12 um slit width, 40 um periodicity.
Goal: distinguish between annihilation on detector and on interferometer grating:

## Slide 7
P at 8 keV, on 300 um sensor
Timepix3 detector for (and )
Timepix3
Detector and readout provided by courtesy of
the CERN Medipix3 collaboration [1]
Very good time resolution (1.5 ns on ToA and ToT)
High density pixel matrix (55 μm) 256 x 256
5 Gbit/s data rate through Spidr readout (VHDCI connector)
Sensor employed:
675 μm Si, p-on-n, depletion @ 200 V by [2]
[1] Timepix3: T. Poikela et al., J. Instrum. 9, C05013 (2014), doi: 10.1088/1748-0221/9/05/C05013
Timepix: X. Llopart et al., Nucl. Instrum. Meth. A 581, 485 (2007).
[2] ADVACAM http://www.advacam.com

## Slide 8
Test run using Timepix3 detector
Time (ns)
Normalized counts
Pixel time distribution
Test run with Timepix3 detector
tunable 1-16 keV [1]
bunch width 200 ns
AD shot 5 MeV
moderated with
Al foil (46 μm)
to 0-100 keV
Test setup with electrostatic deflector and Einzel-lenses
ToA:
<700 ns main burst from
annihilations in moderator
3x annihilation events of slow
(1 μs~ 10 keV, 2 μs ~ 2.5 keV)
Pixel time distribution for different bending voltages
Importance of tagging:
N. Pacifico et al., Nucl. Instrum. Methods Phys. Res. A 831, 12–17 (2016).
[1] Ion Beam Simulator http://ibsimu.sourceforge.net
,..
At ~ keV , about 2 GeV get redistributed
to ~100 MeV products (only MIPs)
nucleus
4 keV threshold (MIP pass over 55 μm pixel ~14 keV)
Notes: 2GeV get redistriuted Average energy of annihilation products is ~100 MeV
Average energy of annihilation products ~100 MeV
Our case the detection threshold was set at 4keV, well below the expected charge released by a MIP in a sideway spath through a 55 μm pixel(∼14keV).

## Slide 9
Test run using Timepix3 detector
Test run with Timepix3 detector
tunable 1-16 keV [1]
bunch width 200 ns
AD shot 5 MeV
moderated with
Al foil (46 μm)
to 0-100 keV
Test setup with electrostatic deflector and Einzel-lenses
Importance of tagging:
4 keV threshold (MIP pass over 55 μm pixel ~14 keV)
Time (ns)
Normalized counts
Pixel time distribution
N. Pacifico et al., Nucl. Instrum. Methods Phys. Res. A 831, 12–17 (2016).
[1] Ion Beam Simulator http://ibsimu.sourceforge.net
,..
At ~ keV , about 2 GeV get redistributed
to ~100 MeV products (only MIPs)
nucleus
Pixel time distribution for different bending voltages
ToA:
<700 ns main burst from
annihilations in moderator
3x annihilation events of slow
(1 μs~ 10 keV, 2 μs ~ 2.5 keV)

## Slide 10
High dynamic range of ASIC allow for tagging of MIPs and heavy fragments
to distinguish between fragments leaving annihilation site
N. Pacifico et al., Nucl. Instrum. Methods Phys. Res. A 831, 12–17 (2016).
pixel #
pixel #
pixel #
Energy (keV)
Energy (keV)
Energy (keV)
pixel #
pixel #
pixel #
Sample topologies of annihilation events of ~1 keV
Topologies of annihilation events of ~1 keV
~1 keV
bunch width 200 ns
Time tagging allows to distinguish initial MIP shower from annihilation events on detector
Time (ns)
Normalized counts
Pixel time distribution
Topologies of annihilation events of ~1 keV
Average energy of annihilation products ~100 MeVs
TOA
300-700 ns main burst
3x annihilation events of slow pbar
Test run with Timepix3 detector
2 heavily ionizing particles | 3 MIPs, 1 heavily ionizing | 3 MIPs, 1 heavy fragment, 5 heavily with Bragg peak particle ionizing particles with Bragg peak
ToA:
<700 ns main burst from
annihilations in moderator
3x annihilation events of slow
(1 μs~ 10 keV, 2 μs ~ 2.5 keV)
Pixel time distribution for different bending voltages

## Slide 11
High dynamic range of ASIC allow for tagging of MIPs and heavy fragments
to distinguish between fragments leaving annihilation site
N. Pacifico et al., Nucl. Instrum. Methods Phys. Res. A 831, 12–17 (2016).
[1] Jacoboni parametrization for hole mobility: C. Jacoboni et al., Solid State Electron. 20, 77 (1977).
Isometric view of annihilation event.
z coordinate by correlating carrier drift time with the generation depth.
Hole drift velocity parametrization in Si from [1].
Topologies of annihilation events of ~1 keV
~1 keV
bunch width 200 ns
Time tagging allows to distinguish initial MIP shower from annihilation events on detector
Topologies of annihilation events of ~1 keV
Average energy of annihilation products ~100 MeVs
TOA
300-700 ns main burst
3x annihilation events of slow pbar
Test run with Timepix3 detector
Distinction of pions (MIPs) and heavy fragments with time tagging and energy profile
Timepix3 successfully tested down to temperatures of 210 K
Energy (keV)

## Slide 12
 Investigation of
beam - cooling
E. Jordan et al., Phys. Rev. Lett. 115 113001 (2015)
Os- spectroscopy:
U. Warring et al., Phys. Rev. Lett. 102 043001 (2009)
La- spectroscopy:
P. Yzombard et al., Phys. Rev. Lett. 114 213001 (2015)
C2- proposal:
Laser cooling in Penning trap, Picture: D. Dubin, O’Neil, http://sdpha2.ucsd.edu/
1) Precision gravity measurement benefit from low
2)
defined by + momentum of Ps*
Goal for (axial: mK + K momentum transfer from Ps)
cooling mechanism:
      Sympathetic radiation electron cooling (Limit ~30 K with trap temperature ~ 10 K)
      Evaporative / adiabatic cooling (limited by numbers and axial confinement)
      Resistive cooling (proven for single ions, difficult on low-Q plasma modes)
      Sympathetic laser cooling with anions :
S. L. Andersen et al., Eur. Phys. J. D. 68, 124 (2014)
formation currently limited to tens of K [1]
[1] G. B. Andersen et al., Nature Physics 7, 558 (2011).

## Slide 13
C2- benefits:
Known level scheme to n/dn ~100 MHz [1]
Commercial lasers at 2.54 mm and 4.53 mm
Production in gas form
C2- challenges:
16 transitions for closed laser cycle including Zeeman splitting
20 kHz linewidth
Homonuclear molecule
C2
[1] e.g. M. Tulej et al., J. Raman Spectrosc. 41, 853 (2010).
Ro-Vib level structure and molecular potential energy of C2- in B=1 T
The anion candidate C2-

## Slide 14
Acceleration and mass selection
Supersonic expansion simulation of C2-
by U. Even, Tel Avis University, Israel
AEgIS
C2- production and beam
[1] U. Even et al., EPJ Techniques Instr. 2, 17 (2015).
Setup specifications:
Supersonic expansion valve
estimated ~10 meV internal
ground-state occupation [1]
Mass spectroscopy for
100 eV C2-
Einzel-lens telescope
Beam diagnostics
(Faraday cups, MCP)
Mass filter magnet

## Slide 15
C2- production and beam
Setup specifications:
Supersonic expansion valve
estimated ~10 meV internal
ground-state occupation [1]
Mass spectroscopy for
100 eV C2-
Einzel-lens telescope
Beam diagnostics
(Faraday cups, MCP)
[1] U. Even et al., EPJ Techniques Instr. 2, 17 (2015).
to Penning trap

## Slide 16
Three step-plan to reach mK with coolant C2- :
1)…
2)…
3)…
Towards cooling...

## Slide 17
1) Photo-detachement cooling, simulation
rate of photo-detachement [2] for 1 W @ 380 nm :
=5x106 cm-3 , B=1 T
[1] GPU framework Simbuca: S. Van Gorp and P. Dupre (2013): http://dx.doi.org/10.1063/1.4796087
[2] Cross-section calculation by: Viatcheslav Kokoouline, Uni. Orlando, USA (2016).
T0= 0.47 eV binding energy
Cooling C2-
GPU based simulation of 1000 C2- [1]:
T0= 0.47 eV binding energy
C2- simplified level scheme:
380 nm
2.5 mm
C2- |g>
C2- |e>
C2
=5x106 cm-3 , B=1 T

## Slide 18
1) Photo-detachement cooling, simulation
=5x106 cm-3 , B=1 T
T0= 0.47 eV binding energy
Cooling C2-
publication submitted
Factor ~5 temperature reduction,
Photo-e- are released with binding energy
of 0.47 eV: C2- + hn  C2 + e-
e- equilibrate with C2- [1], then thermalize
with 4 K environment in 1 T.
~10 ms experimental time window at lower temperature
Simple to implement
but doesn’t cool enough…
Simulated temperature evolution:
GPU based simulation of 1000 C2-:
T0= 0.47 eV binding energy
=5x106 cm-3 , B=1 T
[1] Electron cooling rate equations: S. Rolston, G. Gabrielse, Hyperf. Int. 44, 233 (1988).

## Slide 19
2 x Doppler-selective 2.5 mm laser
6 x Repumper lasers at 2.5 mm and 4.5 mm
Low Doppler limit ~
Reach ~10 mK temperature within minutes
Crystallization effects at low T
Possible photo-detach before production
2) Doppler cooling, simulation
Dense plasma:
Debye length (20 um)
<< plasma dimension (500 um)
Thermodynamic state of plasma:
H. Totsuji et al., AIP Conf. Proc., 498, 77 (1999)
Possible, but challenging in Penning tap
(scatter ~106 photons, 8 lasers plus sidebands to <MHz stabilized)
Cooling C2- /
Simulation of sympathetic cooling
of 1000 C2- / 100 in 1 T Penning trap.
Time axis scaled (cooling forces) by ~103
Initialized at =107 cm-3 and 11 K

## Slide 20
tspon
wz
P=2.5 W
Pump=10 mW
w=0.2 mm
Cavity:
L=100 mm
FSR=1.5 GHz
delta=0.75 MHz
F=1000
1 x 2.5 mm ~1.5 GHz detuned dipole laser (=7 mK)
Spontaneous decay tspon=50 ms > axial trap motion
5 x lasers at 2.5 mm and 4.5 mm
3) Dipole Force Sisyphus cooling, simulation
Simulation of 1000 C2- in 5 T Penning trap
Cooling C2- /
Sisyphus scheme: J. Dalibard and C. Cohen-Tannoudji, J. Opt. Soc. Am. B, 2, 11 (1985).
Sisyphus cooling in magnetic traps: S. Wu, W. Phillips, J. V. Porto et al., Phys. Rev. Lett. 106, 213001 (2011).
parameters: =107 cm-3 , B=5 T, Dipole laser=2.5 W,
Pump laser=10 mW, waist=0.2 mm

## Slide 21
tspon
wz
P=2.5 W
Pump=10 mW
w=0.2 mm
Cavity:
L=100 mm
FSR=1.5 GHz
delta=0.75 MHz
F=1000
1 x 2.5 mm ~1.5 GHz detuned dipole laser (=7 mK)
Spontaneous decay tspon=50 ms > axial trap motion
5 x lasers at 2.5 mm and 4.5 mm
3) Dipole Force Sisyphus cooling, simulation
Cooling C2- /
publication submitted
Sisyphus scheme: J. Dalibard and C. Cohen-Tannoudji, J. Opt. Soc. Am. B, 2, 11 (1985).
Sisyphus cooling in magnetic traps: S. Wu, W. Phillips, J. V. Porto et al., Phys. Rev. Lett. 106, 213001 (2011).
Simulation of 1000 C2- in 5 T Penning trap

## Slide 22
3) Dipole Force Sisyphus cooling, simulation
mK feasible (scatter ~104 photons, 6x lasers drift stabilized to cell/wavemeter)
sub-K production becomes feasible with current Ps technology
production of trapped sub-K negative ions (impacts on many fields of physics)
Preliminary
publication submitted
Sympatheic cooling with C2-
Simulation of sympathetic cooling of 1000 C2- / 100 m’ in 5 T Penning trap
Time axis (Cooling force ) scaled by ~100 to simulate 1 u cyclotron motion

## Slide 23
Timepix3 coupled to 675 mm Si sensor is suitable as an annihilation detector (and for future ).
Strategy and simulated plan for reaching mK at hand using sympathetic cooling schemes with anions (C2-, La-, Os-).
Not presented in this talk:
Many procedures required for pulsed production of antihydrogen atoms are now working (Ps formation, Ps excitation into Rydberg states, cooling and compression
in 4.5 T to r=260 µm).
...but challenges remain (and antihydrogen beam formation still looms).
We should be in a position for (precision) studies of gravitational interaction of antihydrogen very soon…
We should be in a position for (precision) studies of antihydrogen (and Ps) very soon...
_
Conclusion and Outlook

## Slide 24
Thank you very much for your attention!
We should be in a position for (precision) studies of antihydrogen (and Ps) very soon...
_
Conclusion and Outlook
AEgIS
GRACE
Work on Timepix3
Work on C2- cooling