## Slide 1
A T0/Trigger Detector for the External Target Experiment at CSR
Dongdong Hu
University of Science and Technology of China State Key Laboratory of Particle Detection and Electronics, China
INSTR-2017
February, 27 - March,03,2017

## Slide 2: Outline
Introduction
Experiment
MRPC module
Electronics
Cosmic Ray Test
Heavy-ion Beam Test
Summary

## Slide 3
Introduction
► The equation of state (EOS) of iso-spin asymmetric nuclear matter, particularly the density dependence of the nuclear symmetry energy, is an important question in nuclear physics.
J. M. Lattimer and M. Prakash, Science 304, 536 (2004)
Knowledge on this is crucial to understand
The nuclear structure of heavy nuclei
Form and evolution of compact star
Heavy-ion reaction dynamics and system evolution
Notes: to determine the isospin dependence of the in-medium nuclear effective interactions and the equation of state (EOS) of isospin asymmetric nuclear matter, particularly its isospin-dependent term, i.e., the density dependence of the nuclear symmetry energy. The latter has been identified explicitly as one of the most outstanding questions in the 2007 US Nuclear Physics Long Range Plan by the NSF/DOE’s Nuclear Science Advisory Committee
弱束缚晕核，接近滴线区域原子核基本性质以及对于极端丰中子核核碰撞的动力学研究,发展适用于远离稳定线的核结构理论
宇宙中的核素合成;重星体塌陷;超新星爆炸和中子星形成、结构及演化;中子星中的介子凝聚

## Slide 4
Nuclear EOS at high density
► The density dependence of the nuclear symmetry energy has big discrepancy at supra-saturation region.
Bao-An Li, Lie-Wen Chen, Che Ming Ko, Physics Reports 464 (2008) 113–281
  ► Heavy-ion experiment will help clarify the big theoretical uncertainty
► /+ in heavy-ion collision can be a sensitive probe
   Require heavy-ion beam at several hundred AMeV energy
   HIRFL-CSR (Lanzhou), where core density up to ~20 a suitable machine for this study
Notes: Probes for EOS study: ratios of neutron/proton and/or light mirror nuclei, N/Z ratios of intermediate mass fragments, Neutron–proton correlation functions, and The K0/K+ and pi−/pi+ ratios
HIRFL-CSR is a suitable facility to perform this study

## Slide 5
External-target Experiment at CSR
Heavy-Ion Research Facility at Lanzhou (HIRFL) complex
Cooling Storage Ring (CSR)
External Target Experiment
HIRFL-CSR has the ability of accelerating heavy-ion, from Helium to Uranium, to a kinetic energy of around 0.5-1AGeV
  the START detector (T0) and tracking detector be upgraded
T0 detector
tracking detector
Outer
Inner
Multi-gap Resistive Plate Chamber
Notes: The left plot shows the layout of the Heavy-Ion Research Facility at Lanzhou (HIRFL) complex. The Cooling Storage Ring (CSR) at HIRFL is a heavy-ion facility that can accelerate nuclei up to Uranium with a kinetic projectile energy of several hundred MeV to GeV. Detector upgrades are needed to carry out the heavy-ion collision experiment (to study EOS at high density), including a event START (T0) detector and large acceptance tracking detectors. In my talk I will talk about the T0 detector.

## Slide 6
Structure of MRPC
Multi-gap Resistive Plate Chamber (MRPC):
Gaseous detector,
Avalanche mode
Each gap is 0.22 mm
Inner MRPC has 16 pads.
22.9cm×9.5cm×2.45cm
Outer MRPC has 12 strips.
39.1cm×16.1cm×2.45cm

## Slide 7
Electronics && FEE Module
NINO is an ultra-fast and low-power front-end amplifier/discriminator ASIC designed for the multigap resistive plate chamber , by the group of TOF of ALICE
Inner FEE module，2 NINO chips，16 channels
Outer FEE module，4 NINO chips，24 channels
Through the TOT technology , FEE put the analog signal convert to pulse width LVDS signal (the leading time). Pulse width LVDS signal is the quantity of electric charge signal
Time resolution of all channels are less than 20 ps
Outer FEE
Inner FEE
Inner and outer FEE module time resolution
Charge of input signal fc

## Slide 8
Electronics && FPGA TDC
FPGA TDC
Based on Xilinx’s Artix 7, the FPGA TDC can achieve both leading and trailing edge time measurement; this FPGA also integrates trigger match and other functions
TDC module base on PXI 6U standard is installed in the PXI crate
All channel leading time jitter less than 30ps
Electronics platform test system
Charge of input signal fc

## Slide 9
Cosmic Ray Test
aluminum
Trigger signal
cosmic ray through the scintillation detector
coincidence signal of the 4PMTs
NIM-TTL
PMT
PMT
PMT
PMT
MRPC

## Slide 10
The result of the MRPC time resolution
+
MRPC-t0 time resolution
Different pads time resolution
T-TOT Correlation
Results from HPTDC and FTDC are consistent
The time resolution of MRPC is around 80 ps.
HPTDC
FPGA TDC

## Slide 11
Lanzhou Beam Test system@HIRFL CSR November, 2016
MRPC System
Dipole Magnet (CSR ETF)
Ar Beam
Pb/C target
2*6 0.22mm gas gap - MRPC
90%F134a+5%C4H10+5%SF6
HV：~7kV
Stand-alone self-trigger
Total 80 channels – 40 FTDC, 40 HPTDC
In total ~300k events recorded
Ar40 beam 300 AMeV kinetic energy
Target Pb and C12
Ar+C Ar+Pb
Tracking Detector
T0

## Slide 12
Efficiency Plateau && Typical Hit pattern

## Slide 13
Calibration Strategy
Self-triggered, no tracking, no momentum info, no event vertex, no magnetic field map
Calibration must be carefully applied
We try to calibrate each channel by comparing signals from neighboring pads
time offset
TOT slewing correction (iterative)
Velocity correction
with chosen “clean” event
Outer MRPC
Inner MRPC
Target

## Slide 14
Correction (Velocity)&(TOT)
With FTDC
With HPTDC

## Slide 15
Typical time resolution
HPTDC
FTDC
Collision time mainly determined by inner MRPC timing and particle path-length/momentum spread
Analysis still on-going
135 ps
T0

## Slide 16
Simulation study of CSR-T0
The time resolution of MRPC may be around or even better than75 ps
Monte Carlo (MC) simulation based on GEANT4 toolkit, with practical detector (MRPC etc.) model
Event generator:
  UrQMD3.4, kinetic energy 300AMeV 40Ar+12C collision
Beam spread xy=3mm
MRPC timing uncertainty
  t=50ps,75ps,100ps tested
Particle flight trajectory taken from MC
With time smearing t=75ps,
the experiment result and the simulation result are consistent
T0

## Slide 17: Summary
thanks
We have designed and produced the inner and outer MRPC. Tested their performance
Designed the FPGA TDC , FEE electronics System for this experiment , time jitter of electronics System is less than 30 ps
From the Comics ray test, MPRC’s time resolution to be around 80 ps
From the preliminary result of the heavy-ion beam test at the CSR, the performance of the MRPC has met our expectation. The T0 time resolution seems promising.
Analysis is in progress

## Slide 18
backup

## Slide 19
MRPC (Multi-gap Resistive Plate Chamber) is a gaseous detector technology first developed by the ALICE experiment.
Characteristic:
1) MRPC is basically a stack of parallel resistive plates with a bulk resistively of around 1012~1013 cm and create a series of gas gap of 0.2 - 0.3 mm. The narrow gaps will decrease the fluctuation of avalanche development time and thus improves the time resolution.
2) A strong electric field is generated in each gas gap by applying a high voltage across the external electrodes . A signal induced on pickup pad is the sum of signals from all the gas gaps since the resistive plates are electrically floating when charged particle going through the chamber generates avalanches in gas gaps.
Good candidate for time measurement !
MRPC
Nucl. Instr.& Meth. A374 (1996) 132 by M.C.S.Williams et al.

## Slide 20
Peking Beam Test system
Beam
@ Peking
October 2016
Pion and proton is the main particle
Momentum 700 MeV

## Slide 21
Algorithm
Because (-) and (-) is independence ，though the statistics
[(-) - (-)] = (-) +(-)
mean
(-) =[(-) - (-) - (-)
=( - ) - (-)
-= = (- ) -(-)
=[-] - []
σ(-) =
Suppose 𝑇0= (𝑇1+𝑇2+𝑇3+𝑇4)/4
MRPC time resolution is
σ (-)
The time resolution of
σ(-)

## Slide 22
The present result
Before calibration
After calibration
T-A correction
After Slewing correction

## Slide 23
The present result
σ(-) =
=
=81.1 (ps)
The MRPC time resolution is 81.1PS

## Slide 24
MC simulation – event plane
0.5AGeV AuAu collision, simulated by UrQMD3.4.6
Q-vector reconstruction to determine event plane
T0 acceptance
Event plane resolution
1st order Q-vector
T0 detector can also be used to determine event plane

## Slide 25
target
—CSR Trigger/T0 Detector simulation and design optimization
w/o MRPC resolution
w/o field
Track-length from MC
ART1.0, Xe+Xe 700AMeV
By inner MRPC itself to decide the starting time is inaccuracy.
We can Slewing correction momentum dispersion eliminate the time error , through inner and outer layer MRPC time difference.
CSR-T0/Trigger Detector
v'=L2/(T2-T1)/c
Notes: T0 = T1-L1/v = T2-L2/v
V can be estimated by T1,T2 and L1,L2
v’= L2/c/(T2-T1)其中T1、T2 分别为同一带点粒子在内、外桶上的击中时间，L1、L2 为内、外桶击中位置到靶点的直线距离。由于末态带电粒子动量较低，在飞行过程中有明显的能量损失，为了得到好的T0 定时精度，需要根据粒子动量（或速度）加以刻度。定义约化粒子速率为
v'=L2/(T2-T1)/c
T2-T1 为两次击中的时间差，c 为真空中光速。