## Slide 1: WA105 experiment at CERN: large demonstrator of Dual Phase Liquid Argon TPC detector for DUNE
Wladyslaw Henryk Trzaska on behalf of WA105 Collaboration
INSTR - 2017

## Slide 2: DUNE – Deep Underground Neutrino Experiment
The aim: broad physics program including CP violation, mass hierarchy, precision neutrino oscillation measurements, search for nucleon decays, and supernova neutrino observation
The method: a long-baseline neutrino experiment that will observe neutrino oscillations with a 40 kton underground far detector and upgradeable 1.2 MW neutrino beam
Logistics: Fermilab beam  far detector in South Dakota, USA
Detector technology: a 4 x 10 kton (fiducial) LAr TPC
Timescale: first beam in 2026, first 10 kton detector in 2024

## Slide 4
4 x 10 kton (fiducial) Liquid Argon
Time Projection Chamber

## Slide 5
4 x 10 kton (fiducial) LAr TPC

## Slide 6: Principle of operation of a LAr TPC
20 ppt O2
2 ppt O2
0.2 ppb O2
0.5 kV/cm
1.5 kV/cm
1.25 kV/cm
1 kV/cm
0.75 kV/cm

## Slide 7: LAr TPC: the “electronic bubble chamber”
800cm
ICARUS T600 (2 x 300 ton) at Gran Sasso

## Slide 8: Dual Phase LAr TPC
Large Electron Amplifier (LEM)
0.5 – 1 kV/cm

## Slide 9
Stable gain of x 27
Signal-over-noise ratio > 200
2D readout anode
E-field configuration
Badertscher, A. et al. NIM A641 (2011) 48-57 arXiv:1012.0483 [physics.ins-det]

## Slide 10: Advantages of DP vs. SP LAr TPC
Amplification in the gas phase
  Improved signal to noise ratio
  Improved imaging capabilities
Key instrumentation (Charge Readout Planes) on the top
  Fiducial volume completely free of interfering objects
  Scalable and cost-effective
  Good accessibility / service
Not yet tested on a large scale (~300 ton)
  This is the task of WA105

## Slide 11: WA105  DUNE
Large demonstrator at CERN (pilot) 3 x 1 x 1 m3
  Starts operation in Spring 2017
ProtoDune DP 6 x 6 x 6 m3 at CERN
  Scalable design, underground-like installation
  Measurements with charged particle beam in 2018
    Detector calibration & reconstruction algorithms
Detector module underground 60 x 12 x 12 m3
  It is likely that already the 2nd 10 kton module will be DP

## Slide 12: WA105 3 x 1 x 1 m3 demonstrator
First large-scale dual phase TPC
Total LAr mass 25 ton
Active mass 4.2 ton
readout pitch 3 mm
2 views
1920 readout channels
(3+2) 8” PMTs
Membrane tank (LNG technology)

## Slide 13
3x1x1 membrane tank LNG-type

## Slide 16
Cosmic Ray Trigger

## Slide 17
Charge Readout plane (CRP)
Drift cage (500 V/cm or 1kV/cm)
TPB coated photomultipliers
CRP suspension.
1 m
3 m
1 m

## Slide 18
4 July 2016

## Slide 24: WA105  CENF NP02  protoDUNE DP
2012: proposal submitted to CERN  WA105
  the main outcome of LAGUNA-LBNO
  Long-term goal in 2012: LBNO with CERN to Pyhäsalmi beam
2014: new CERN strategy
  No neutrino beam from CERN; instead
  CERN Neutrino Platform (CENF) was established,
  WA105 6x6x6 became part of CENF as NP02
2015: DUNE Collaboration formed
  WA105 6x6x6  ProtoDUNE Dual Phase

## Slide 25
EHN1 – new building to house
6 x 6 x 6 ProtoDUNE SP
6 x 6 x 6 ProtoDUNE DP

## Slide 26
April 2016

## Slide 27
October 2016

## Slide 28
2 December 2016

## Slide 29
NP04 January 2016

## Slide 30
http://cenf-ehn1-np.web.cern.ch/multimedia/images

## Slide 32
E=0.5-1.0 kV/cm
Cathode
Segmented anode
in gas phase with
dual phase amplification
LAr volume
X and Y charge collection strips
3.125 mm pitch, 3 m long  7680 readout channels
Dual phase liquid argon TPC
6 x 6 x 6 m3 active volume
Drift
Drift coordinate
6 m = 4 ms
sampling 2.5 MHz
(400 ns), 12 bits
10000 samples
per drift window
6 m
3 m
Prompt UV
light
dE/dx  ionization
Photomultipliers
Event size:
drift window of 7680 channels x 10000 samples ⇒ 146.8 MB
6 m
10 kton DUNE 5.872 GB/event
Event size estimation

## Slide 33
6 m
6 x 6 x 6 Modular & scalable construction

## Slide 34
CRP 3x3 m2 units in 3.2x3.2x0.5 m3 boxes inserted via TCO using a rail system
Underground-like installation scheme

## Slide 35: ProtoDUNE  DUNE 10 x longer, 2 x wider, 2 x taller
6 x 6 x 6
60 x 12 x 12

## Slide 36
65.84m
39 frames (1.6m)
18.94m
17.84m
8frames (1.6m)
Membrane tank for a 10 kton detector

## Slide 37: Cryogenics will be installed on top of each 10 kton detector unit
35 m
12 m
2.3 m
7.7 m

## Slide 39
WA105: 122 scientists, 21 institutes, 8 countries
All are also members of DUNE Collaboration!

## Slide 40: Thank you for your attention!