## Slide 1
Status and perspectives for the INFN Frascati national laboratory
Laboratori Nazionali di Frascati (LNF) is the oldest (1955) Italian research infrastructure for fundamental research.
It is also the biggest lab of Istituto Nazionale di Fisica Nucleare (INFN), the institution that in Italy funds and coordinates the research for Nuclear and Particle Physics.

## Slide 2
LNF History
The tradition of the lab has been always in the field of hadron physics:
1959 – 1975 Electro-Syncrotron (max energy 1.1 GeV);
1960 Anello di Annichilazione First particle collider (beam energy 200 MeV);
1969 – 1993 ADONE e+e– collider (c.m. energy up to 3 GeV);
2001 – today DAΦNE e+e– collider (c.m. energy 1.120 GeV);
ADA
DAΦNE

## Slide 3
LNF activities
DAΦNE
KLOE
data taking this year
FINUDA
end of data taking in 2007
SIDDHARTA
new of data taking in 2015
Developments
of new accelerator
technique
CTF3
CLIC
Research and
Developments
of
Detectors
Medical Application
X-ray
Laboratory
ATLAS-CERN
CMS-CERN
LHC-b-CERN
NA62-CERN
BES3-BEPC
BABAR-SLAC
Belle2-KEKB
Astro-particles
Physics
Physics in
space
Cryogenic
antenna
NAUTILUS
High intensity
laser
FLAME
Free Electron
Laser (FEL)
SPARC
Syncrotron
light
LdS
Hadron
therapy
CNAO

## Slide 4
Accelerator Complex
BTF
DAΦNE
DAΦNE-light
LINAC
FLAME

## Slide 5
A better view of the BTF Complex
DR hall
BTF
hall
DR
power
BTF
control room
Nuclear Physics
building
DR pumping
KLOE
DAFNE hall
Linac tunnel
Modulators
hall

## Slide 6
BTF Diagnostics
High intensity
Integrating current toroid
Fluorescence flag
Medium-low intensity
Scintillating fibers hodoscope
Silicon micro-strip detectors (currently under maintenance]
GEM Time-projection chambers

## Slide 7
Photon tagging
dipole magnet
silicon tagging
target
silicon detectors
Be window
Bremsstrahlung
photon
Incoming electron
Designed and built in close collaboration with the AGILE collaboration with the main purpose of the AGILE scientific payload calibration:
  Silicon trackers + calorimeter

## Slide 8
And…Neutron source
d (m) | ×10-5 n/cm2/pr
0.5 | 63
1 | 5.7
1.5 | 1
At 1.5 m distance:
Total neutron flux: 8×10-7 n/cm2/pr ±3%
Flux = 4.5×105 n/cm2/s
Equivalente dose = 45 mSv/h

## Slide 9
In the future.. New btf lines
  Keep using 0° line for ‘standard’ testing
  Use 45° line to drive beam to a new “target area”
    This allows to have a target station dedicated to neutron production and
    A space for neutron experiments
  Add 90° to build a “low energy” line
    This allows to use the Linac groundwork and tunnel as additional shielding

## Slide 10
Advanced Acceleration at SPARC_LAB
Sources for Plasma Accelerators and Radiation Compton with Lasers And Beams

## Slide 11
Advanced Acceleration at SPARC_LAB
Undulators
u = 2.8 cm
Kmax = 2.2
r = 500 nm
15 m
Diagnostic and Matching
150 MeV S-band linac
12 m

## Slide 12
New installations
Thomson source
Plasma acceleration

## Slide 13
The External Injection Experiment@SPARC_LAB (Simulation results)
EXIN goals:
Produce High brilliance e-beam peak
or global.
Stability
Reproducibility.
Everything in the easiest way
εnx = 3.5 μm
σx = 2.0 μm
E = 630 MeV
Δγ/γ= 7.7 %
Best beam: Δt = 182 fs, σx = 3.8 μm.
Experiment will take place in 2-3 years from now
The plasma is created by the laser pulse which also drives the beam

## Slide 14
Particle Wakefield acceleration
Resonant plasma excitation by a Train of Bunches
Laser Comb to produce high Brightness electron bunches?
High quality bunch preservation during acceleration and transport. preservatiort?

## Slide 15
First test results
Resonant plasma excitation by a Train of Bunches
In this case plasma is created by
a discharge in Hydrogen and driven by the
first 3 driver beams.
2015-2016 first experiment results

## Slide 16
IRIDE: Interdisciplinary Research Infrastructure with Dual Electron linacs&lasers
aims and potentials (The Future)
Science with Free Electron Lasers (FEL) from infrared to X-rays,
Nuclear photonics with Compton back-scattering g-rays sources,
Science with THz radiation sources,
Advanced Neutron sources by photo-production,
Fundamental physics investigations with low energy linear colliders
Physics with high power/intensity lasers,
R&D on advanced accelerator concepts including plasma accelerators and polarized positron sources
ILC technology implementation
Detector development for X-ray FEL and Linear Colliders
R&D in accelerator technology and industrial spin – off

## Slide 17
2K-CRYO
2K-CRYO
GeV
GeV
GeV
I R I D E is a large infrastructure for fundamental and applied physics research. Conceived as an innovative and evolutionary tool for multi-disciplinary investigations in a wide field of scientific, technological and industrial applications, it will be a high intensity “particle beams factory”.
Based on a combination of a high duty cycle radio-frequency superconducting electron linac (SC RF LINAC) and of high energy lasers it will be able to produce a high flux of electrons, photons (from infrared to g-rays), neutrons, protons and eventually positrons, that will be available for a wide national and international scientific community interested to take profit of the most advanced particle and radiation sources.
PWA
1032
1030
n,po
1014
e+
109
g
IRIDE

## Slide 18
IRIDE
FEL2
Inj2
FEL1
FF
CS
Inj1
THz
L1
L2

## Slide 19
Using extremely short and intense X-ray pulses to capture images of objects such as proteins before the X-rays destroy the sample.
Single-molecule diffractive imaging with an X-ray free-electron laser.
Individual biological molecules will be made to fall through the X-ray beam, one at a time, and their structural information recorded in the form of a diffraction pattern.
The pulse will ultimately destroy each molecule, but not before the pulse has diffracted from the undamaged structure.
The patterns are combined to form an atomic-resolution image of the molecule.
The speed record of 25 femtoseconds for flash imaging was achieved.
Models indicate that atomic-resolution imaging can be achieved with pulses shorter than 20 femtoseconds.
Lawrence Livermore National Laboratory (LLNL)
There is also room for Protein imaging
P. Branchini on behalf of LNF

## Slide 20
Superconductivity Energy gap Symmetry of the order parameter Direct determination of the superfluid density Dynamics of Cooper pairs
Low-dimensional materials
Dimensionality crossover Non-Fermi liquid normal states Broken symmetry ground states
Coherent Phase Transitions Polarons Structural Phase Transitions
Magnetic sub-ps Dynamics
Condensed Matter Physics
Life Sciences
Macromolecules conformation
Secondary and tertiary structure
Coherent dynamic development
Imaging
3D tomography of dry tissues
Near-field sub-wavelenght spatial resolution
Polar liquids
Hydrogen bond
Van der Waals interactions
Acoustic-Optic phonon mixing in water
Solutions
Static and dynamic interactions between solvated
ions and solvent
Physical and Analytical Chemistry
New Technologies
THz technologies
Array THz detectors
Metamaterials
Medical diagnostic
Skin cancer detection
Industrial production
Material inspection
Production line monitoring
Defense industry/Homeland security
Detection of explosives and biohazards
P. Branchini on behalf of LNF
THz radiation source

## Slide 21
This source may be suitable for multiple applications, ranging from material analysis for industrial and cultural heritages purposes to chip irradiation and metrology. These applications envisage the development of properly designed beam lines with neutron moderation and possibly cold/thermal neutron transport systems. The proposed new facility will represent a great opportunity for research and development of neutron instrumentation (e.g. detectors) as well as training of young scientist in the use and development of neutron techniques.
Neutron source
P. Branchini on behalf of LNF

## Slide 22: e-γ, γ-γ Collider options
And last but not least: Particle physics opportunities
P. Branchini on behalf of LNF
studies of the nucleus structure at the Pigmy and Giant Dipole Resonance with unprecedented resolution in the reconstruction of the nuclear states;
electron-photon collision can be a source of π0 produced via the Primakoff effect having an electron as a “target” instead of a nucleus;
search for beyond-standard-model (BSM), weakly interacting boson “U”;
The elastic photon-photon scattering offers unique opportunities to probe the nature of QED vacuum. An experiment to observe photon-photon scattering in the range 1 MeV – 2 MeV CM energy, i.e., near the peak of the QED cross-section will be performed.
e−
γ
e−
γ
U
e−
e+
Nuclear and Particle Physics will benefit from the availability
of these new generation γ-ray beams for:

## Slide 23: e+ e- Linear Collider
And last but not least: Particle physics opportunities
P. Branchini on behalf of LNF
An electron-positron collider with luminosity of 1032 cm−2s−1 with c.m. energy ranging from the the φ-resonance up to ∼3.0 GeV, would allow many fundamental measurements.
CRYO
CRYO
1.5 GeV
1.5 GeV
3 GeV
e+
Precision measurement of muon (g-2);
Precise measurement of the fine-structure constant αS;
Study of scalar resonances;
Spectroscopy of baryon form factors

## Slide 24
The Frascati F factory
Production of Φ particles via the
annihilation of electrons and positrons
at the energy of the resonance.
 | DANE upgrade SIDDHARTA Crab Waist collision scheme | DANE KLOE | DANE FINUDA
Lpeak [cm-2s-1] | 4.53•1032 (5.0•1032) | 1.5•1032 | 1.6 •1032
L∫day [pb-1] | 14.98 | 9.8 | 9.4
L∫1 hour [pb-1] | 1.033 | 0.44 | 0.5
Syncrotron ligth from DAΦNE
LNF are part of the European
Infrastructure
for syncrotron light
UV 2 - 10 eV
X-ray 900 - 3000 eV
IR 1.24 meV - 1.24 eV

## Slide 25
Dafne Luminosity 2001-2009
Crab-Waist COLLISION SCHEME
Design Goal
SIDDHARTA (DEAR)
KLOE
FINUDA

## Slide 26
KLOE at DAFNE
The experiment has taken data from 2000 to 2006, collecting 2.5 fb-1 at the Φ peak, plus additional 0.25 fb-1 at 1000 MeV.
KLOE is multi-purpose detector optimized for KL physics
Drift Chamber
E.M. Calorimeter
Huge, transparent Drift Chamber
in 5.2 k Gauss field of a SC coil;
Carbon fiber walls, 55000 stereo wires,
2 m radius, 4 m long, He/CO2 gas mixture;
Momentum resolution: σ(pT)/pT ~ 0.4%.
Pb-Scintillating Fiber Calorimeter with excellent timing performance
24 barrel modules, 4 m long and C-shaped End-Caps for 98% solid angle coverage
Time resolution = 54 ps / √E(GeV) ⊕ 50 ps;
Energy resolution = 5.7% / √E(GeV)

## Slide 27
Large Crossing Angle, Small x size
KLOE
FINUDA
1) Head-on,
Short bunches
Overlap region
sz
sx
sz
sx
(1) and (2) have same Luminosity, but (2) has longer bunches and smaller sx
2) Large crossing angle,
long bunches
Vertical waist has to be a function of x:
Z = 0 for particles at –sx (- sx/2q at low current)
Z = sx/q for particles at + sx (sx/2q at low current)
Large Piwinski angle:
F = tg(q)sz/sx
Y
y waist can be moved
along z with a sextupole
on both sides of IP
at proper phase
“Crab Waist”

## Slide 28
Crab-Waist Scheme
KLOE
FINUDA
Crab sextupoles OFF: Waist line is orthogonal to the axis of other beam
Raimondi, Shatilov, Zobov http://arxiv.org/abs/physics/0702033
Crab sextupoles ON: Waist aligned with path of other beam
particles at higher ß do not see full field of other beam
no excessive beam-beam parameter due to hourglass effect

## Slide 29
september 2013
I ~ 460 mA
I1b ~ 7.3 mA
Beam current limited by collective effects:
  Transverse beam size grows with the current due to ion trapping
  transverse instabilities appear above ~ 460 mA.
Further improvements required:
  recovering optimal vacuum condition
  tuning transverse feedbacks
100 bunches
September 26th 2013

## Slide 30
From september up to now
Natural coupling of the positron beam
Coupling of the electron beam
After much work on collider consolidation
we are gettiing close to the DAFNE design
parameters.
We could store:
I+ ~ 1.1 A
I- ~ 1.4 A

## Slide 31
Feb 10th 2014
Daily integrated luminosity
As measured by KLOE.
Obtained:
A week after restarting collisions
With Crab-Sextupoles off
The uptime is close to 100%

## Slide 32
Het Status
Modification/Improvement of the mechanics of the movement system
New Detector BOX in order to locate Front End board very close to the PMT essentially to reduce the noise

## Slide 33
Test of the HETs
Noise without Beam :
A threshold of about 20 mV reduce the noise at level of few Hz
Data with e- or e+ beams on DAFNE :
We clearly identify and distinguish contiguous bunches (2.7 ns)

## Slide 34
Low Energy Tagger
Integration with QCALT
Installation completed in June 2013
W shields
LET
QCALT
Window in the
beam-pipe support

## Slide 35
Calibration with cosmics
Z [cm]
X [cm]
track intersection with
the horizontal plane ⇒
Track selection with
EMC
TDC spectrum [counts]
MIP examples
⇒

## Slide 36
QCALT Installationand tests
LET housing and shileding
Both QCALT installed
on May 2013
26pe/mip
750 ps time resolution after slewing correction LY 26 pe/mip/tile
Results already satisfying for QCALT requests

## Slide 37
Ccalt installation and performances (Timing)
We determined it at BTF of Frascati, with a single crystal (20x20x15 mm2) read out by a 10x10 mm2 Hamamatsu APD
250 (90) ps @ 500 MeV
290 (120) ps @ 100 MeV
Time resolution:

## Slide 38
IT final assembly
The final assembly of the KLOE-2 Inner Tracker, with the insertion of all the triple-CGEMs one into the other took place in March 2013

## Slide 39
IT integration
Protection shell installation
Interaction region movement
Kapton protection on the HV boards
IR positioning

## Slide 40
Results from first KLOE-2 runs
Number of strips hit for event on all the layers for both views
Efficiency | 
Layer 1 | 75%
Layer 2 | 89%
Layer 3 | 90%
Layer 4 | 57%
To be investigated
Cosmic-ray muon sample selected with EMC info
Operational parameters not yet optimized

## Slide 41
KLOE-2 Physics Program
Kaon Physics
  Test of CPT (and QM) in correlated kaon decays and test of CPT in KS semileptonic decays
  Test of SM (CKM unitarity, lepton universality)
  Test of χPT (KS decays)
Spectroscopy of light mesons
  η,η’,f0,a0,σ in φ radiative decays
Hadronic cross section from 2mπ to 2.4 GeV
  αem(MZ) and (g-2)μ
γγ Physics
  Study of Γ(S/PS→γγ), test of χPT, existence and properties of σ meson………
Dark Matter searches (light bosons at at O(1 GeV))

## Slide 42
SIDDHARTA future plans
SIDDHARTA Physics program will continue for next years with SIDDHARTA-2.
The detector will be placed in the IP2 after the KLOE-2 data taking.
Kaonic deuterium measurement - 1st measurement
Kaonic helium transitions to the 1s level
3) Other light kaonic atoms (KO, KC,…) 4) Heavier kaonic atoms measurement
(Si, Pb…) 5) Kaon radiative capture – Λ(1405) study 6) Investigate the possibility of the measurement of other types of hadronic exotic atoms (sigmonic hydrogen?) 7) Kaon mass precision measurement at the level of <10 keV

## Slide 43
Conclusions
DAΦNE accelerator scientific life is almost at the end.
LNF is exploring new exciting possibilities and can evolve
into a multi-disciplinary laboratory.
SPARC, IRIDE and space science together with the particle physics (a traditional activity at LNF) science will play an important role in the years to come.