## Slide 1
PANDA Solenoid Magnet
as a prototype for Super c-tau factory

## Slide 2
The accelerator facility FAIR and GSI

## Slide 3
The main milestones of production of the PANDA solenoid magnet
The scope of delivery includes:
Magnetic and engineering design of the magnet including tools and support;
Production and delivery of the magnet (consisting of yoke, cold mass and cryostat, alignment components, proximity cryogenics, support frame and platform beams) and all tools;
Power converter and quench protection and instrumentation.
Item | Date
Start contract | 03/2017
Control assembling of the Yoke of solenoid at the BINP site | 09/2019
Magnetic tests of the PANDA solenoid including safety system and electrical components at BINP (additional contract) | 07/2020 - 05/2021
Assembling and tests at the FAIR site | 
Assembling of the Yoke at Darmstadt | 11/2021
Acceptant tests at FAIR | 08/2022
Installation of the PANDA solenoid magnet in beam position and start final acceptance tests | 01 - 05/2023

## Slide 4
The PANDA solenoid is designed to provide a magnetic field of 2 T with a uniformity of ± 2% and radial magnetic field integral in the range 0 to 2 mm over the central tracking region. The magnet is characterized by a warm bore of 1.9 m diameter, a free length of 4 m and 22.4 MJ of stored energy.
PANDA solenoid magnet
Artistic view of the solenoid magnet including detector systems

## Slide 5
PANDA solenoid magnet, BINP responsibility
Arrangement of the components of the PANDA solenoid.
Power supply and energy extraction system
Cable channel
Control Dewar box
Solenoid and yoke
Frame of solenoid

## Slide 6
Hydraulic cylinders.
PANDA solenoid magnet posibilities
The PANDA magnet will be transported to the beam position after assembly and back for maintenance on four track-guided roller carriages placed below the platform beams. The length of moving is about 18,5 m during 4-8 hours.
The magnet poles are made in a form of doors that can be opened for access to the inner detectors. Each door consists of two wings, which are resting on the rails on the platform cornices and can slide along the rails on the roller carriages. The door opening mechanism is based on the use of hydraulic cylinders. Estimation time to dismount the door from barrel part of yoke and open the wings is 3-4 hours.

## Slide 7
Longitudinal section of the solenoid
Solenoid consists from 3 coils.
Holes for target pipe

## Slide 8
2 Coils - 6 layers - 78 turns (2x3300 м)
1 Coil - 6 layers - 35 turns (1500 м)
Magnetic field - 2 T
Current - 4.96 kA
The design of Cold mass.

## Slide 9
Magnetic flux density distribution in the YZ-plane of the PANDA detector.
Magnetic Analysis
The PANDA solenoid is designed to provide a magnetic field of 2 T over a length of about 4 am in a bore of 1.9 m. The field homogeneity constraints over the Central Tracker volume require uniformity better than ±2% and a radial field integral below 2 mm.
The magnetic design has been validated via 3D finite element modeling in TOSCA.

## Slide 10
The cryogenic scheme of the PANDA solenoid relies on indirect cooling of the cold mass by circulating saturated helium at 4.5 K by natural convection. The thermo-syphon circuit consists of a bottom and top manifolds connected by 16 parallel syphon tubes attached to the outer surface of the support cylinder.
Cold Mass Thermalization
Control Dewar with 300l LHe vessel
Cold mass
Transfer line to
helium liquefier
T=4,5K | Thermal loads, W
Normal | 18,1
Transit regime | 29,7
T= 60K | 
Normal | 180,1
Transit regime | 240,6
300 l LHe vessel

## Slide 11
Development of the PANDA solenoid magnet on today
Name of item | Status of work
Yoke and frame | Design is ready, start production
Cryostat of solenoid | Design is ready, FDR 11/2018 Technologic work, design of tools
Cold mass | Design is ready, FDR 11/2018 Technologic work, design of tools
Conductor purchasing | Development work
Control Dewar box | Design in progress
Cable channel | Start design
Power supply and energy extraction system | Design in progress, FDR 11/ 2018
Magnet safety system | Start discussing 11th week 2018

## Slide 12
Magnets for SCTF and PANDA
SCTF requirements | 
Length Inner diameter Magnetic field Stored energy I, solenoid (1,5T) Weight | 4m; 3,2 m; 1 ÷ 1,2 T; 28 MJ; 4 kA; 500 t.
PANDA requirements | 
Length Inner diameter Magnetic field Stored energy I, solenoid Weight | 3m; 1,9 m; 2 T; 22,4 MJ; 5,1 kA; 340 t.
Longitudinal section of the
yoke with cryostat of the magnet
Octant of the yoke

## Slide 13
Conclusion
Engineering design of the magnet including tools and support;
Procedures assembling of the yoke with frame;
Procedures moving of the detector;
Procedures open/close the doors of the yoke;
Design of the cryostat and cold mass;
Technology production of coils;
Procedures assembling of the cold mass, installation of the cold mass to cryostat and installation of the cryostat to the yoke;
Development of the proximity cryogenics with using helium liquefier;
Procedures assembling/disassembling of the cryogenic system that moving the detector;
Development power converter 5kA, quench protection and extraction energy system;
Magnetic measurement procedures,
Delivery PANDA solenoid magnet includes:
all these developments will be used in the design and manufacture of a magnet for SCTF.

## Slide 14
Thank you for your attention