## Slide 1
15, Novosibirsk, 17.11.2015
The Barrel DIRC of the
Experiment at FAIR
Georg Schepers
(GSI Darmstadt)
for the PANDA Cherenkov Group
PANDA Experiment
DIRC Concept
Barrel DIRC of PANDA
Prelim. Test Beam Results

## Slide 2
experiment

## Slide 3
HESR
SIS 100/300
SIS18
RESR/CR
30 GeV Protons
70 MeV
p-Linac
p Target
PANDA
experiment

## Slide 4
HESR
SIS 100/300
SIS18
RESR/CR
30 GeV Protons
70 MeV
p-Linac
p Target
PANDA
experiment
HESR
1011 stored antiprotons with beam momentum of 1.5 - 15 GeV/c
Δp/p of 4 x 10-5 with 1010 stored antiprotons

## Slide 5
Target Spectrometer Forward Spectrometer
experiment
AntiProton ANihilation at DArmstadt
12m

## Slide 6
12m
experiment
>500 physicists
67 institutes
19 countries
Collaboration
Target Spectrometer Forward Spectrometer

## Slide 7
experiment
anti-proton beam on pellet/cluster target
Target Spectrometer Forward Spectrometer
12m
Luminosity
up to 2 x 1032 cm-2s-1
Average interaction rate up to 2 x 107/s

## Slide 8
experiment
Study of open issues of QCD
Target Spectrometer Forward Spectrometer
12m
Hadron spectroscopy
Properties of hadrons
in matter
Nucleon structure
Hypernuclei

## Slide 9
experiment
Particle identification methods
momentum range: 0.2 GeV/c – 10GeV/c
Target Spectrometer Forward Spectrometer
12m
Energy loss
EM showers
Time of Flight
Cherenkov radiation

## Slide 10
Cherenkov effect
Particle velocity β = v/c > 1/n
transmitted into photon angle cos θc = 1/βn(λ)
concept
momentum [GeV/c]
[mrad]

## Slide 11
DIRC Concept
Novel kind of
Ring Imaging Cherenkov Detector
B.N. Ratcliff, SLAC-PUB-6047 (Jan. 1993)
Detection of Internally Reflected Cherenkov Light
concept

## Slide 12
DIRC Concept
concept
Radiators with polished surfaces and
orthogonal sides:
For n>√2 some photons are always
totally internally reflected for β≈1 tracks
Magnitude of Cherenkov angle conserved during internal reflections
Photons exit radiator via the (optional) focusing optics into expansion region, detected on photon detector array
Novel kind of
Ring Imaging Cherenkov Detector
B.N. Ratcliff, SLAC-PUB-6047 (Jan. 1993)
Detection of Internally Reflected Cherenkov Light

## Slide 13
DIRC Concept
concept
Radiators with polished surfaces and
orthogonal sides:
For n>√2 some photons are always
totally internally reflected for β≈1 tracks
Magnitude of Cherenkov angle conserved during internal reflections
Photons exit radiator via the (optional) focusing optics into expansion region, detected on photon detector array
Measurement: x, y, and time
Deduction: θc, φc, tpropagation
Information: PID-Likelihood from
hitpatterns for different
particle species
Geometrical Reconstruction: Bar to Pixel
Novel kind of
Ring Imaging Cherenkov Detector
B.N. Ratcliff, SLAC-PUB-6047 (Jan. 1993)
Detection of Internally Reflected Cherenkov Light

## Slide 14
Successful BaBar DIRC
concept
500cm
500cm
Single photon timing resolution 1.7ns
Single photon Cherenkov angle
resolution ~10mrad
Photon yield, photons per track 20 - 60
Track Cherenkov angle resolution 2.4mrad
(di-muons)
π/K separation power 4.3σ@ 3GeV/c
~3σ @ 4GeV/c
Time cut on Accelerator background from the water tank
Expansion Volume
common water tank

## Slide 15
DIRC Cherenkov Angle Resolution
  Correlated term:
  tracking detectors, multiple scattering
  Single photon Cherenkov angle resolution: bar size, pixel size, chromatic, bar imperfections
  Number of photons: bar size, bar imperfections, photon detection efficiency of the detector
concept

## Slide 16
DIRC Cherenkov Angle Resolution
  Correlated term:
  tracking detectors, multiple scattering
  Single photon Cherenkov angle resolution: bar size, pixel size, chromatic, bar imperfections
  Number of photons: bar size, bar imperfections, photon detection efficiency of the detector
concept

## Slide 17
DIRCs in PANDA
Kaon phase space coverage for reactions with
p-bar momentum between 6 GeV/c and 15 GeV/c
Simulation
panda dirc

## Slide 18
DIRCs in PANDA
Target Spectrometer
Barrel DIRC
Design similar to BaBar DIRC
Polar angle coverage:
22° < θ < 140°
PID goal:
3σ π/K separation up to 3.5 GeV/c
Endcap Disc DIRC
Novel type of DIRC
Polar angle coverage:
5° < θ < 22°
PID goal:
3σ π/K separation up to 4 GeV/c
Kaon phase space coverage for reactions with
p-bar momentum between 6 GeV/c and 15 GeV/c
Simulation
panda dirc

## Slide 19
Barrel DIRC Baseline Design (BaBar-like)
expansion volume
Radiator bars
Photon detectors and electronics
Focusing optics
240cm
100cm
panda dirc

## Slide 20
Barrel DIRC Baseline Design (BaBar-like)
expansion volume
Radiator bars
Photon detectors and electronics
Focusing optics
240cm
100cm
panda dirc
Barrel:
  radius: 47.6 cm
  80 radiator bars,
Bars:
    1.7 cm × 3.2 cm × 240 cm
  synthetic fused silica
Expansion volume:
  30 cm depth
  mineral oil
Read out:
  ~15k channels of MCP-PMT

## Slide 21
Barrel DIRC Baseline Design (BaBar-like)
expansion volume
Radiator bars
Photon detectors and electronics
Focusing optics
240cm
100cm
panda dirc
Barrel:
  radius: 47.6 cm
  80 radiator bars,
Bars:
    1.7 cm × 3.2 cm × 240 cm
  synthetic fused silica
Expansion volume:
  30 cm depth
  mineral oil
Read out:
  ~15k channels of MCP-PMT
Expected
performance
  Single photon Cherenkov angle resolution: 10 mrad
  Number of detected photons for track: > 15

## Slide 22
Improvement of Expansion Volume
Instead of one common oil tank
panda dirc

## Slide 23
Improvement of Expansion Volume
Instead of one common oil tank
one synthetic fused silica prism per segment
Better optical properties
Smaller detection surface meaning fewer photon sensors
panda dirc

## Slide 24
Improvement of Expansion Volume
Instead of one common oil tank
one synthetic fused silica prism per segment
Better optical properties
Smaller detection surface meaning fewer photon sensors
30 cm
panda dirc

## Slide 25
Improvement of Radiator Width
Instead of 5 narrow bars per segment
panda dirc

## Slide 26
Improvement of Radiator Width
Instead of 5 narrow bars per segment
one wide plate
Fewer pieces to be polished
Less strict requirements for optical and mechanical quality of side surfaces
panda dirc

## Slide 27
Improvement of Radiator Width
Instead of 5 narrow bars per segment
one wide plate
Fewer pieces to be polished
Less strict requirements for optical and mechanical quality of side surfaces
panda dirc

## Slide 28
Improvement of the Optics
Removal of
  bar size contribution
    Focusing with mirrors or
    Lens-systems
  pixel size contribution
    Segmented Photosensors
    (MCP-PMTs)
panda dirc

## Slide 29
SiO2
LaK33
Improvement of the lens design
panda dirc
29
Lens design aimed for a focal plane
matching the flat photon detector plane
PbF2 is radiation hard, g ~ 100 kR
Other optical radiation resistant glasses?
Radiation level ~ 10 kR
Afternoon, Lee Allison

## Slide 30
Improvement of the lens design
panda dirc
30
Dispersing +
focusing lens
for flat focal plane
Geant
Zemax
Geant Zemax

## Slide 31
Improvement of photon sensors
panda dirc
Compact, fast multi-pixel sensor
  Single photon detection inside B-field with
  high gain 106 at 1-2 Tesla magnetic field
Good geometrical resolution over
a large surface
Very good time resolution of
~100 ps for single photons
High detection efficiency with
low dark count rate
High rate capability with
rates up to MHz/cm2
Long lifetime with
integrated anode charge of 0.5 C/cm2/y

## Slide 32
Simultaneous and continuous illumination
of all improved MCP PMT types
- >3 years of measurement up to now
Since 2011 life time of MCP PMTs enhanced by factor 20
panda dirc

## Slide 33
Improvement of the FEE
panda dirc
  Fast Front End Electronics for
    Time measurement
      read out chain
      σ Single Photo-Electron ~ 100 ps
      Reduction of background
  Charge determination
    Time over Threshold
    Walk correction

## Slide 34
FEE Concept
PAndaDIrcWAsa card
(PADIWA)
FPGA discriminator (reprogrammable)
Developed at GSI
Trigger and Readout Board v3 (TRB3)
Developed at GSI
4 FPGAs programmed as TDC
10 ps RMS time precision
67 MHz max hit rate
Time over Threshold measurement
MCP PMT
input
LVDS
output
panda dirc

## Slide 35
Barrel DIRC Prototype Tests
Modular configurations
Bar or plate with/without lenses
Radiators and lenses
Several bars/plates of different vendors
High-n cylindrical/spherical lenses
Wide range of beam-bar angles and positions
Readout
960 channels with PADIWA3 card and TRBv3 boards
Sensors
Photonis Planacon XP85012
Typical gain 106
Rise time 0.6 ns
at GSI & CERN T9 beamline
Radiators
test beam

## Slide 36
Barrel DIRC
Trigger1/Veto1
FLASH
TOF2
Disc DIRC
Fiber hodoscope
Trigger2/Veto2
TOF1
(20m upstream)
Barrel DIRC Prototype Tests
test beam
CERN T9 beamline

## Slide 37
Barrel DIRC Prototype Tests
test beam
CERN T9 beamline

## Slide 38
Barrel DIRC Prototype
Modular configuration
lateral displcament in x and y
change of angle remote controlled
test beam

## Slide 39
Read out plane
3 x 5 MCP PMT array (8 x 8 channels each)
Complicated hit patterns (reflections in prism)
test beam
8 x 8

## Slide 40
Occupancy plots
3 x 5 MCP PMT array (8 x 8 channels each)
Complicated hit patterns (reflections in prism)
test beam
Data from bar measurent @ 7 GeV/c, focussing

## Slide 41
Occupancy plots
3 x 5 MCP PMT array (8 x 8 channels each)
Complicated hit patterns (reflections in prism)
test beam
Data from bar measurement for different angles @ 7 GeV/c, focussing

## Slide 42
Time Resolution
test beam
Electronics (Calibration)
Picoquant laser (T0)
12ps
240ps
8,5ps
180ps
all channels
all channels

## Slide 43
Time Resolution
test beam
Data
best
worst
8
278ps
323ps
297ps

## Slide 44
Hit and event selection
No selection
Hit pattern for 3 component lens @ 7 GeV/c @ 50 degree
test beam
selection
Event selection
Time cut around trigger time
(scintillator in the beam)
Hit: selection
Masking noisy pixel
For each channel timing cut
(time offset calibration
with laser data)

## Slide 45
Time of Flight measurement
test beam
ToF1
ToF2
29m
Two fast MCP PMT counter
Pion/Proton separation up to 10GeV/c
7GeV/c

## Slide 46
Time of Flight: Walk correction
test beam
before after
184ps
142ps
7GeV/c
7GeV/c

## Slide 47
Hit Pattern Pions Protons @ 3 GeV/c
test beam
Pions
Protons
125 degree with 3-component lens

## Slide 48
Hit Pattern Pions Protons @ 7GeV/c
test beam
125 degree with 3-layer lens
Pions
Protons
π/K @ 3GeV/c
corresponds to
p/π @ 7GeV/c

## Slide 49
Photon Yield
test beam
Photon yield for 3-component lens @ 7 GeV/c
photon [#]
preliminary

## Slide 50
Single Photon Angular Resolution
test beam
3-component lens @ 7 GeV/c
example of
fit @ 60 degree
preliminary
12mrad

## Slide 51
Occupancy Plate Design
test beam
Data 2 component lens no lens
Simulation 2 component lens no lens
plate @ 55deg @ 7GeV

## Slide 52
Probability Density Functions
π
K
x
y
MC
Simulation
PMT map, with 5 x 3 sensors, 64 pixels each

## Slide 53
Probability Density Functions
Probability density functions (pdf) can be generated with ~100k Monte Carlo tracks with same parameters and saved in histograms.
22° polar angle
p = 3.5 GeV/c
π
K
In 3 dimensions (x, y, t) hit patterns show differences between particle species
π
K
PMT map, with 5 x 3 sensors, 64 pixels each
x
y
normalized PDF for a specific pixel
Inspired by Belle II TOP
MC
Simulation

## Slide 54
Probability Density Functions
Probability density functions (pdf) can be generated with ~100k Monte Carlo tracks with same parameters and saved in histograms.
22° polar angle
p = 3.5 GeV/c
π
K
In 3 dimensions (x, y, t) hit patterns show differences between particle species
π
K
PMT map, with 5 x 3 sensors, 64 pixels each
x
y
normalized PDF for a specific pixel
π sample
K sample
Inspired by Belle II TOP
MC
Simulation
Likelihood ratio test lnLK-lnLP

## Slide 55
Reconstruction with Probability Density Functions
In simulation this method works over the full phase space

## Slide 56
Plate: Time distribution of a single pixel
Leading edge time for pions (light particles) and protons
DATA measured without lens @ 7GeV/c @ 55 degree

## Slide 57
Outlook
  Early 2016: Decision about technology (plate vs. bar / prism vs. oil tank).
  Summer 2016: TDR
  Summer 2017 component construction
  2020 ready for beam
Sumary
  Baseline design of the Barrel DIRC with narrow bars and high-refractive lens index
  meets PANDA PID goals.
  Cost optimization identified two design alternatives (wide plate, solid fused silica prism)
  Prototype tests show promising results
      Number of observed photons
      Single photon angular resolution
  Plate still needs reconstruction
Sumary and Outlook

## Slide 58
PANDA Cherenkov Group
GSI Darmstadt, JINR Dubna, Goethe University Frankfurt, University of Erlangen-Nuremberg, JLU Giessen, University of Glasgow, HIM Mainz, JGU Mainz, Novosibirsk, SMI Vienna
THANK
YOU

## Slide 59
Back Up

## Slide 60
Ionization and acceleration
of residual gas atoms
Different countermeasures of manufacturors
  Al2O3 film to stop backflow of ions
  Improvement of vacuum
  Ultra-thin Atomic Layer Deposition
ALD
Ionbackflow causes rapid aging of photo cathode
  MCP PMTs would not survive more
  than 3 month of PANDA
panda dirc

## Slide 61
T9 2015 TESTBEAM DATA
Many different configurations tested, most of them with detailed angle and/or momentum scans.
Run 1 – May 2015
Barrel DIRC Prototype

## Slide 62
Cherenkov Angle Resolution
concept