## Slide 1: Neutrinoless double beta decay searches: gearing up for the tonne-scale era
Lior Arazi
Ben-Gurion University, Israel
INSTR20 conference
Budker Institute of Nuclear Physics and Novosibirsk State University, Novosibirsk, Russia 24 - 28 February, 2020

## Slide 2: Neutrinoless double beta decay
SM double beta decay :
BSM neutrinoless double beta decay :
: violates lepton number by 2 units, neutrinos must be Majorana
Observed, ,
Unobserved, ,

## Slide 3: vs.
counts
Total electron kinetic energy
can only occur in nuclei with , with relative rate
Q-value shared among 4 particles
Q-value shared among 2 e-

## Slide 4: The Majorana neutrino challenge
Lifetime ~1027-1028 years. 1 signal event in a tonne of active volume per year
Lifetime ~1030 years. 1 signal event in 100 tonne of active volume per year
15 meV

## Slide 5: Backgrounds
Natural radioactivity
leakage into the ROI
Cosmogenic activation
Neutrinos
Background suppression requires excellent energy resolution + additional handles

## Slide 6: searches
Germanium detectors
Bolometers
Loaded liquid scintillators
Liquid xenon TPCs
High-pressure gaseous xenon TPCs
(Others)
All experiments give “forward-looking” MC-based predictions about their tonne-scale expected performance

## Slide 7: Germanium detectors
Majorana, GERDA, LEGEND

## Slide 8
HPGe detectors enriched in >85% 76Ge
Superb energy resolution (0.13% FWHM at )
Diode geometry optimized for PSD
High purity and radio-purity
High detection efficiency
Ge diodes for in 76Ge

## Slide 9
Background suppression
Event topology + anti-coincidence between HPGe detectors + pulse shape discrimination + liquid argon veto
Event topology
Differentiate point-like ββ topology from:
Detector
anti-coincidence
multi-detector interactions
Pulse shape discrimination
multi-site / surface interactions
Detector-LAr anti coincidence
interactions with coincident energy deposition in LAr

## Slide 10
Continues taking data
Existing and future Ge experiments
+

## Slide 11
Bare crystals
GERDA

## Slide 12
LAr used for shielding, cooling + veto
GERDA

## Slide 13
GERDA

## Slide 14
GERDA results
Background index = counts/(keV kg y) at - practically background free!
Science 365 (2019) 1445

## Slide 15
200 kg HPGe in existing (upgraded) infrastructure at LNGS
Ge detectors from Majorana and GERDA + new inverted coaxial detectors (larger mass)
Background reduction: factor 5 compared to GERDA (reduce 42K, 214Bi, 208Tl)
Discovery sensitivity (10 y):
(inside the IO band)
LEGEND-200
arXiv:1709.01980

## Slide 16
LEGEND-1t baseline design
4 LEGEND-200 payloads
LEGEND-1t
Discovery sensitivity (10 y):- cover IO band
challenging

## Slide 17: Bolometers
CUORE, CUPID, AMoRE

## Slide 18
absorber + thermometer @ 10-20 mK
Detects particle energy in the form of heat
Key features for
High energy resolution (few keV)
Versatility in the choice of materials
What is a bolometer?

## Slide 19
CUORE: in 130Te
ΔE/E~8.7 keV FWHM (0.34%)
988 natTeO2 (34% 130Te) crystals @ 10-15 mK @ LNGS
“The coldest cubic meter in the universe”
60Co
Sum peak
arXiv:1912.10966

## Slide 20
CUORE
Background dominated by α particles, 1.38 × 10-2 c/(keV∙kg∙yr)
External γ background 10-3 c/(keV∙kg∙yr)

## Slide 21
Same as a bolometer + detector for scintillation
Particle ID by light/heat ratio  rejection of α particles
Reduction of α background: scintillating bolometers

## Slide 22
Reduction of γ background: isotopes with large
Isotope | abundance
116Cd | 7.5%
82Se | 9.2%
100Mo | 9.6%
96Zr | 2.8%
150Nd | 5.6%
48Ca | 0.19%
E [keV]
End point of 232Th γ radioactivity 2615 keV
End point of 238U β radioactivity 3270 keV
Expensive enrichment
Preferred

## Slide 23
CUPID: CUORE Upgrade with Particle IDentification
Scintillating bolometers with 100Mo,
Crystals: Li2100MoO4
Sensors (baseline): neutron-transmutation-doped (NTD) germanium thermistors, for both heat and light
Current status: CUPID-Mo, 20 crystal demonstrator taking data (LSM, France)
 210Po
 /
/() separation ~15
Preliminary
ΔE=5 keV FWHM, high radiopurity
arXiv:1907.09376

## Slide 24
CUPID: proposed plan
Install 1534 Li2100MoO4 crystals in the CUORE cryostat (250 kg 100Mo, >95% enrichment)
Expected background index: b  10-4 counts/(keV kg yr)
Expected sensitivity after 10 years: (– enough to cover the IO band)
Future potential:
“CUPID-1T”, after 10 years, requires a new cryostat and 20-fold improvement in background
arXiv:1907.09376

## Slide 25
AMoRE: Advanced Mo-based Rare process Experiment
~10keV FWHM
β/γ
α
L/H ratio
PSD
Fast rise-time
β/γ
α
40Ca100MoO4 (X100MoO4) + Metallic Magnetic Calorimeters (MMC)
MMC: superconducting sensor with fast response time (~200 µs)
Main advantage: better rejection of pileup (considerable background in large 100Mo crystals)

## Slide 26
AMoRE-I
2020
~1.5x10-3 ckky T1/2: 1025 y
13 48depCa100MoO4 crystals + 5 Li2100MoO4, ~3 kg 100Mo
AMoRE-II
Phased 2022-2024, fully funded
~10-4 ckky
T1/2: 5x1026 y, m: 17-29 meV
Favored Li2100MoO4, ~100 kg 100Mo
Yemilab (new), Korea
AMoRE-Pilot
Completed
Six 48depCa100MoO4 crystals, ~1 kg 100Mo
MMC proof of principle
EPJC 79 (2019) 791
Y2L, Korea

## Slide 27: Loaded liquid scintillators
KamLAND-Zen, SNO+

## Slide 28: KamLAND-Zen: in 136Xe
KamLAND neutrino detector + inner balloon, filled with liquid scintillator loaded with Xe (91% 136Xe) at 3 wt%, ~25 tonnes total
1879 PMTs (17”, 20”), photo-coverage 34%
Inner balloon: 25 µm-thick nylon film
Event location determined by photon time-of-arrival pattern (7.7 cm rms at Qββ)
E-res: 11% FWHM  major background

## Slide 29
KamLAND-Zen series
Published (90% C.L.):
PRL 117, 082503 (2016)
PAST
Expected sensitivity 5y:
ONGOING
Expected sensitivity 5y:
FUTURE

## Slide 30
E-resolution: 11% FWHM
Main backgrounds in ROI: (47%), 214Bi (23%), Spallation products (30%)
PRL 117, 082503 (2016)
Strongest limit to date:
KamLAND-Zen series

## Slide 31
238U and 232Th background reduction by factor ~10
TAUP 2019
Towards in 5 years (28-76 meV)
KamLAND-Zen 800 first results (132.7 live days)

## Slide 32
Add Winston cones for all PMTs (×1.8 increased light collection)
Replace PMTs (current QE~22%  >30%)
Replace LS (8,000 photons/MeV  12,000 photons/MeV)
Expected increase in energy resolution 11%  < 6% FWHM
~1000 kg 136Xe
Expected sensitivity in 5 years (14-38 meV)
KamLAND2-Zen (future)
ICISE Vietnam 2019

## Slide 33
Successor of the SNO experiment at SNOLAB, Canada
Primary goal: in 130Te ()
Secondary goals: measurements of solar, reactor and geo neutrinos + nucleon decay
SNO+: in 130Te
Most photogenic detector in the field

## Slide 34
Acrylic vessel
6 m radius, 10 cm thick
~780 t of LABPPO scintillator + ~4 t of natural tellurium (34% 130Te)
Inner water shield (~1700 t)
~9300 PMTs, 53% optical coverage, on St.St. support
Outer shield: cavity in rock ~5400 t ultrapure water
Electronics and DAQ
Holding ropes
~2 km depth, ~6 km.w.e.,
~3 muons/hour

## Slide 36
Expected energy resolution with 0.5% Te: 7.5% FWHM (188 keV)
Expected energy distribution
with nominal backgrounds
SNO+ expected performance
arXiv:1809.05986

## Slide 37
90% confidence limit after 5 years with 0.5% tellurium (6.8 tonne-year exposure): ()
SNO+ expected sensitivity

## Slide 38
Phase II (4% Te + increased light yield):
SNO+ future sensitivity

## Slide 39: Liquid xenon TPCs
nEXO (EXO-200), DARWIN

## Slide 40
nEXO: LXe TPC for in 136Xe
Builds on experience gained in EXO-200 (110 kg LXe active mass, )
Single-phase LXe TPC: 1.16 m inner diameter, 1.25 m drift height (single drift direction)
5.1 t LXe (90% 136Xe) in total (4.0 in the TPC)
Charge readout by induced current on charge collection tiles (top)
Light readout by SiPM tiles (4.5 m2 total) on barrel behind the field cage
EXO-200 mounted in cryostat
e- drift direction
arXiv:1710.05075, 1805.11142

## Slide 41
nEXO – background suppression
2.5 MeV γ attenuation length 8.5 cm – take data away from wall
Double-beta events are mostly single-site, while γs Compton-scatter  resolve multi-site events in space and time
Optimize energy resolution (EXO-200 achieved 2.7% FWHM, expect 2.5% FWHM in nEXO)
Cosmogenic production of 137Xe by muon-induced neutron capture in 136Xe (137Xe beta decays with Q=4173 keV)  deep underground lab + active veto
214Bi decays inside LXe active volume (from 222Rn) tagged by subsequent 214Po α decay
Use entire active volume to establish background model
Background index < 10-3 counts/(kev kg y)
Parallel R&D on barium tagging – currently not the baseline option

## Slide 42
nEXO – expected sensitivity
Similar half-life sensitivity as LEGEND-1000, but better mass sensitivity because of Xe’s larger phase space factor

## Slide 43
DARWIN
Two-phase TPC: 2.6 m diameter, 2.6 m height
50 t LXe in total (40 in the TPC)
Primary goal: WIMP search down to the “neutrino floor”
Secondary goal: in 136Xe
If natural Xe: 3.5 ton 136Xe in the TPC!
XENON1T E-res 1.9% FWHM  same expected in DARWIN

## Slide 44
DARWIN: expected background and sensitivity
TAUP 2019
Discovery sensitivity (10 y): - cover IO band
(Significant improvement possible in deeper site than LNGS and enhanced radiopurity)
preliminary
Sensitivity sweep through different fiducial masses

## Slide 45: High-pressure gaseous xenon TPCs
NEXT, PandaX-III, AXEL

## Slide 46
NEXT: High-pressure Xe gas TPC - in 136Xe
Working in high-pressure (10-15 bar) gas rather than liquid allows:
Excellent energy resolution by proportional electroluminescence (demonstrated 1% FWHM at Qββ , aim at 0.5%)
1.1% FWHM at 1.6 MeV
 1.0% FWHM at Qββ
Reconstruction of track topology to discriminate between background and signal
2 blobs
1 blob

## Slide 47
NEXT: Mode of operation
S1 (PMTs) gives
-30kV
-8kV
S2 magnitude by proportional EL (PMTs) gives the event energy
S2 time-slice images (SiPMs) give the event topology
Primary scintillation (S1)
e-
EL (S2)
G

## Slide 48
NEXT-White (now)
Running with enriched Xe since Feb 2019
TPC inner diameter 45 cm, drift length 53 cm, 5 kg fiducial mass at 15 bar

## Slide 49
NEXT-White: events in data

## Slide 50
Sensor response
Deconvolution
XY
XZ
YZ
2.19 MeV
NEXT-White: events in data

## Slide 51
NEXT-100 (assembly in 2020)
Pressure vessel: St-St, rated for 15 bar
TPC: 97 kg active region, 130 cm drift length
Energy plane: 60 radio-pure PMTs, 30% coverage
Inner shield: 12 cm Cu
Outer shield: lead castle with Rn-free air
Tracking plane: 5600 SiPMs at 1 cm pitch
Main goal: technology demonstrator on the 100 kg scale
Expected background index counts/(keV kg y)

## Slide 52
NEXT-HD (future)
1000 kg enriched Xe
Bi-directional symmetric TPC
Tracking + energy by radiopure SiPMs
Operated at low temperature (to reduce SiPM dark count rate)
Low-diffusion gas mixture (e.g., Xe/He 85/15) to further improve topology
Expected sensitivity after 10 years:
arXiv:1906.01743

## Slide 53
The aggressive approach: NEXT-BOLD
Tagging the barium daughter in a candidate event can lead to a background-free experiment

## Slide 54
Single Molecule Fluorescent Imaging comes back to physics!

## Slide 55
SMFI barium tagging in NEXT
Coat cathode plane with chelating molecules that selectively catch barium ions (not Xe).
The molecules are non fluorescent in isolation and become fluorescent upon chelation (or alternatively – change fluorescence color when containing barium).
Following a trigger on the event energy, scan cathode with a laser. A single molecule holding Ba appears as a bright spot.
Bicolor molecule developed at DIPC/EHU by the F. Cossio group
arXiv:1909.02782

## Slide 56
SMFI barium tagging in NEXT
Development at UTA based on monocolor molecules: on/off
Enhanced fluorescence when “on”
Development at DIPC based on bicolor molecules (FBI)
Enhanced fluorescence and spectral separation

## Slide 57
NEXT-BOLD sensitivity

## Slide 58
PandaX-III: High-pressure Xe gas TPC - in 136Xe
  Multi-module approach (each ~100 kg) in CJPL China
  Xe-TMA – favor topology over energy resolution
  Readout by mosaic of bulk MicroMegas
  First 100 kg module to be commissioned in 2020
AXEL High-pressure Xe gas TPC - in 136Xe
  EL in perforated PTFE structure, with SiPM readout for individual holes
  Now operating a 4.5 kg Xe prototype with 168 channels
  To be followed by a 40 kg module
Additional projects (details in backup slides)
PTFE w/ holes
Anode
GND mesh
SiPM array

## Slide 59
SuperNEMO - in multi isotopes
  Successor of NEMO-3
  Isotope contained in a thin foil, with the outgoing electrons passing through a gas tracker and a calorimeter
  Ideal for characterizing the mechanism once a discovery is made by other experiments
COBRA
  Array of CdZnTe crystals, containing five and four isotopes, including 116Cd and 130Tl
  Crystals serve as both source and detector
  Background suppression by multi-crystal hits and PSD
  Room temperature operation with ~35 keV FHWM
  Two demonstrators with different crystal sizes taking data at LNGS (total masses 300 and 400 g).
Additional projects (details in backup slides)
PRC 94, 024603 (2016), NIM A 807 (2016) 114

## Slide 60
Summary
The importance of detection justifies a multi-isotope approach
Several major players, but funding for the tonne-scale is still uncertain
Tonne-scale experiments will require many tens of M€, clearly not all will make it
GERDA and Majorana demonstrated a successful merger. Can this model apply to others?
Normal-ordering appears favored by oscillation experiments, but other effects beyond light Majorana neutrinos exchange may contribute to
quenching lurks in the dark, but advanced nuclear matrix element calculations may save the day

## Slide 62: Backup slides

## Slide 63
PandaX-III: High-pressure Xe gas TPC - in 136Xe
TPC: 100 kg scale high pressure TPC with charge readout
Main design features: good energy resolution and tracking capability
Traditional cuts and neural network topological studies (arXiv:1903.03979 ;1802.03489)

## Slide 64
PandaX-III: readout plane
Microbulk MicroMegas films made of Copper and Kapton only
  Perfect for radio-purity purpose
  20 by 20 cm
  3 mm pitch size, 128 strip readouts
Mosaic layout to cover readout planes
2

## Slide 65
PandaX-III: status and sensitivity
A 20-kg scale prototype TPC is running (arXiv:1804.02863)
1st 100-kg scale module to commission in 2020
Half-life sensitivity with 3 years of data: 9×1025 yr (90% CL)

## Slide 66
AXEL: High-pressure Xe gas TPC - in 136Xe
AXEL: A Xenon ElectroLuminescence detector to search for neutrinoless double-beta decay

## Slide 67
AXEL road map

## Slide 68
AXEL: 180L phase 1

## Slide 69
AXEL: 180L phase 1 performance

## Slide 70
SuperNEMO: overview

## Slide 71
SuperNEMO: the tracker-calorimeter technique

## Slide 72
SuperNEMO: demonstrator

## Slide 73
SuperNEMO: future directions

## Slide 74: Largest source of uncertainty: the size of axial coupling
for weak interaction and decays of nucleons
Quenching effects inside the nucleus may considerably reduce
Conservatively one should consider several options:
The degree of quenching is unknown. The expression for is based on half-lives and may be different for

## Slide 75: Effect of uncertainty in
For 136Xe taking pushes up the limit on by a factor of
KamLand-Zen + EXO-200 2015 data