## Slide 1
Using of Epics Channel Access protocol in Novosibirsk FEL control system
Serednyakov S.S.
BINP SB RAS, Novosibirsk, Russia
Abstract
The Free Electron Laser(FEL) based on multi-turn microtron-recuperator is currently operated at Novosibirsk. For successful operation of facility, the specialized control system is developed. The software part of this system consists of set of different program modules. For ensuring program connection between client and server part of control software, protocol Channel Access from EPICS framework was used. The features and examples of using of this protocol without using of whole EPICS system are described in this article.
2. FEL Subsystems Control Hardware Table
3. FEL Control System Software Architecture
Subsystem | Interface | Control devices | Control channels | Diagnostics channels
Electron GUN | CAMAC, CANbus | 7 | 10 | 10
RF-system | CAMAC | 28 | 50 | 200
Magnetic system | CANbus | 61 | 400 | 800
Beam diagnostic system | CAMAC | 75 | 0 | 280
“Technological” parameters control system | CANbus | 16 | 20 | 330
Optical system | CANbus, RS-485 | 10 | 10 | 20
Total | - | 164 | 490 | 1640
4. Usage of Channel Access Library
Software Components:
EPICS(Experimental Physics and Industrial Control System) – set of software tools developed to create software of distributed control systems of large scientific facilities
Channel Access – Epics component, responsible for connection and data transfer between client and server parts of control software
CAS(Channel Access server) – server part of Channel Access protocol
CAC(Channel Access client) – client part of Channel Access protocol
CA Server library classes and structures :
CaServer – used to create main server object, containing all PV objects
CasPV – used to create PV object, responsible for all client requests(read,write)
pvInfo – used to create PV object, storing all PV parameters(Name,Value, Units ..)
CA Client main calls :
ca_search – search and connect to specified PV by its name, return channel ID
ca_put(ca_put_callback) – write new value to specified PV by its ID
ca_get(ca_array_get) - read and return value from PV using specified ID
5. Client Applications, using Channel Access protocol :
5.1 CA Archiver - standalone application from EPICS extension set, intended for store of PV values in real time with specified period
1. The main functions of control of FEL subsystems:
Electron GUN – the realization of control over cathode-mesh unit – specifying of heat, cathode, acceleration voltage. Specifying the bunch repetition rate. Real-time diagnostics of beam losses in vacuum chamber.
RF system - The control over RF-generators. Control and diagnostics of all 19 RF resonators.
Magnetic system – The control over power supplies, diagnostics of their state as well – investigating of output current ripples and time stability
Beam position monitoring system - Real-time measurement and output of beam position coordinates. Accordance of tools for investigation of time stability of electron beam position and average current.
Technological parameters monitoring system - Readout and output of values from temperature, vacuum and water sensors. Prohibition of electron gun switching on, if value of one of the temperature sensors exceeds allowed maximum
FEL Radiation control system – Positioning of mirrors of optical resonator, monitoring of radiation power and wavelength, using different radiation sensors and monochromator. Transfer of the measured radiation values to other computers in FEL control LAN, and users stations computers as well.
Plots of history of some FEL parameters, stored by CA Archiver
5.2 Beam Alignment аpplication - used to electron beam move to the center of specified quadrupole lens, using control of specified magnet elements and data from specified BPM station.
5.3 CA RealTime Plot – Windows application. Outputs plots of values of specified PVs in real-time( as StripTool)
5.4 FEL radiation wavelength tune application
Executes step-by-step modification of undulator current to its required value, with simultaneous tracking of electron beam losses. If beam losses value exceeds allowed maximum value, the special tuning magnetic elements loop is switched on, to minimise these losses