## Slide 1
Toward the next generation of high-peak-power lasers:
compression after compressor approach
V.N. Ginzburg, I.V. Yakovlev, A.S. Zuev, A.P. Korobeinikova, A.A. Kochetkov,
A.A. Kuz’min, S.Yu. Mironov, A.A. Shaykin, I.A. Shaykin, E.A. Khazanov
Institute of Applied physics of Russian Academy of Science
Motivation
Compression after Compressor Approach (CafCA)
  Small-scale self-focusing suppression in powerful laser beams
Experimental results
Conclusions

## Slide 2
t
S(ω)
ω
ω
ω
ω
ω
ω
S(ω)
S(ω)
S(ω)
S(ω)
S(ω)
I(t)
I(t)
I(t)
I(t)
I(t)
φ(ω)
φ(ω)
φ(ω)
φ(ω)
φ(ω)
φ(ω)
t
t
t
t
S
A
C
NE
I(t)
t
I
a
I
g
I
m
CPA
б
I
g
DM
DM
S – stretcher,
A – laser amplifier,
C – compressor,
NE – nonlinear element,
DM – dispersion mirror;
Ia , Ig – breakdown threshold of the amplifiers, diffractions gratings.
Chirped Pulse Amplification

## Slide 3
energy
pulse duration
amplifier
damage threshold
grating
damage threshold
New idea is wanted for the next jump

## Slide 4: Compression after Compressor Approach
CafCA
FTL pulse
chirped pulse
Self-phase modulation
FTL pulse
ω
ω
S(ω)
I(t)
φ(ω)
t
S(ω)
φ(ω)
I(t)
t
ω
S(ω)
I(t)
φ(ω)
Ig
CafCA
nonlinear
element
chirped
mirror
Ig
Im
chirped
mirror
Compression after Compressor Approach

## Slide 5
S – stretcher,
A – laser amplifier
C – compressor
NE – nonlinear element
CM – chirped mirror
Ia , Ig and Im– breakdown threshold of the amplifiers, diffractions gratings and chirping mirrors.
t
S(ω)
ω
ω
ω
ω
ω
ω
S(ω)
S(ω)
S(ω)
S(ω)
S(ω)
I(t)
I(t)
I(t)
I(t)
I(t)
φ(ω)
φ(ω)
φ(ω)
φ(ω)
φ(ω)
φ(ω)
t
t
t
t
S
A
C
NE
I(t)
t
I
a
I
g
I
m
CPA
CafCA
I
g
CM
CM
CPA + CafCA

## Slide 6
Motivation
Compression after Compressor Approach (CafCA)
  Small-scale self-focusing suppression in powerful laser beams
Experimental results
Conclusions

## Slide 7
B=n2IkL=L/Lnonlinear
D=k2L(τpulse)2=L/Ldispersion<<1
a=E(t,z)/E(0,0) : electric field
Z=z/L : normalized distance
η=(t-z/u)/τpulse, : normalized time
τpulse : pulse duration
Fspectra= 1+0.9B(1-1.5D1/2)
Fpulse = 1+0.6B(1-1.25D1/2)
Fpower = 1+0.5B(1-1.2D1/2)
nonlinear
element
z
z=0
z=L
CafCA theory basics

## Slide 8
Fspectra = 1+0.9B(1-1.5D1/2)
Fpulse duration = 1+0.6B(1-1.25D1/2)
Fpower = 1+0.5B(1-1.2D1/2)
Fpower ≈ 1+B/2
D=0
D=0.02
D=0.05
D=0
D=0.02
D=0.05
D=0
D=0.02
D=0.05
Fspectra
Fpulse
Fpower
CafCA theory basics

## Slide 9: CafCA hystory from nJ to mJ
nJ
mJ
Fisher, R.A., Kelley, P.L., and Gustajson, T.K., "Subpicosecond pulse generation using the optical Kerr effect " Applied Physics Letters 14(4), 140-143, 1969.
idea
Laubereau, A., "External frequency modulation and compression of picosecond pulses," Physical Letters 29A(9), 539-540, 1969.
liquid
Nakatsuka, H., Grischkowsky, D., and Balant, A.C., "Nonlinear Picosecond-Pulse Propagation- through Optical Fibers arith Positive Group Velocity Dispersion," Physical Review Letters 47(13), 910-913, 1981.
fiber
Rolland, C. and Corkum, P.B., "Compression of high-power optical pulses," Journal of the Optical Society of America B 5(3), 641-647, 1988.
focused beam
Nisoli, M., Silvestri, S.D., and Svelto, O., "Generation of high energy 10 fs pulses by a new pulse compression technique," Applied Physics Letters 68(20), 2793-2795, 1996.
hollow core fiber

## Slide 10: CafCA hystory from nJ to J
CafCA hystory from nJ to J

## Slide 11: CafCA hystory from nJ to J
CafCA hystory from nJ to J

## Slide 12
Motivation
Compression after Compressor Approach (CafCA)
  Small-scale self-focusing suppression in powerful laser beams
Experimental results
Conclusions

## Slide 13
Physical problems : Solutions:
small-scale self-focusing free space beam filtering
non flat-top beam shape negative lens
Technological problem: Solutions:
very high aspect ratio 1:100+ plastic instead of glass
Power scaling
B=n2IkL
CafCA scaling problems and solutions

## Slide 14
θ=k/k
knoise
knoise
L, n2
k
z
V.I. Bespalov and V.I. Talanov, "Filamentary structure of light beams in nonlinear liquids," JETP Letters, 3, 307-310 (1966).
B=n2IkL
Instability if
Small-scale self-focusing basics

## Slide 15
Kmax=exp(2B)/2
K(θ=0)=1+4B2
B=n2IkL
Rozanov, N.N. and Smirnov, V.A., "Small-scale self-focusing of laser radiation in amplifier systems," Soviet Journal of Quantum Electronics 10, 232-, 1980
Small-scale self-focusing basics

## Slide 16
Fpower<2…2.5
B<2…3
Fpower≈1+B/2
Small-scale self-focusing basics

## Slide 17: Small-scale self-focusing suppression
For ns laser beams intensities I ~ 1÷10GW/cm2 θmax=0.73÷2 mrad
The technique of beam filtering depends on the intensity level
d
F
F
D
Vacuum spatial filters
F>>D
How laser beam can be filtered at the intensity ~ 1TW/cm2?

## Slide 18
For ns laser beams intensities I ~ 1÷10GW/cm2 θmax=0.73÷2 mrad
For fs laser beams intensities I ~ 1÷10TW/cm2 θmax=20÷50 mrad
The technique of beam filtering depends on the intensity level
Free space propagation leads to beam self-filtering
I=1TW/cm2, d=100mm: the safety distance D>1.6m
y
d
D
θ
θv
Beam self-filtering

## Slide 19
B-intergal
Distance from the mirror
100 shots were made in each point
S.Y. Mironov, V.V. Lozhkarev, V.N. Ginzburg, I.V. Yakovlev, G. Luchinin, A.A. Shaykin, E.A. Khazanov, A.A. Babin, E. Novikov, S. Fadeev, A.M. Sergeev, and G.A. Mourou,
IEEE Journal of Selected Topics in Quantum Electronics 18, 7-13 (2012).
Beam self-filtering

## Slide 20
Beam self-filtering may be used not only for CafCA but for any transparent optical element:
λ/2, λ/4 plates
polarizers
beam splitter
second harmonic generation
window
XPW generation
Beam self-filtering

## Slide 21
Motivation
Compression after Compressor Approach (CafCA)
  Small-scale self-focusing suppression in powerful laser beams
Experimental results
Conclusions

## Slide 22
Ø 20mm, W=20mJ, Tpulse=66fs -> 30fs, Lplastic=3mm, B~2
Spectra before and after SPM
ACF w/o SPM and
after SPM & chirped mirrors
ACF
ACF
43fs
30.5 fs
pulse
93fs
V. N. Ginzburg, A. A. Kochetkov, I. V. Yakovlev, S. Y. Mironov, A. A. Shaykin, E. A. Khazanov, Influence of the cubic spectral phase of high-power laser pulses on their self-phase modulation Quantum Electronics, 46, 106, 2016
CafCA in experiments
Example 1: at the output of the PEARL front-end

## Slide 23
Ø 100mm, W=6J, Tpulse=56fs -> 24fs, Lplastic=0.5mm, B~3
Spectra before and after SPM
ACF w/o SPM and
after SPM & chirped mirrors
ACF
ACF
24 fs
pulse
S.Y. Mironov, V.N. Ginzburg, I.V. Yakovlev, A.A. Kochetkov, A.A. Shaykin, E.A. Khazanov, and G.A. Mourou, Quantum Electronics 47, 614-619 (2017).
CafCA in experiments
Example 2: at the output of the PEARL

## Slide 24
CafCA in experiments
Ø 160mm, W=12J, Tpulse=63fs -> 21fs, Lglass=3 mm, B~6
V. N. Ginzburg, I. V. Yakovlev, A. S. Zuev, A. A. Korobeinikova, A. A. Kochetkov, A. A. Kuz'min, S. Y. Mironov, A. A. Shaykin, I. A. Shaykin, and A. E. Khazanov,
"Compression after compressor: threefold shortening of 200-TW laser pulses," Quantum Electronics, 49, 299, 2019.
time, fs
time, fs
wavelength, nm
Intensity, a.u.
ACF, a.u.
Intensity, a.u.
Example 3: at the output of the PEARL

## Slide 25
Ø 160mm, W=17J, Tpulse=70fs -> 14fs, Lglass=3 mm, B~7.5
Fresh new results
PRA, 101, 013829 2020

## Slide 26
Ø 160mm, W=17J, Tpulse=70fs -> 14fs, Lglass=3 mm, B~7.5
Fresh new results

## Slide 27
Ø 160mm, W=17J, Tpulse=70fs -> 14fs, Lglass=3 mm, B~7.5
Fresh new results
КЭ, 50,(4),331–334 (2020)

## Slide 28
ω
ω
S(ω)
I(t)
φ(ω)
t
S(ω)
φ(ω)
I(t)
t
any high power laser
1TW ... 10+PW
15fs … 1ps
mJs … kJs
1 m2… 1000+m2
100k$ ... 1G$
ω
S(ω)
I(t)
φ(ω)
Ig
CafCA
free
space
beam
self-
cleaning
glass
plate
self-
phase
modulation
Ig
Im
E.Khazanov, S. Mironov, and G.Mourou
"Nonlinear compression of high-power laser pulses: compression after compressor approach,” Phys. Usp., accepted, (2019)
Instead of conclusion
CafCA is simple, robust and cheap recipe:
just add free space, glass plate and chirp mirror(s)
chirped
mirror(s)
pulse
compression

## Slide 29
Thank you

## Slide 30: Conclusions
The peak power of present-day lasers is limited by the breakdown threshold of the optical compressor diffraction gratings.
The Compression AFter Compressor Approach (CafCA) is one of the most promising ways for overcoming this barrier.
The pulse spectrum is broadened thanks to the self-phase modulation in a medium with Kerr nonlinearity and then the pulse is compressed after reflection at dispersion mirrors.
CafCA possesses undoubted merits:
  simplicity and low cost
  negligibly small energy loss
  applicability to any high-power laser
Fivefold pulse shortening is demonstrated at 250 TW laser power

## Slide 31
PW laser
chirped
mirror(s)
Self-Phase Modulation (SPM)
B=n2IL
Defocusing lens for uniform SPM
S.Y. Mironov, V.V. Lozhkarev, E.A. Khazanov, and G. Mourou,
Quantum Electronics 43, 711-714 (2013).
S. Mironov, P. Lassonde, J.C. Kieffer, E. Khazanov, and G. Mourou,
European Physical Journal-Special Topics, 223, 1175-1180 (2014).
Lassonde, S. Mironov, S. Fourmaux, S. Payeur, E. Khazanov, A. Sergeev, J.-C. Kieffer, and G. Mourou,
Laser Physics Letters, 13, 075401 (2016).

## Slide 32
Defocusing lens for uniform SPM

## Slide 33
Ø 38mm, W=170mJ, Tpulse=33fs ->16fs, Llens=0.3mm, B~5, -220fs2
16 fs
pulse
Example 1: at ALLS, Canada, in defocussing lens
CafCA in experiments
P. Lassonde, S.Mironov, S.Fourmaux, S.Payeur, E.Khazanov, A.Sergeev, J.-C.Kieffer, G. Mourou, "High energy femtosecond pulse compression," Laser Physics Letters, 13, 075401, 2016.

## Slide 34
PW laser
chirped
mirror(s)
Self-Phase Modulation (SPM)
B=n2IL
Plastic – unlimited aperture and aspect ratio
G. Mourou, S. Mironov, E. Khazanov, and A. Sergeev,
European Physical Journal-Special Topics, 223, 1181-1188 (2014).

## Slide 35
Plastic (polyethylene terephthalate)
G. Mourou, S. Mironov, E. Khazanov, and A. Sergeev, "Single cycle thin film compressor opening the door to Zeptosecond-Exawatt physics,"
European Physical Journal-Special Topics, vol. 223 , 1181–1188, 2014.

## Slide 36
PW laser
chirped
mirror(s)
Self-Phase Modulation (SPM)
B=n2IL
Small-scale self-focusing suppression in powerful laser beams
S.Y. Mironov, V.V. Lozhkarev, V.N. Ginzburg, I.V. Yakovlev, G. Luchinin, A.A. Shaykin, E.A. Khazanov, A.A. Babin, E. Novikov, S. Fadeev, A.M. Sergeev, and G.A. Mourou,
IEEE Journal of Selected Topics in Quantum Electronics 18, 7-13 (2012).
S. Mironov, V. Lozhkarev, G. Luchinin, A. Shaykin, and E. Khazanov,
Applied Physics B, 113, 147-151 (2013).
V.N. Ginzburg, A.A. Kochetkov, A.K. Potemkin, E.A. Khazanov,
Quantum Electronics 48 (4) 325 – 331 (2018)

## Slide 37
W
z
Experimental Results
diameter/distance
Theoretical curves: logarithm of noise power.
Experimental points: black, gray and white circles correspond to high, small and zero transmission reduction due to optical damage

## Slide 38: CafCA in experiments
PW laser
chirped
mirror(s)
Self-Phase Modulation (SPM)
B=n2IL
S Yu Mironov, V N Ginzburg, E I Gacheva, D E Silin, A A Kochetkov, Yu A Mamaev, A A Shaykin, E A Khazanov, and G A Mourou
Laser Phys. Lett. 12, 025301 (2015)
V.N. Ginzburg, A.A. Kochetkov, I.V. Yakovlev, S.Y. Mironov, A.A. Shaykin, and E.A. Khazanov
Quantum Elrctronics, 46, 106-108 (2016).
P. Lassonde, S. Mironov, S. Fourmaux, S. Payeur, E. Khazanov, A. Sergeev, J.-C. Kieffer, and G. Mourou
Laser Physics Letters, 13, 075401 (2016).
S.Y. Mironov, V.N. Ginzburg, I.V. Yakovlev, A.A. Kochetkov, A.A. Shaykin, E.A. Khazanov, and G.A. Mourou,
Quantum Electronics 47, 614-619 (2017).

## Slide 39
а
б
в
г
CafCa
второй каскад CafCa
НЭ
НЭ
НЭ
НЭ
НЭ

## Slide 40
Example 4: at the output of the PEARL front-end
CafCA scaling problems and solutions

## Slide 41
E0(t)
S0(ω)
T
k﬩
NP
E0(t)e-iγ1│E0(t)│2
CM
1st stage CafCA
R=eiα1ω2
E1(t)
2nd stage CafCA
E1(t)
ω
E2(t)
t
R=eiα2ω2
t
t
t
t
t
ω
ω
ω
ω
ω
NP
BC
CM
S1(ω)
S1(ω)
S1(ω)
S1(ω)
S2(ω)
E1(t)e-iγ2│E1(t)│2
in
out 1
out 2
CafCA: double-stage