## Slide 1
Laser based source of electrons/ions for nuclear medicine and nuclear waste transmutation
A. V. Brantov, M. G. Lobok, O. E. Vais, S. G. Bochkarev, V. Yu. Bychenkov
P. N. Lebedev Physics Institute, Russian Academy of Science, Moscow, Russia
Center for Fundamental and Applied Research, VNIIA, ROSATOM, Moscow, Russia

## Slide 2: Outline/summary
Self-trapping regime of laser pulse propagation in sub-ctritical plasma is optimal for effective electron beam generation with multi-nC charge. Such beams opens a way to high-yield production of gammas and photonuclear particles.
4 J femtosecond laser with a repetition rate of 10 Hz, which is already commercially available can provide therapeutic amount of certain medical radioisotopes.
Low efficiency of transmutation in pure LLFP targets will require the next generation continuously operating high-repetition laser systems (MHz range rep-rate and tens of joules).
M G Lobok A V Brantov and V Yu Bychenkov
2022 Plasma Phys. Control. Fusion 64 054002

## Slide 3
Nuclear medicine
SPECT
PET
(Single Photon Emission Computed Tomography)
(Positron Emission Tomography)

## Slide 4
Medical cyclotrons
Clinical Nuclear Medicine ed H Ahmadzadehfar, H J Biersack, L Freeman and L Zuckier (Cham: Springer) 2020.

## Slide 5: Electron acceleration from low-density target
x
y
z
L = 10 - 200 
x y z = 58   25   25 
x  y  z = /50  /10  /10
2 
2 RL
Laser pulse
laser
target
electrons
heavy ions
Target
~4 J
81020 W/cm2
 = 30 fs
2 RL = 5 μm
linear polarization
converter
electron bunch
gamma-rays
PIC code
Vsim (Vorpal)
GEANT-4
Collect all electrons behind target with energy more than 1 MeV
Moving window

## Slide 6
Laser bullet acceleration regime
R (n, I) - matching
R
Propagation over  10 Rayleigh lengths
 - numeric factor ~ (1-2)
Stable propagation only for matched conditions !

## Slide 7
Electron acceleration from near-critical targets
Stochastic electron injection
Flat-top electron spectra
Modification of electron trajectories due to small electron momentum perturbations

## Slide 8
Electron acceleration from near-critical targets
Laser - electron beam conversion efficiency ~15 %
Te=97 MeV
Te=210 MeV
M. G. Lobok et al., Plasma Phys. Control. Fusion.Vol. 60. P. 084010 (2018)
V. Yu. Bychenkov et al., Plasma Phys. Control. Fusion. Vol. 61.P.124004 (2019)

## Slide 9: Photonuclear reaction
Main contribution from Giant resonance

## Slide 10: Laser-triggered gamma-ray source for nuclear reactions
Spectrum of electrons accelerated by a 135 TW laser
Corresponding gamma spectra for the Ta-converters
Electrons

## Slide 11: Medical isotopes production
The use of direct electron beam irradiation has the advantage of simplifying the photonuclear production of isotopes.
used in brachytherapy as a seed or a stent.
SPECT diagnostics – 99mTc
PET diagnostics – Cu isotopes
99Mo (66 hours ->) 99mTc
SPECT diagnostics – 111In, 123I

## Slide 12: Photo-nuclear production of medical isotopes
Therapeutic amounts of some medical radioisotopes can be produced with 4J 10 Hz laser system, while creating, e.g., (99Mo99mTc)-generator will require 100 Hz laser.
The same amount of 64Cu and 62Cu medical isotopes can be produced with the three times less in energy laser as reported earlier. The 99Mo isotope yield per one electron is comparable to that obtained at PW-class Bella laser system [i.e.∼ 2×10−3 atoms per electron].

## Slide 13: SPECT isotopes (99mTc) production
The era of nuclear reactors in the production of isotopes is over ???
The medical 99mTc isotope production through a particle
accelerators ?  100Mo(p,2n)99mTc
Production of 99mTc with cyclotrons is widely discussed
Protons with
energy of ~30 МэВ
↓
I~1021W/cm2

## Slide 14
Proton acceleration for Tc-99m production
V. Y. Bychenkov, A. V. Brantov, G. Mourou, Laser and Particle Beams (2014), 32, 605.
1
2
3
4
1
2
3
4

## Slide 15
The Tc-99m production versus irradiation condition and target thickness

## Slide 16
Laser triggered protons/deuterons acceleration from thin foil for medical PET isotope production
3 J, 30 fs
R=10 λ
3D PIC MANDOR
GEANT4
laser
laser
foil
deuterons
protons
reaction

## Slide 17
Spectra of protons accelerated from СН2 foil with thickness of 0.02 λ at instant of 386 fs
р-polarization
s-polarization
Spectra have exponential form ~ exp[-ε/Th] with “temperature” Th= 2.7 MeV and energy cut-off at 21 MeV -25 MeV.
Proton acceleration from thin foil (different incident angels)
Change of incident angle up to 10° has rather negligible effect on ion acceleration

## Slide 18
Normal incident
Incident under angle of 10°
2×1011 protons with energy in excess 1 MeV
Total bunch energy 110 mJ
Conversion efficiency 3.7%.
Proton acceleration from thin foil (different target thickness)

## Slide 19
Normal
incident
Oblique
incident at 10°
TNSA –like acceleration
Proton acceleration from thin foil (bunch directionality)

## Slide 20
Deuteron acceleration from thin foil
5.5×1010 deuterons with energy in excess of 1 MeV
full bunch energy ~ 30 mJ
conversion efficiency ~ 1%.
Relatively small total number of accelerated deuterons leads to small number of produced medical isotopes.

## Slide 21
Reaction | Isotope, τ1/2 | Atoms per shot | Activity 10 Hz | Irradiation time | Required activity
14N(p,α)11C | 11C, 20.4 min | 8×106 11C | 78 MBq | 2 h | 500 MBq
15N(p,n)15O | 15O, 2 min | 7×106 15O | 67 MBq | 10 min | 350 MBq
18O(p,n)18F | 18F, 110 min | 1.5×107 18F | 130 MBq | 5.5 h | 250 MBq
16O(p,α)13N | 13N, 10 min | 2.6×106 13N | 25 MBq | 45 min | 370 MBq
66Zn(p,n)66Ga | 66Ga, 8.5 h | 1.8×107 66Ga | 174 MBq | 40 h | 350 MBq
61Ni(p,n)61Cu | 61Сu, 3.3 h | 107 61Сu | 100 MBq | 19 h | 300 MBq
Laser triggered PET production
For medical dose production (~ 300 MBq) of PET isotopes laser system with energy of several J and repetition rate of 100 Hz is required
To reach activity comparable with cyclotrons (~ 100 GBq) the repetition rate should be ~ 10 kHz.

## Slide 22
Laser triggered protons/deuterons acceleration from near-critical targets for medical PET isotope production (fs laser pulse)
Laser pulse
nuclear target
laser target
with protons (deuterons)
5 J, 30 fs
R=4 λ, I=9×1020 W/cm2

## Slide 23
Spectral - angular distribution of proton accelerated from target with density of 2.0nс.
Transversal ion acceleration from near-critical target
Protons
Deuterons
ε, MeV
ε, MeV

## Slide 24
Maximum bunch charge (nC) of protons (red line) and deuterons (blue line) vs. target density
Transversal ion acceleration from near-critical target
> 1 MeV
> 3 MeV
15N(p,n)15O, 14N(d,n)15O for production β+ activity atoms 15O
18O(p,n)18F, 20Ne(d,α)18F
for production β+ activity atoms 18F
14N(p,α)11C for production β+ activity atoms 11С
Q , nC
Q , nC
.

## Slide 25
GEANT4 - calculation
Laser triggered PET production (5 J, 30 fs)
11C (activity ~ 500 MBq)
– 2 h, 2 kHz
18F (activity ~200 MBq )
– 100 h, 100 Hz
15O (activity~350 МБк)
- 10 min, 1 kHz
Atoms per shot
Atoms per shot
deuterons
protons
Required irradiation condition for medical dose production
Does not any improvement in comparison with thin foils

## Slide 26
proton from target with (ne =1.5nс)
Laser triggered protons acceleration from near-critical targets for medical PET isotope production (sub ps laser pulse)
E = 30 J,  = 1.055 µm ,  = 500 fs,
 = 10 µm, I = 5х1019 W/cm2

## Slide 27
Reaction | Isotope, τ1/2 | Atoms per one shot | Maximum activity (for Hz) | Repetition rate for med. dose
18O(p,n)18F | 18F, 110 min | 3.1×107 | 30.9 MBq | 5 Hz
15N(p,n)15O | 15O, 2 min | 1.3×107 | 13.1 MBq | 26 Hz
14N(p,α)11С | 11С, 20 min | 1.3×107 | 12.7 MBq | 40 Hz
In comparison with fs laser pulse
18F yield for 1 J of laser pulse increases 2 times
15O yield for 1 J of laser pulse increases 4 times
11C yield for 1 J of laser pulse increases 8.5 times
Irradiation time >> τ1/2 . Optimal concentration : ne = 2.5 ncr
Laser triggered PET production (30 J, 500 fs)

## Slide 28
E = 0.5 kJ,  = 1.055 µm,  = 2 ps,  = 10 µm, I = 2х1020 W/cm2
0 150мкм
3nc
nc
Laser triggered protons acceleration from near-critical targets for medical PET isotope production (2 ps laser pulse)
protons
deuterons
~3х1013

## Slide 29
Reaction | Isotope, τ1/2 | Atoms per one shot | Maximum activity (for 1 Hz) | Repetition rate for med. Dose
18O(p,n)18F | 18F, 110 min | 4.6×108 | 460 MBq | 0.4 Hz
natNe(d,x)18F | 18F, 110 min | 5.3×108 | 530 MBq | 0.4 Hz
15N(p,n)15O | 15O, 2 min | 1.8×108 | 180 MBq | 2 Hz
14N(d,n)15O | 15O, 2 min | 8.6×108 | 860 MBq | 0.4 Hz
14N(p,α)11С | 11С, 20 min | 1.7×108 | 170 MBq | 3 Hz
Isotope productions for 1 J are the same as in the case of sub-ps 30 J laser
Laser triggered PET production (0.5 kJ, 2 ps)
Irradiation time >> τ1/2 . Optimal concentration : ne = ncr

## Slide 30: Summary
Certain medical radioisotopes production is possible with 4 J femtosecond laser with a repetition rate of 10 Hz.
Laser -> electrons>gammas ->isotopes it seems more perspective than laser->protons->isotopes for production of high-Z radioisotopes.
Radial proton acceleration from near-critical targets for isotope generation are not effective for modern laser systems.

## Slide 31
Major long-lived nuclides in spent nuclear fuel

## Slide 32
Scheme of transmutation technology
Oigawa H 2015 JPS Conf. Proc. 6 010004

## Slide 33
Photo-nuclear nuclear waste transmutation
Composition of sludge
No effect of transmutation !
Distribution of gamma photons in the converter and sludge
Energy deposition of gammas in sludge

## Slide 34
Photo-nuclear nuclear waste transmutation

## Slide 35
Gamma based nuclear waste transmutation

## Slide 36
Yield of photonuclear reaction per one laser shot vs. target thickness
A cylindrical target with the radius of 0.5 cm and the length(3-5) cm is the best candidate for most effective transmutation
To reach noticeable reduction of overall activity (∼ 10%) the 10-years continues irradiation by laser produced gammas of 10 g LLFP by using 100 kHz laser system is required.

## Slide 37: Summary
Self-trapping regime of laser pulse propagation in sub-ctritical plasma is optimal for effective electron beam generation with multi-nC charge. Such beams opens a way to high-yield production of gammas and photonuclear particles.
The efficiency of photonuclear reactions is not inferior to the efficiency of ion-neutron reactions, despite the fact that photonuclear cross sections are smaller than typical nuclear cross sections due to the electromagnetic nature of the interaction.
4 J femtosecond laser with a repetition rate of 10 Hz, which is already commercially available can provide therapeutic amount of certain medical radioisotopes.
Low efficiency of transmutation in pure LLFP targets will require the next generation continuously operating high-repetition laser systems (MHz range rep-rate and tens of joules).