## Slide 1
Development of the DLA platform at the ARC/NIF
with PHELIX as a testbed
Разработка платформы DLA на ARC/NIF с использованием
PHELIX в качестве испытательного стенда
Olga Rosmej, Nikolay Andreev, Nataliya Borisenko
Mikhail Gyrdymov, Parysatis Tavana, Jakub Cikhardt,
PHELIX, and NIF -teams
Новые методы ускорения частиц и экстремальные состояния материи, 15.02.2024

## Slide 2: NIF Discovery Science project: Platform development.
Hui Chen, chen33@llnl.gov
Andreas Kemp, kemp7@llnl.gov
Shaun Kerr, kerr24@llnl.gov
Dean Rusby, rusby1@llnl.gov
Dieter Schneider, schneider2@llnl.gov
Scott Wilks, wilks1@llnl.gov
Expected impact and the need for NIF:
The development of the DLA platform at NIF promises a 10 -fold increase in the conversion efficiency from laser to MeV directional Bremsstrahlung (BS) compared to the application of the Compound Parabolic Concentrator (CPC).
Experimental approach:
Direct laser-accelerated electron generation in interaction of a 1ps/10 ps,
ARC pulse with pre-ionized low-density polymer foams (CHO, CH).
A nanosecond NIF beam is used to trigger supersonic ionization inside the foam, creating mm long NCD plasma .
Ultra-bright MeV photon sources driven by direct laser accelerated (DLA) electrons with ARC/NIF.
Supporting team:
Oral Presentation (web-conference) of top proposals (by invitation) on November 9th.

## Slide 3: NIF’s short pulse laser, the Advanced Radiographic Capability (ARC)
Largest amount of available short pulse energy in the world (up to 4 kJ)
but intensity remains quasi-relativistic (IL < =1018 W/cm2) -> low fraction of MeV particles and photons

## Slide 4: Need for broadband x-ray and gamma sources for HEDS

## Slide 5: Report of the Lawrence Livermore National Laboratory 2020
Self Modulated LWFA is a main platform to produce laser-driven sources of MeV particles and radiation.

## Slide 7: LWFA for X-rays and gamma-rays production

## Slide 8: LWFA-driven sources on large kJ-class ps lasers

## Slide 10
Results for 0.7 ps, ao= 6.6
ne=8x1018 cm-3, Φnozzle= 6 mm
Charge 700±420 nC
(≤700 kA current)
weighted average electron energy 17.9 MeV
(Alfven current ( g=40) = 700 kA)
OMEGA EP
SM-LWFA-based LPA
~ 50 cm
J. Shaw et al,
Sci. Reports 2021
50% charge in 0.1 rad
Ee > 0.9 MeV
MS IP after 37 mm Al
Ee > 0.02 MeV

## Slide 11: SM-LWFA at high electron densities show unstable for electron acceleration
(2021) 11:7498

## Slide 12
Direct laser acceleration (DLA) as an effective way toward ultra-bright sources of MeV particles and radiation at near-relativistic laser intensity and above.

## Slide 13: Direct laser acceleration of relativistic electrons at betatron resonance
A. Pukhov, Z.- M. Sheng, and J. Meyer-ter-Vehn, V6, N7, PoP 1999
self-focusing: laser peak power PL(500 TW) >> Pc=17 GW × nc / ne ~ 17 GW
ponderomotive force expels background plasma electrons from laser channel
generation of quasi-static radial E-field that has a pinching polarity for electrons.
self-generated quasi-static B azimuthal (≥100 MG) that traps electrons in the plasma channel
transversal betatron oscillations of electrons where they gain energy from laser field.
NCD > 100 × higher plasma density than for LWFA and SM-LWFA -> higher charge of super-ponderomotive electrons but with lower energies
X. F. Shen et al, Appl. Phys. Lett. 118, 134102 (2021);
3D PIC for PHELIX, 1019 W/cm2
Notes: All the more astonishing that DLA appears to be a very stable process

## Slide 14
Variety of foams for generation of long-scale NCD plasma
Stochastic 3D nano-network,
2 mg/cc-> 0.4 ncr
bundle thick. < 5-10 nm,
Uniform NCD after 400fs
sharp (0.4 µm) vacuum-plasma boundary
W Ma Nano Lett 2007
J H Bin PRL 2018
W.J. Ma PRL 2019
Y Shou NatPhot 2022
C-nano foams (CNF)
near-critical
pore size ~ 10 nm
Stochastic 3D micro-network,
2 mg/cc-> 0.65 ncr
bundle thick. ≥ 40 nm,
Uniform NCD: ps (1 keV) and some of ns (10 eV)
NG Borisenko, J. Phys. 2020
O Rosmej, PPCF 2015 2020
S Chaurasia, PoP 2017
CHO (TAC)
pore size ~ 1 mm
GSI
O. S. Jones
Polystyrol
pore size ~ 20 mm
O S Jones PoP 2021
P. Wang HPLS 2021
T. Wiste J. App. Phys.2023
pore size ≥10 mm
AM foams C8H9O3
over-critical
Additive manufacturing
Stochastic 3D micro-network,
closed pore, 20-30 µm,
3-4 µm thick walls.
Demands ns-time scale for
homogenization
NG Borisenko et al,
LPB26 (04) 2008
Regular 3D nano-network,
12-93 mg/cc,
bundle thick. ~ 0.1 - 1 mm,
Uniform after 70 ps (1.5 keV) and some of ns (100 eV)
super-critical plasma (green)

## Slide 15: Generation of NCD plasma in interaction of ns-laser pulse with foam
1013-10-14 W/cm2
CHO: 2 mg/cc (2×1020 at/cm3)
> 500 µm thick NCD plasma “target” (Ne ≲ 0.7 x 1021 cm-3 ) is created by a 1013-1014 W/cm2 ns pulse.
Ionization wave velocity ~ (1-2)x107 cm/s. Main pulse interacts with NCD plasma with a delay of 3-5 ns.
foam ionization is triggered by well-defined ns-pulse with parameters adjusted to the foam density and thickness
3D aerogel structure
sub mm thick foam provides increased interaction path
50-100 nm solid ( 0.1g/cc)+ ca. 1 mm evacuated pore
advantage of foam: it absorbs up to 90% laser energy
O. N. Rosmej et al, New J. Phys. 21(2019) 043044
O. N. Rosmej et al Plasma Phys. Control. Fusion 62 (2020) 115024

## Slide 16: Well-directed high-current beams of super-ponderomotive electrons (PHELIX)
electron angular distribution
shot on foil
laser
foam
foil
O. N. Rosmej et al, New J. Phys. 21(2019) 043044
O. N. Rosmej et al Plasma Phys. Control. Fusion 62 (2020) 115024
collimated e-beam
isotropic
Most fraction of electrons is accelerated
along laser axis; Emax = 100 MeV, T eff > 10 MeV
PHELIX: 1019 W/cm2, 1 mm,
0.7 ps, 20 J FWHM, a0= 3.5
> 3.5 MeV
> 3.5 MeV
½ =13°
shot on foam+foil
shot on foil

## Slide 17
1019 W/cm2
1021 W/cm2
O. N. Rosmej et al Plasma Phys. Control. Fusion 62 (2020) 115024
More high energy electrons ( > 30 MeV) in case of foam+foil at 1019 W/cm2 (red) than in shot with 1021 W/cm2 on foil (green)
100× increase of laser energy coupling to MeV electrons using foams
spectra measured along laser axis (0°)

## Slide 18
Foams are produced using different technologies:
CHO (N. Borisenko, LPI) PHELIX 2017-21
CH (General Atomics, US) PHELIX 2022-23
CHO (W. Nazarov, Scotland) PHELIX 2022-23
densities: near critical and over-critical 2-8 mg/cc
areal densities: 0.16-0.2 mg/cm2
ns pulse: ~ 1013 – 3x1014 W/cm2, 3- 5 ns delay
Th ~ 15-17 MeV
Al high contrast
Al + ns
foam + ns
Stability of the DLA process by appl. of different foams and ns-pulses
PhD M. Gyrdymov, GU-Frankfurt

## Slide 19: 10-times less 10 MeV photons in direct shot on W-converter with ns-pulse
sh. 37 Foam 4 mg/cc, 0.5mm + 2mm W +ns-pulse
sh. 41 Direct shot on 2mm W + ns-pulse
Cu-foil -27 mm from TCC
Cu-foil 40 mm from TCC
= 18
= 25
= 15-19
for convertor thickness 2-4 mm
(E>10 MeV)
Visualization of the gamma-rays angular distribution using autoradiography

## Slide 20: No DLA electrons were observed in interaction with foams w/o pre-ionization by ns-pulse
Ponderomotive electrons from foam and foil w/o ns-pulse
Al-foil, high contrast (10-11) shot
Polymer foam, high contrast shot
backward
and to the side
forward
accelerated
electrons
electron angular distribution
Teff=1.2 MeV
No difference in electron spectra for foil and foam at high laser contrast
M. Gyrdymov

## Slide 21: Ultra-bright betatron radiation produced by DLA electrons
X. F. Shen et al, Appl. Phys. Lett. 118, 134102 (2021), O. N. Rosmej et al, Matter Radiat. Extremes 6, 048401 (2021)
PETAL 1 kJ , SM-LWFA (a0= 7.5, ne= 1018 cm-3, Ee~ 1 GeV) 7×1011 photons with Ec = 10 keV,
Ferri et al, Phys,. Rev. Accelerators and Beams 19, 101301 (2016)
Broad spectrum, large photon number: 7×1011 (1-30 keV) with Ec = 5 keV,
3D PIC for PHELIX (a0=2.5)
X.F. Shen, A. Pukhov
Notes: by the electrons.
F is the transverse force felt by the electrons. ~ Ne
is the transverse force felt

## Slide 22: Modified magnetic spectrometer for X-rays (X-MS)
Mikhail Gyrdymov, Goethe University, Frankfurt, GSI

## Slide 23
experiment
Measurements of betatron radiation produced by DLA electrons (PHELIX 2021-22)
PhD, M. Gyrdymov
α1/2= 6° (Eph> 10 keV)
100 mrad
Cu-washer
Cu-washer
1010 (10-30 keV), div=100 msr -> fluence 3×1011 ph/sr
Brilliance: ≥ 2x1020 photons/s/mm2/mrad2/0.1%BW
Au-foil
Notes: protons and electrons can falsify signal

## Slide 24: Betatron from CHO-foam at 0.7 ps, 1019 W/cm2 vs. CNF at 20 fs, 1021 W/cm2
Nature Photonics 2022, Y. Shou, …W. Ma
CoReLS, Korea: Ti:Sa laser at 1021 W/cm2
Elas=20J, 20 fs, w=7 um
Carbon nano-foams 2 mg/cc, 80 um thickness
,
PHELIX at 1019 W/cm2, 0.7 ps, w=15 um
Elas (after comp.) =60J, WFHM=20 J
CHO (TAC) 2 mg/cc 400 um thickness
≥ photons/J 10-40 keV
CNF
pre-ionized CHO
simulations (X. Chen)
More about DLA-based betatron measurements on PHELIX by Mikhail Gyrdymov, PP seminar, on November 7th, 2023

## Slide 25
Nuclear Reactions for Investigation of MeV Bremsstrahlung
generated by DLA Electrons in high-Z Materials.
Record breaking conversion efficiency of 2% of directed BS in GDR
= 18

## Slide 26
experiment
Record breaking efficiency of generation of MeV bremsstrahlung in the GDR-range
1012/sr photons with E > 8 MeV, Teff = 13 MeV with divergence of 0.2 sr
Record conversion efficiency laser-BS of 2% (GDR) (Vulcan laser: 0.2%)
DLA-electrons propagate in high Z converter and generate BS with 10´s of MeV photon energy
= 18
laser
foam
Measured isotope yields (up to Au 192 (g, 5n) at 50 MeV)
(g, xn) photo nuclear reactions
DLA at 1019 W/cm2 vs 1021 W/cm2: 10 × higher photon number and twice higher Teff.
Au 192
Au-converter
E gamma=10-20 MeV

## Slide 27: Wide-range diagnostic of 0.1 MeV-100 MeV radiation
8-channel in vacuum TLD spectrometer at PHELIX
GEANT 4 simulation of the shot 30 (PHELIX 2022)
TLD Spectrometer
0.99T-MS
0.99T-MS
0.99T-MS

## Slide 28: Reconstructed BS spectrum: 8-channel TLD spectrometer and nuclear diagnostics
Teff = 16 MeV
1012/sr collimated gammas with 2% conv. efficiency of laser energy into BS > 8 MeV
Record breaking conversion efficiency compared to Vulcan, Nova (0.2% in GDR)

## Slide 29: Gamma-driven Isotope production at 1019 W/cm2: up to Au190 ( g,7n) with Epeak ~ 70 MeV
P. Tavana

## Slide 30: Efficient laser energy coupling in electrons using foam + converter at 1019 W/cm2
Crater in Ta-converter after PHELIX shot
Direct laser shot on Ta at high laser contrast
PHELIX: 1019 W/cm2 , 20 J (FWHM) 0.7 ps, focus=15 um
Nuclear diagnostic:
No Ta-isotopes
directed part of DLA beam
Nuclear diagnostic:
up to 175 Ta (g, 6n) at Eg > 48 MeV
After 1000 um 2 mg/cc, LPI (2021)
crater depth: 500 µm
1 mm
to laser
before and after shot

## Slide 31
DLA platform for generation of ultra-bright sources
of MeV particles and radiation
M. M. Günther, O.N. Rosmej, P. Tavana, M. Gyrdymov, A, Skobliakov, A. Kantsyrev, S. Zähter, N.G. Borisenko, A. Pukhov, and N.E. Andreev.
Forward-looking insights in laser-generated ultra-intense gamma-ray and neutron sources
for nuclear applications and science, Nature Communications 13, 170 (2022)

## Slide 32
ARC with Compound Parabolic Concentrator ( CPC)
versus PHELIX with foams at 1018 W/cm2
5 mm
15 mg/cc
Au 1mm

## Slide 33: 1 ps ARC beam performance
Shaun Kerr, 01.09.2023
Note that the four ARC beams all have different levels of performance, and that these graphs are for the best performing beam, 353A (highest intensity, smallest focal spot). The variation can be large: on this shot the worst performing beam, 354A, had only 5% of energy at >1e18, vs. 22% for 353A.
.
total 260 J
ARC beam 353A
50 J (22% > 1018 W/cm2)
200 µm
0
-200 µm

## Slide 34: Can we produce relativistic electrons using sub-relativistic intensities?
≥ 1018 W/cm2 - 5 J (0.72 %)
≥ 1017 W/cm2 - 300 J (47%)
1016 W/cm2 - 1017 W/cm2 ~ 200 J
focal spot 50% = 120 µm
ARC 10 ps, 600 J /beam

## Slide 35: Enhanced laser-target coupling at near-relativistic intensities using CPC at ARC
Order of magnitude increase in laser-target coupling at 1018W/cm2 using CPC (G.J. Williams et al)
Compound Parabolic Concentrator (CPC) at the Advanced Radiographic Capability laser system:
large fraction of energy contained in the wings of the beam (80%) is repointed towards the central beam spot
HD and PIC simulations show that the increase in the coupling laser-to target is due to a combination of the longer scale length plasma and the enhanced acceleration mechanism driven by laser turbulence that develops from reflections from the cone walls.
Notes: PRE2021, Williams:
In summary, we demonstrate that CPC cones can be used as robust target components to increase the conversion efficiency into MeV electrons by nearly an order of magnitude and electron temperature by >3× compared to flat targets. Hydrodynamic and PIC simulations reveal that the increases in conversion efficiency are primarily due to additional preformed plasma at the cone tip, whereas the temperature increase is due to a combination of the longer scale length plasma and the enhanced acceleration mechanism driven by laser turbulence that develops from reflections from the cone walls.

## Slide 36: ARC-results on electron acceleration using CPC
6 MeV
Flat
Cone
Cone
The increased performance is primarily due to the presence of turbulent laser fields from light reflecting from the cone walls
as well as increased NCD plasma volume confined in the cone-> conditions for generation of super-ponderomotive electrons.

## Slide 37: ARC- results on MeV bremsstrahlung production using CPC
Converter: 0.5-1 mm Au
1.6 x1018 W/cm2, 10 ps
CPC: low directionality
of gamma rays (FWHM115°)

## Slide 38: CPC-approach is not compatible with gas jet/gas tank
N. Lemos, F. Albert
due to turbulent character of the laser field in the cone exit
SM-LWFA can be driven only at 1018 W/cm2 ARC intensity only
4 mm
NIF
NIF

## Slide 39
Can a large focal spot ( ≥ 50 µm ) make DLA less effective?
X.F. Shen, A. Pukhov et al, Cross-Filament Stochastic Acceleration of Electrons in Kilojoule
Picosecond Laser Interactions with Near-Critical-Density Plasmas Phys. Rev. Appied18, 064091 (2022)
Large focal spot -> simulation for PETAL (1 kJ, 50 mm, 0.7 ps)
filaments only partially merge together: no joint channel for DLA;
instead, Cross-Filament Stochastic Acceleration
Longer laser pulse improves the situation
ARC: 1 ps, 250 J , 22% (50J) with ≥ 1018 W/cm2;
ARC: 10 ps, 600 J, 0.7% (only 4J) with ≥ 1018 W/cm2
PETAL-conditions
ARC, PETAL

## Slide 40: Experimental setup P22-48 October 2023
Front view
TP
(+160°)
MS
(+138°)
MS
(+15°)
MS
(-10°)
MS
(-45°)
X-rays
Ross
Cylinder (3X3 mm)
Neutrons
Laser
CHO 2 mg/cc
300-800 um
PHELIX: 0.65 ps, 1019 W/cm2

## Slide 41: Results with CHO-foam: no DLA at high ns contrast, but with ns -pulse
DLA-beam is mostly centered
E > 10 MeV
Target: 0.5 mm CHO + Cu-foil + ns
Target: 0.8 mm CHO + Cu-foil + ns
M. Gyrdymov
~ 23 MeV
0.16 sr
best focus
PHELIX, October 2023

## Slide 42: TITAN experiments on DLA in expanding plasmas

## Slide 43: Great international team of P22-48
GSI, Friedrich-Schiller University, Goethe-Universität Frankfurt, Czech Technical University, ENEA Frascati, Xi’an Jiaotong University, Chinese Academy of Sciences, Extreme Light Infrastructure (ELI NP)