## Slide 1
High intensity X-ray source using large optical cavity and the future
Junji Urakawa (KEK), WG-1 presentation, 2021.3.17 afternoon session
Abstract
We are developing relatively large 2D 4-mirror optical cavity to reduce the crossing angle between electron bunch train and laser pulse train. Total length of first 2D 4-mirror optical cavity is 7.56m and it includes 9 laser pulse train to realize the crossing angle of 8 degrees between electron beam in Linear accelerator and the laser pulse train in the optical cavity [1]. Second 2D 4-mirror optical cavity is under design and the total length of planed cavity is 16.6m in which 18 laser pulse train can circulate and we have the possibility to realize the crossing angle of 2 degrees.
I will report the performance of first 2D 4-mirror optical cavity and the experimental plan on 2D 4-mirror optical cavities. Below photo shows 1.9m long 2D 4-mirror optical cavity which is operating to generate X-ray. We hope it will be installed into Super-conducting Linear accelerator (STF) to generate high brightness g-ray in the future.
[1] Kazuyuki Sakaue et al., “Stabilization of an optical enhancement cavity using a counter propagating mode” REVIEW OF SCIENTIFIC INSTRUMENTS 89, 023305 (2018).
2-mirror vs 4-mirror optical cavity
*4-mirror is 100 times stable system.
*4-mirror is more flexible in the following points.
Laser injection, feedback to stabilize the resonance
and monitoring the laser profile and intensity in the
Optical cavity.

## Slide 2: Laser Compton Scattering (LCS)
Head-on collision
90°collision
(Exam.)
Laser 800 nm
0°scattering
Inverse Compton Scattering
Laser
Several 10 MeV electron beam
  (Small accelerator)
Several 10 keV X-ray
(like as large SR accelerators)
Property of LCS X-ray
small source point
monochromatic by collimation
Tunable Energy
short pulse (ps, fs)
1. LUCX (Laser Undulator Compact X-ray)

## Slide 3: Electron Accelerators in KEK used for LCS R&D and experiments to develop technologies
Cs2Te
Photocathode RFgun
マルチバンチ電子ビーム生成
Damping Ring
低エミッタンスビーム
S-band Linac (1.3 GeV)
Electron beam: 1.3 GeV
Intensity: ~2x1010 e/bunch,
1 ~ 20 bunches/train, 3.12 Hz
  x/y ~ 1.5nm/4pm
ATF
cERL
STF
Superconducting RF
Pulsed beam:
1.3 GHz, 1 ms
Higher energy:
60 MeV  300 MeV
Plan to restart in 2018
Superconducting RF
CW beam 100 uA  10 mA
20 MeV-35MeV
Normal conducting RF
Pulsed beam: 357 MHz - 1000 bunches/pulse
1.2MW pulse laser stacking in optical cavity as the peak
24 MeV-32MeV
LUCX
Notes: KEK constructed the Accelerator Test Facility (ATF) and the Superconducting Accelerator Facility (STF) for ILC R&D and operates them for educating and training young researchers. Also, Compact Energy Recovery Linac (cERL) and Laser Undulator Compact X-ray source (LUCX) for developments to the application were constructed and are operated. From many experiences based on the construction and the operation in these four facilities, I would like to explain how to design and construct the advanced electron accelerator in the energy range of 3MeV to 30MeV as extremely useful facility with some application examples.

## Slide 4: LUCX and ATF electron source: 3.6-cell RF gun
e- beam
UV laser
(266nm)
Cs2Te photocathode
Tuner
RF Input
Waveguide
100mm
Frequency (π-mode) 2856 MHz
Qvalue 15000
Coupling β 0.99
R/Q 395Ω
Mode separation (π-2π/3) 2.8 MHz

## Slide 5: LUCX accelerator
LCS X-ray
electron source
Photocathode RF gun
12-cell Booster
Optical Cavity:
LCS X-ray source
Optical Cavity

## Slide 6
Energy | 30MeV
Intensity | 0.4nC/bunch
Number of bunch | 1000
Beam size at the collision point (1σ) | 33μm ×33μm
Bunch length | 10ps
Bunch spacing | 2.8ns
Energy | 1.17eV(1064nm)
Intensity | 8mJ/pulse
Waist size(1σ) | 55μm ×25μm
Pulse length | 7ps
Photon flux more than 108 per second
My colleagues got the X-ray
Flux of 107 at 12.5Hz.
Still we have problem
on cavity rigidity.
We need the improvement
of table and installation of
high reflectivity mirrors.
Brightness 1012
Photons/sec/mm2/mrad2 in 0.1%b.w.
Application to novel light sources
Several second is enogh to get X-ray imaging.
Calculation

## Slide 7: LUCX Optical cavity and Laser system
2. Laser Pulse Accumulation with Burst Amplification

## Slide 8
K. Sakaue (Waseda univ.)

## Slide 9
3W
3W picked up pulse
30kW burst amplified pulse
We installed the Pockels cell in order to collect the amplification
power at the electron beam timing.

## Slide 11
Stability of stored pulse intensity: 15% rms
About 0.2nm accuracy of cavity length adjustment was not achieved two years ago.
Laser power stability in the optical cavity
2.8mJ/pulse
Stability of stored pulse intensity: 3.5% rms
About 0.2nm accuracy of cavity length adjustment is achieved now.
Optical cavity is not stable due to the vibration and laser
injection optics drift.

## Slide 12
Development of multi-bunch e- beam at LUCX
2012： 150 bunches, 90 nC
2013： 300 bunches, 380 nC
2014：1000 bunches, 600 nC, 24 MeV
Energy compensation by RF amplitude modulation
Electron beam stability :0.2%(in s)
Number of bunches (1000)
Electron Bunch Charge
LUCX beam target：
30 MeV, 357 MHz
bunch spacing 2.8 ns
more than 1000 bunches/pulse,
beam size less than 100mm
LCS
Collision point
X-ray detector
RF cavity

## Slide 13
Summary of Laser-Electron Beam Parameters at the photon-electron collision point
Wavelength | Repetition | Power | Pulse energy
1064nm | 357MHz | 1MW | 2.8mJ
Size(H) | Size(V) | Pulse duration | Col. angle
60um | 25um | 7ps | 7.5°
Energy | Repetition | Charge | N. bunch
22MeV | 357MHz | 0.6nC | 1000
Size(H) | Size(V) | Bunch length | Emi (H) | Emi (V)
40um | 70um | 15ps | 5πmmmrad | 6πmmmrad
9keV LCS X-ray Energy
ELECTRON
LASER
40μm×70μm
Laser pulse
Energy in the
Optical cavity
Total charge
per train

## Slide 14
Number of X-ray:
1.2x107 Photons/train
Rep. Rate: 3.13Hz
CAIN Simulation assumed following measured values.
Number of X-ray: 3.6x107 Photons/sec
X-ray Energy: 9keV
Source size: 60um x 25um
X-ray flux at the HyPix-3000:
11.83 photons/sec/pixel
This pixel size is 100um x 100um.
X-ray energy distribution at the HyPix-3000
Energy band width(FWHM): ~4%
Calculated by CAIN
Measured X-ray intensity distribution and the comparison with CAIN simulation
12.5Hz

## Slide 15: LCS X-ray imaging at LUCX
small source dimensions
clear expansion of image
edge contrast enhancement by refraction
Chili pepper
280 sec
detector
Chili pepper
300 sec
detector
LCS
point

## Slide 16: Evaluation of present LCS performance
LCS X-ray (LUCX)
10 sec exposure
at 107 photons/sec
SR X-ray (PF-AR)
30 msec exposure
for angiography
Assume the angiography by LCS X-ray,
need 100 improvement
intense electron beam
intense laser pulse
smaller beam size
increase repetition rate
…
small crossing angle
higher e- beam energy
…
integrate challenges!
LCS X-ray (cERL)
100 sec exposure
at 107 photons/sec
still improving…

## Slide 17
3. How to increase the photon yield?
*Reduce the crossing angle, then we need a large optical cavity. (8 to 2 degrees increases ~10 times.)
30f electron beam duct
~4m
*Multi-optical cavity system is possible, then we have to develop multi-fiber laser system with acceptable cost. (increases ~10 times)
2m
2m
70mm
Electron beam
X or g-ray
Electron beam
laser beam
Concave mirror

## Slide 18
View from Beam Dump
X-ray Detector
Beam Dump
Development for Next Generation Compact High Brightness X-ray
Source using Super Conducting RF Acceleration Technique
*Increase electron beam current, then we have to use super-conducting linear accelerator. (increases ~1000 times)
2D four mirror cavity to generate X-ray with two cylindrical lenses.

## Slide 19: 4. Summary
It is a fundamental technology development to realize a compact X and g-ray source ,which energy is several tens of keV or MeV, where a wide variety of application is expected.
Compact LCS X and g-ray source can be small to fit in universities, industrial labs and hospitals, then will contribute to improve our life.
Isolator
Compact Fiber Laser Oscillator with 4 mirror optical cavity
Fibered Stretcher
LD
LD
LDs
1st Pre-amplifier
2nd Pre-amplifier
Power Amplifier
YDF
6/125 PM
DC YDF
12/125 PM
DC YDF
40/200 PZ
Isolator
We can select the repetition rate of the laser pulse which is 162.5, 325 or 650MHz.
For example, 0.3mJ/pulse x 325MHz <100W, so we can use fiber rod for power
amplification.
Possible mode-lock laser system
for photocathode
Free Space Compressor

## Slide 20
Super-conducting accelerator system for compact high
brightness X and g-ray under design
High brightness X and g-ray facility
Thank you for your attention!
To get clear X-ray imaging every second, we have to increase
the X and g-ray flux by factor ~ 100, which is 109 photons/sec.
<50cm
Decelation for beam dump and energy recovering.
We can generate 1013 to 1016 photons/sec by LCS X and g-ray source using long 4-mirror multi-optical cavity system and super-conducting linear accelerator.