## Slide 1
Compact FEL-THz facility at IUAC – commissioning and initial testing of the sub-systems
(Project is supported by IUAC and DAE-BRNS)
Subhendu Ghosh. Inter University Accelerator Centre, New Delhi, India
S.Ghosh, B.K. Sahu, P. Patra, J. Karmakar, B.Karmakar, A. Sharma, S.R. Abhilash, S. Tripathi, P. Barua, A. Kothari, S.K.Saini, S. Kumar, G.O. Rodrigues, M. Aggarwal, V. Joshi, R. Kumar, S.K. Suman, M. Kumar, S. Sahu, S.V.Ramanan, P.Singh, N. Madhavan, R.K. Bhandari, D. Kanjilal and A.C. Pandey, Inter University Accelerator Centre (IUAC), India
A. Aryshev, J. Urakawa, High Energy Accelerator Research Organization, KEK, Japan
S. Tripathi, Diamond Light Source Ltd, Diamond House, Didcot, Oxfordshire, UK
M. Tischer, Deutsches Elektronen-Synchrotron (DESY), Germany
V. Naik, Variable Energy Cyclotron Center, Kolkata, India
V. Teotia, E. Mishra, J. Itteera, K. Singh, S. Malhotra,
Bhabha Atomic Research Center, Mumbai, India
T. Rao, Brookhaven National Laboratory, USA

## Slide 2
Plan of Presentation
Outline of the Compact FEL facility
Commissioning status of various sub-components
Deliverables from Delhi Light Source
Conclusion

## Slide 3
Design parameters of the FEL-THz facility (DLS)
S. No. | Parameters | Max | Min
1. | Radiation Frequency | 3.0 THz | 0.18 THz
2. | Electron energy | 8.2 MeV | 4.0 MeV
3. | Acc. Field (2.6 cell 2860 MHz, Cu cavity) | 112 MV/m | 59 MV/m
4. | Electron beam FWHM at Photocathode | 200 fs | 200 fs
5. | Photocathode material | Cu and CsTe | 
6. | Number of microbunches | 16 | 2
7. | Max charges in a single microbunch | 15 pC | 15 pC
8. | Peak current at Undulator entrance | 75 Amps | 20 Amps
9. | Undulator type | Planer Undulator | 
10. | Undulator period length and total numbers | 48 mm and 33 | 
11. | Magnetic field (K-value) | 0.09 T (0.41) | 0.6 T (2.79)
12. | Undulator length | ~ 1.7 m | 
13. | Klystron and Modulator | 25 MW / 5 kW (peak / average power) | 
14. | Operating Frequency, Bandwidth | 2860 MHz,  1 MHz | 
15. | RF pulse duration | 4.0 sec. | 0.4 sec.
16. | THz Power, pulse duration | 1.7 MW, 15 ps | 1.9 kW, 195 ps

## Slide 4
Major components Pre-bunched FEL – Our case
Electron
beam
Laser
beam
Solenoid
Solenoid
10 Hz
0.375 fs – 6.6 ps
Laser
Undulator Magnet
An electron gun – laser operated PC & a resonator powered by klystron/modulator
A laser system – produce the electron bunches – single pulse is split into many
3. Photocathode – Copper and Cs2Te (Deposition system)
Solenoid, other electromagnets – focus/steer electron beam – Cavity to Undulator
5. Undulator – to produce THz radiation
6. Beam diagnostic and e.m. radiation detector systems
7. Electronics and Control system
U – Undulator wavelength
BU – Undulator mag field

## Slide 5
Tuning of THz frequency in FEL of IUAC
5 MHz
0.333-6.6 ps
U – Undulator wavelength
BU – Undulator mag field
f ~ 3 – 0.18 THz
T = 333 fs to 6.6 ps
 = 100 m to 2 mm
Laser pulses as well
Electron bunches
½ w plate rotates S-wave by 45o.
Polarizing beam splitter makes S-wave & P-wave by reflection & transmission.
16 micro bunched laser within 6-7 psec.
Electron
beam
Laser
beam
Solenoid
Solenoid
Laser

## Slide 6
Scheme of production of Electron
Micro-bunches

## Slide 7
~ 3 μs (RF width)
160ms (6.25 Hz)
200 ns
Total no. of laser
pulses (5 MHz)
are 15
333 fs (3 THz)
200 ns
~ 6 ps
So total no. of laser micropulses/e-bunches/THz pulses 15  16  6.25 = 1500 pulses/sec
Production of electron beam microbunches -
Multi-bunch train of THz
3 s
3 s – nominal RF pulse width
6.25 Hz – Klystron/Mod freq.
Laser Osc. Frequency – 5 MHz
Laser splitting freq. – 3 / 0.18 THz
1
2
15
1
15
1
16

## Slide 8
Beam line of DLS

## Slide 9
Ion Pump
Gate Valve
Turbo Pump
RF Cavity
BPM
Solenoid
Ion Pump
PC Insertion Chamber
Laser Reflection Chamber
Beam Viewer-1
Steerer-I
QP
BPM
Beam Viewer-2
Magnetic Manipulator
Gate Valve
DN160 all metal GV
Steerer-2
Ion Pump
FCT
DN40 Gate Valve
Bending Magnet-1
Beam Viewer-3
Beam Viewer-4
Bending Magnet-2
QP triplet
Steerer-3
QP doublet
Steerer-4
BPM
Undulator
Wave Guide
Radiation extraction Chamber
BPM
400 l/s Ion Pump
FCT
CTR Chamber
DN40 Gate Valve
Pre-Undulator Section
Post-Undulator Section
Based on beam optics designs - Beam line design was completed
Beam Line

## Slide 10
Beam Line completed till Dec. 2020
Magnetic manipulator
Turbo pump
PC insertion chamber
Ion Pump
Electron Gun
Solenoid magnet
BPM
FCT
Beam Viewer
Laser Reflection chamber
Wave Guide is connected to the electron gun
Directional coupler
Electron Gun

## Slide 11
High power RF system, Wave Guide and electron gun
RF system: fully conditioned w load in Oct. ’20
RF system connected w Cavity: Nov.-Dec. ’20
Cavity Conditioning started: Jan. ’21 – going on

## Slide 12
Photocathode, Insertion chamber and electron gun
Cu-Be Spring for RF contact

## Slide 13
Cu-Be Spring for RF contact
Mechanism to insert the PC
plug into the RF cavity
Magnetic manipulator

## Slide 14: RF Measurements of RF Gun
Parameters | KEK (after fabrication) | IUAC (after installation)
Loaded Q-factor | 7988 | 7060
External Q-factor | 16822 | 14892
Unloaded Q-factor | 15211 | 13424
Coupling Coeff. β | 0.904 | 0.901
Mode Sep (0 and π) | 11.17 MHz | 11.24 MHz
Mode Sep (2π/3 and π) | 4.17 MHz | 4.37 MHz
Accelerating Field profile Measured
( bead pull) & simulation

## Slide 15
High Power RF System
Cavity
Cavity
Original Plan
Present status

## Slide 16
REFLECTED
FORWARD
4 μsec RF On
RF Conditioning
With Dummy load
With Cavity
4 μsec RF On
FORWARD
REFLECTED

## Slide 17
Pick up
4 μs
Reflected
Forward
4 μs
4 μs
RF Conditioning of Cavity

## Slide 18: First signature of electron beam at IUAC – Dark Current
March 01, 2021

## Slide 19
Why cavity filling time is > 2μs?
How to reduce filling time and minimize the reflected power?
Do we need frequency tracking during conditioning?
Role of variation in photocathode position during conditioning?
Doubts ?

## Slide 20
Measurement through Directional Coupler near cavity
Port 1: FWD port of Directional Coupler through 1 W amplifier (28 dBm max.)
Port 2: REF port of Directional Coupler
Plot of S21 shows peak at 2862.7 MHz
Expected frequency = 2860 MHz
Details of Directional Coupler
  FWD Coupling = 57 dB
  REF Coupling = 60 dB
  Directivity = 30 dB
Span: 2.74 MHz
Span: 50 MHz

## Slide 21
Measurement through Directional
coupler near Klystron
Port 1: FWD port of Directional Coupler through 1 W amplifier (28 dBm max.)
Port 2: REF port of Directional Coupler
Plot of S21 shows peak at 2862.7 MHz
Expected frequency = 2860 MHz
Spectrum Analyzer Ouptut at FWD port of DC near cavity = 2862.5 MHz
Details of Directional Coupler
  FWD Coupling = 58 dB
  REF Coupling = 59 dB
  Directivity = 30 dB

## Slide 22: Doubts??
Why peak appears at 2862 MHz and not at 2860 MHz? Because when feeding with klystron power, cavity gives maximum output around 2860 MHz.
Is the power actually going into cavity? Is the method correct?
Is the VNA plot showing actual Reflection from cavity?
Or is there a new cavity formed between two directional couplers as the waveguide offers < 1 dB attenuation while the directivity is > 30 dB for directional couplers.

## Slide 23
Energy budget (16 microbunches) and Energy available
Case | Copper PC | Cs2Te PC
Charge/bunch (pC) | 15 | 15
No. electrons/bunch | 9.38e+07 | 9.38e+07
Q.E. of PC | 1.0 e-05 | 1.0 e-03
No. photons required | 9.38 e+12 | 9.38 e+10
Photon energy required | 7.3 J | 72.6 nJ
Stages | Energy
Pre-Amp output | 25 nJ, IR
Output of Amp-1 (48 dB), ~ 260 times | 6.5 J, IR
Output of Amp-2 (48 dB), ~ 260 times | 1.69 mJ, IR
After 4th harmonic, 20% eff. | 338 J, UV
After splitting, 16 pulses, 3.1% eff. | 10.5 J
BUDGET
AVAILABLE

## Slide 24
Oscillator: 130 MHz
Pump (LD1): CW
Pulse Picker by
Semiconductor Optical
Amplifier: 130 to 5/10 MHz
Pre-Amplifier
Pump (LD2): CW
1st
stage
of
Amp.
2nd.
stage
of
Amp.
Fibre Laser system

## Slide 25
Fibre Laser system
Completed sections:
Oscillator
Pulse picker
Pre-Amplifier
Amplifier-1
Amplifier-2
Pulses is compressed upto ps
– working to compress further from ps to fs
Power after FHG is still low – working to improve the power
Single laser pulse will be split in to many.

## Slide 26
Initial loading chamber
TOP VIEW SCHEMATIC
Photocathode: Deposition system for semiconductor PC

## Slide 27
Photocathode Deposition System
Present status:
Te evaporation was demonstrated succesfully
~ 2 ½ weeks of baking @ 1500C.
Vacuum = 8.9X10-11 torr was achieved
Final Demonstration, Dismantling:
in presence of IUAC’s personnel
Planning to be shipped by April ’21 by sea

## Slide 28
Undulator: Quick Introduction
1. | Undulator | U48 ( U-> undulator, 48-> undulator period)
2. | Undulator Period | 48 mm
3. | Number of periods | 33
4. | Length of undulator | 1584 mm (magnet structure) Total length along with structure ~ 2400 mm
5. | Undulator Technology | Pure Permanent Magnet (PPM) , Symmetric undulator
6. | Magnet material | NdFeB
7. | Individual magnet dimensions | 70 mm (y) x 22 mm (z) x 12 mm (x)
8. | Undulator gap: working range | 16 mm (min) – 45 mm (max) {open gap: 140 mm}
9. | Measurements performed | Hall probe (BESSY) Stretched wire (DESY)
Magnet Structure
λu =48 mm; N= 33
Table: Specifications of U48
z
x
y
Undulator is a periodic arrangement of magnets in such a way that the particle passing along its axis experience a sinusoidal varying magnetic field.

## Slide 29
Undulator
Spare Undulator was donated by HZB, Germany – estimated cost ~ 6 crores
Refurbished at DESY – 3 IUAC personnel were trained in the measurement, operation
Magnetic field measurements were done at HZB followed at DESY
Vacuum chamber & Various correction coils were designed and mounted/to be mounted
Transported to basement in last Jan. 2021, soon will be moved / installed in the beam line

## Slide 30
Undulator: Current Status
The undulator was expected to come to IUAC in April/ May, however due to COVID-19 situation, it got delayed.
Subsequently, U48 along with its other accessories reached IUAC on 25th December, 2020.
Current Status: The magnet is now in the basement area of FEL and sitting on three original legs and three indigenously fabricated in IUAC (for height extension).
DESY
IUAC

## Slide 31
Fabrication, testing of BM, Quads and Steering magnets
2 BMs, 7 Quads, 5 steering magnets
are designed and developed at
Electromagnetic Applications
and Instrumentation Division,
BARC in record time.
They have arrived at IUAC &
are waiting to be installed
In the beam line.
P.S. of all the magnets - IUAC

## Slide 32
THz from source to experiments: Extraction, Detection and Transportation of THz

## Slide 33
Terahertz Transportation and Detection
OAP: Off-axis parabolic mirror, FM: Flat mirror, TL: THz lens
After undulator, THz radiation will be emitted along with electron beam.
The radiation is reflected, the electron beam passes through Ti-foil
Pyroelectric detector for power detection: procurement in progress
Undulator Vacuum Chamber
Undulator Magnet
Bellow
BPM
THz Extraction Chamber with Titanium foil
Electron Beam + Undulator THz
Reflected THz
Electron Beam Path-2
CTR THz
CTR Chamber with Aluminium foil
(Future plan)
Beam Dump
FCT
Electron Beam Path-1 (to experimental stations)
Bellow
Bending magnet
Schematic of THz beam line after the undulator

## Slide 34
Coherent Transition Radiation (CTR) simulation
Two THz source: Undulator based (narrow band) and CTR based (Broad band).
CTR chamber

## Slide 35
Design and Calculations on various sub-systems
Correction scheme for Undulator field roll-off effect.
Simulations of Dark current detection.
Radiation simulations for THz power calculations.

## Slide 36
New control room is being constructed
Control scheme are being developed for
  Vacuum control and interlock system
  Photo Cathode deposition System
  Beam line magnets control
  Beam Diagnostics
  Undulator
  THz detection and transportation
  Radiation safety and interlock
Control scheme

## Slide 37
Time width | No. of electrons | Total electron current
~ 200 fs | 9.3  107 | 75 A
~ 6 ps | 1.5  109 | 40 A
~ 3 s | 2.25  1010 | 1.2 mA
1 sec. | 1.4  1012 | 22.5 nA
Deliverables: THz radiation and electron beam
Freq (THz) | λ(mm) | T_pulse (simulation) (ps) | Peak power @fwhm | Δf fwhm (THz)
0.18 | 1.667 | ~195 | ~ 1.9 kW | 0.0078
3.0 | 0.1 | ~15 | ~1.7 MW | 0.2786

## Slide 38
Conclusion
A compact FEL-THz facility named as Delhi Light Source is under construction.
It is a Pre-bunched FEL - microbunch structure will be produced @ photocathode.
First signature of electron beam from dark current was observed.
Photocathode based RF electron gun will produce quality e-beam (~ 4 – 8 MeV)
Electron beam to be injected in to a compact undulator to produce THz (0.18 to 3.0)
THz radiation & Electron beam to be used for experiments in multidisciplinary Sc. in fundamental and applied areas.

## Slide 39
Acknowledgement
Dr. K.K. Pant, RRCAT, Indore, India
Dr. Abhay Deshpande, SAMEER, Mumbai, India
Dr. Ulf Lehnert, ELBE facility, HZDR, Germany
Prof. Xijie Wang, SLAC, USA
Dr. Jinfeng Wang, Osaka University, Japan
Dr. Siriwan Krainara, Kyoto University, Japan

## Slide 40
Thank you for your attention