## Slide 1
Innovative accelerator techniques in Novosibirsk
Konstantin Lotov
Budker Institute of Nuclear Physics
Novosibirsk State University
Institute of Laser Physics

## Slide 2
K. Lotov, AFAD-2021, 17.03.2021, p. 2 of 17
Where we are?
Novel accelerator studies in:
Budker Institute of Nuclear Physics
Institute of Laser Physics
Almost all researchers are also with Novosibirsk State University
(that’s why dual affiliations)
City with 1.6 M population (No. 3 in Russia)
> 30 Institutes and University

## Slide 3
Research groups at BINP and ILP
Ivan Kargapolov
(MS)
Laser-plasma experiments
Dr. Vladimir
Trunov
Dr.Sc.Svetlana
Avtaeva
Dr. Konstantin
Gubin
Stanislav Frolov
Dr. Victor Petrov
Gleb Kuptsov (MSc)
Vladimir Petrov
(MSc)
Dmitri
Schvydkoy
(PhD student)
Radiation from beams and plasmas
Dr. Sc. Igor Timofeev
Dr. Vladimir
Annenkov
Evgeniia Volchok
(PhD student)
Vladimir
Glinskiy (MS)
Vladislav
Kurshakov (BS)
Dr. Evgeny
Berendeev
LCODE Team: theory and simulations of
PWFA & LWFA
Prof. Konstantin Lotov
Vladimir Minakov
Mikhail
Baistrukov (MS)
Alexander Gorn
(PhD student)
Petr Tuev
(PhD student)
Roman Spitsyn
Nikita
Okhotnikov
(BS)
Vlada
Yarygova
(BS)
Novel
W-band structures
Dr. Alexey
Levichev
Mariya Arsentyeva
(PhD student)
K. Lotov, AFAD-2021, 17.03.2021, p. 3 of 17

## Slide 4
LCODE Team: theory and simulations of PWFA & LWFA, (mostly) using a quasi-static code
(numerical example for n0=1016см-3 and 500 GeV (γ=106) final energy)
accelerating structure size c/ωp≈50 μm
driver wavelength
λ≈0.8 μm
betatron period,
up to c/ωp~5 cm
Acceleration length,
γc/ωp~50 m
106
~108
Quasi-static approximation is good for plasma wakefield acceleration, which has too different time and length scales
Moving window: beam changes slowly,
all plasma particles started from r0 with p0 (almost) copy the motion of each other
Co-moving coordinate x =z-ct
Particle parameters: x, y, z, px, py, pz
Depend on: t x
Simulation domain: x, y, z
Trajectory parameters: x, y, px, py, pz
Depend on: x
Simulation domain: x, y
(beam energy/mc2)1/2 (window length / grid step) times faster
long time step for beam
-1 dimension
up to 109 for AWAKE baseline (compared to PIC)
LCODE:
quasi-static,
2d (axisymmetric/plane) freely available (https://lcode.info/),
3d under development,
well tested for long simulation windows, long propagation distances and charged drivers
The team not only develop the code, but also make theoretical studies
Any kind of collaboration is welcome
LCODE Team: theory and simulations of
PWFA & LWFA
Prof. Konstantin Lotov
Vladimir Minakov
Mikhail
Baistrukov (MS)
Alexander Gorn
(PhD student)
Petr Tuev
(PhD student)
Roman Spitsyn
Nikita
Okhotnikov
(BS)
Vlada
Yarygova
(BS)
K. Lotov, AFAD-2021, 17.03.2021, p. 4 of 17

## Slide 5
LCODE Team: Recent studies: AWAKE simulations (proton-driven PWFA)
from E.Adli et al. (AWAKE Collaboration), Nature 561, 363 (2018)
400 GeV
σz~7 cm
σr~0.2 mm
εn~3 mm mrad
1014–1015 cm-3
Ti:Sapphire, 780 nm,
120 fs, 450mJ
20 MeV, 650 pC,
15 mm mrad, 2 ps
from A.Caldwell et al (AWAKE Collaboration),
Nuclear Instr. Methods A 829, 3 (2016).
The measured spectrum shape and energy gain (2 GeV) are consistent with predictions.
K. Lotov, AFAD-2021, 17.03.2021, p. 5 of 17

## Slide 6
LCODE Team: Recent studies: AWAKE simulations (proton-driven PWFA)
from E.Adli et al. (AWAKE Collaboration), Nature 561, 363 (2018)
400 GeV
σz~7 cm
σr~0.2 mm
εn~3 mm mrad
1014–1015 cm-3
Ti:Sapphire, 780 nm,
120 fs, 450mJ
20 MeV, 650 pC,
15 mm mrad, 2 ps
F. Braunmüller et al., PRL 125, 264801 (2020).
Proton beam micro-bunching: predicted in 2010 (N.Kumar, et al., Phys. Rev. Lett. 104, 255003),
measured in 2018
from E.Adli et al. (AWAKE Collaboration), Phys. Rev. Lett. 122, 054802 (2019).
K. Lotov, AFAD-2021, 17.03.2021, p. 6 of 17

## Slide 7
LCODE Team: Recent studies: AWAKE simulations (proton-driven PWFA) – quantitative agreement
Maximum radius of deflected protons: simulations (2d axisymmetric LCODE) agree with measurements. In beam population scans, the difference is below 5% without fitting parameters (all input data are taken from measurements).
A.A.Gorn et al. (AWAKE Collaboration), Plasma Phys. Control. Fusion 62, 125023 (2020).
Simulated with LCODE.
K. Lotov, AFAD-2021, 17.03.2021, p. 7 of 17

## Slide 8
LCODE Team: Recent studies: FACET simulations (electron-driven PWFA)
Scheme of the experiment, plasma image, and comparison with simulations.
Wakefield evolution up to 3000 wave periods (world record) taking into account Coulomb collisions and impact ionization of the surrounding gas (for the first time), quantitative agreement with measurements.
R.Zgadzaj, T.Silva, V.K.Khudyakov, A.Sosedkin, J.Allen, S.Gessner, Z.Li, M.Litos, J.Vieira, K.V.Lotov, M.J.Hogan, V.Yakimenko, and M.C.Downer, Dissipation of electron-beam-driven plasma wakes. Nat. Comm. 11, 4753 (2020).
It turned out that a long chain of events takes place after the beam passes through the plasma:
Wavebreaking occurs
Wave energy goes to a small fraction of fast electrons
Fast electrons escape from plasma, plasma becomes positively charged
Electric field accelerates ions radially
Ions impact-ionize a small fraction of surrounding neutrals
Emerging electrons (dragged by ions or appeared due to ionization) continue ionizing the gas, the plasma density increases exponentially, the main channel is two-step ionization (via excited states)
Plasma radius grows rapidly
K. Lotov, AFAD-2021, 17.03.2021, p. 8 of 17

## Slide 9
Radiation from beams and plasmas: Problems
System “plasma – electron beam/laser pulse”
as a radiation source.
Search and study of new mechanisms
of radiation generation.
Solar radio bursts:
Electron beams generated during magnetic
reconnection, solar flares and coronal mass
ejections provide free energy for wide variety of
different radio emission processes.
Source: Nasa/SDO
Beam-plasma discharge
Theoretical and numerical study of the beam-plasma interaction
peculiarities. In particular, in the context of experiments at open
magnetic traps for plasma confinement.
Gas dynamic open trap
GOL-PET experiment
THz radiation sources
Astrophysical problems
Plasma as a nonlinear medium supports long-
lived oscillations with extremely large electric
fields which provides a fairly narrow radiation
spectrum and high conversion efficiency.
The radiation frequency can be tuned by a
simple change of plasma density.
Radiation from beams and plasmas
Dr. Sc. Igor Timofeev
Dr. Vladimir
Annenkov
Evgeniia Volchok
(PhD student)
Vladimir
Glinskiy (MS)
Vladislav
Kurshakov (BS)
Dr. Evgeny
Berendeev
K. Lotov, AFAD-2021, 17.03.2021, p. 9 of 17

## Slide 10
Radiation from beams and plasmas: Key instruments
To find the whole unstable spectrum, the algorithm for solving
the dispersion equation within the framework of the exact
relativistic kinetic theory, taking into account a finite magnetic
field, has been developed. The algorithm allows one to find the
growth rate of instability of a beam-plasma system with an
arbitrary distribution function of its components.
(a) Particle distribution of the beam after transportation to the strong magnetic
field. (b) The growth rate for the instability of a beam with the
distribution function shown in (a).
a
b
Timofeev I.V., Annenkov V.V. Phys. Plasmas, 20(9), 092123 (2013)
V. V. Annenkov et al. Phys. Plasmas 25, 113110 (2018)
To study collective beam-plasma interaction PIC code with open
boundary conditions has been developed. This formulation of the
problem makes it possible to correctly reproduce the process of continuous injection of particles into the plasma.
Special plasma buffers delete the outgoing particles, create particles that would have to pass through its boundary in the case when there was a real plasma behind them, and also maintain the correct current values in the boundary cells of the simulated plasma.
K. Lotov, AFAD-2021, 17.03.2021, p. 10 of 17

## Slide 11
Radiation from beams and plasmas: Radiation mechanisms
Beam-plasma antenna
Three wave interaction
Colliding plasma waves with differing profiles of electrostatic potential can be an efficient mechanism for generating high-power THz emission at
Nonlinear interaction of counter propagating
plasma waves
I. V. Timofeev et al. Phys. Plasmas 24, 103106 (2017)
V. V. Annenkov et al 2020 ApJ 904 88
Generation of electromagnetic radiation during the coupling of oblique
oscillations excited in a plasma by counter streaming electron beams.
A thin plasma column with a longitudinal density
modulation works like a plasma antenna in
which an electron beam can excite a
superluminal wave of electric current. The current
can be converted in electromagnetic radiation at
plasma frequency harmonics.
Radiation conditions for the 1st harmonic
Radiation angle
V. V. Annenkov Plasma Phys. Control. Fusion 58, 045009 (2016)
K. Lotov, AFAD-2021, 17.03.2021, p. 11 of 17

## Slide 12
Novel W-band structures: between conventional RF structures and plasmas in size and fields
The W-band structure is to be fed by the train of electron bunches from the SKIF linear accelerator
First prototype of the structure
2.7 mm
0.8 mm
1.75 mm
1.75 mm
The structure to be manufactured
(shown here is electric field excited by the electron beam)
Operating frequency | 85 GHz
Bunch charge | 0.3 nC
Bunch distance | 5.6 ns
RMS bunch duration | 2.5 ps
Number of cavities in the structure | 100
Lost energy | up to 5 MeV
Induced electric field | up to 25 MV/m
Novel
W-band structures
Dr. Alexey
Levichev
Mariya Arsentyeva
(PhD student)
K. Lotov, AFAD-2021, 17.03.2021, p. 12 of 17

## Slide 13
The W-band structure is to be fed by the train of electron bunches from the SKIF linear accelerator
2.7 mm
0.8 mm
1.75 mm
1.75 mm
Novel W-band structures: between conventional RF structures and plasmas in size and fields
SKIF accelerator structure
Spectrometer
Faraday cup
W-band structure
Operating frequency | 85 GHz
Bunch charge | 0.3 nC
Bunch distance | 5.6 ns
RMS bunch duration | 2.5 ps
Number of cavities in the structure | 100
Lost energy | up to 5 MeV
Induced electric field | up to 25 MV/m
K. Lotov, AFAD-2021, 17.03.2021, p. 13 of 17

## Slide 14
Laser-plasma experiments at ILP: Two channel multiterawatt laser system based on OPCPA
532nm 90 ps
0.6J, 10Hz per
pump channel
Laser Phys. Lett. 11, 095301, 2014
beam pointing
distributions
contrast of compressed pulses in the 1st channel (a) and the 2nd one (b)
Intensity >5*1018 W/cm2
Features
Low beam pointing instability
(the ability of experiments with narrow hollow waveguides)
High contrast of compressed pulses
Precise time synchronization between channels
(better than 100 as )
High space quality (M2<1.1)
(high focusibility)
up to 30-50TW (20fs)
ps pump
Laser-plasma experiments
Dr. Vladimir
Trunov
Dr.Sc.Svetlana
Avtaeva
Dr. Konstantin
Gubin
Stanislav Frolov
Dr. Victor Petrov
Gleb Kuptsov (MSc)
Vladimir Petrov
(MSc)
Dmitri
Schvydkoy
(PhD student)
K. Lotov, AFAD-2021, 17.03.2021, p. 14 of 17

## Slide 15
Laser-plasma experiments at ILP: Pulse propagation through narrow capillaries
Capillary: triangular-shaped, height ~60 μm, length 2 cm produced by engraving triangular grooves on a polished copper plate; another (not grooved) plate closes the capillary gap between the plates < 0.5 μm
Laser: 850 nm, up to 30 mJ (0.6 ТВт), 50 fs, contrast 10-8, angular instability 2 μrad (1.5 μm fluctuations at the entrance) best transmission observed with the focal spot of 35 μm in diameter at the entrance almost no focal spot changes as the energy increases
Camera (VC): 10-6 Bar, diameter 5.5 cm, length 76 cm on the five-dimensional stage (3 coordinates and 2 angles).
20 mm length
Capillary transmission:
is high
absolute = -------------------------
transmitted energy
pulse energy
relative = -----------------------------------
transmitted energy
energy falling into the hole
A problem:
capillary degradation
Reduction of the absolute transmission with the number of transmitted pulses for different pulse energies.
entrance
Plugs (~1 mm long) at the distance of 2–4mm from the entrance are observed, because of matter re-distribution. Plugs block the capillary completely.
Reason: high reflectivity of metals at these parameters
What happens?
K.V.Lotov, et al., Phys. Plasmas 22, 103111 (2015).
K.V.Gubin, et al., J. Appl. Phys. 120, 113103 (2016).
K. Lotov, AFAD-2021, 17.03.2021, p. 15 of 17

## Slide 16
Laser-plasma experiments at ILP, plans: LWFA at moderate intensities, Compton γ-source, THz generation
1 – laser beams, 2 – supersonic gas jet, 3 – electron beam, 4 – collimator, 5 – phosphor screens, 6 – magnet dipole,
7 – Faraday cap, 8 – CCD.
Parameters:
laser system: 10 Hz, 100÷300 mJ, ~20 fs, 810 nm;
acceleration area: diameter ~ 10÷15 μm, length ~ 0.5 mm;
supersonic He jet: diameter ~1.2 mm, gas density 1018÷1019 cm-3, Mach number 3.5÷4, gas backpressure 5÷10 atm
Special features:
aimed at quantitative agreement with simulations
two laser pulses (Compton scattering, THz radiation)
Schematic of the experiment
PM: parabolic mirrors
PD: photodiode detector
PC: personal computer
Radiation generation by counter propagating laser pulses:
proof-of-principal experiment
K. Lotov, AFAD-2021, 17.03.2021, p. 16 of 17

## Slide 17
Thank you