## Slide 1
Injection facility for SCT-Factory
Alexey Petrenko, BINP
2021 workshop on future Super c-τ factories, Nov. 17, 2021, Novosibirsk.

## Slide 2
5 nC, 2.5 GeV e-
on e+ production target
5 nC, 200 MeV e+
1.5 GeV e+
3 nC, (2·1010)
1.5 GeV e- bypass
1.5 GeV e-/e+ linac
Two options to produce
2·1011 e+ / sec:
10 Hz operation with
5 nC e- bunch
20 Hz operation with
2.5 nC e- bunch
+ an additional 1.5-2x frequency increase required for e- production
Old injector layout for the 3 GeV BINP-based facility:
With 4.8 nC (3e10 e-), 2.5 GeV electron beam on target we get 5 nC e+ after the solenoid at 200 MeV, 3.5 nC before the damping ring and 3.0 nC e+ captured by the damping ring:
2
2020 Joint Workshop on Future charm-tau Factory

## Slide 3
3
New injector layout for the 3.5 GeV facility:
The goal is to be able to work at 50 Hz, although 20 Hz is probably enough.
With 3 nC of 3.5 GeV electrons per bunch on target we should capture at least 1.5 nC (1010) positrons per bunch, i.e. 1010 e+/bunch at 50 Hz or 5·1011 e+/sec – good safety margin (2·1011 e+/sec is required by the collider).

## Slide 4
Positron production system
http://www.inp.nsk.su/~petrenko/c-tau/Injector/p-linac/Martyshkin/
Positron distribution after the solenoid (Pavel Martyshkin):
2.5 GeV
4
Old simulation for 5 nC 2.5 GeV e- bunch on target.

## Slide 5
Losses during transition to quadrupole focusing:
5
Old simulation for 5 nC 2.5 GeV e- bunch on target.

## Slide 6
Similar system at KEK
From Pavel Martyshkin’s presentation
6

## Slide 7
1.5 GeV damping ring (scaled down CLIC Pre-Damping Ring)
7
Damping times: τδ = 2.3 ms, τx,y = 4.7 ms.
Energy loss per turn = 430 keV (1-2 MV RF required)
With 1.5 MV RF the 3 nC bunch will have σz = 7 mm, εx,y = 3 nm.
Wigglers
Wigglers
TME cells
This seems to be enough for 50 Hz operation even in a single bunch regime. The ring could be downsized if we assume multiple bunches stored for more than one cycle.

## Slide 8
Conclusion
8
New e+/e- injector design is proposed for the 3.5 GeV SCT-factory with fully independent electron and positron linacs (total energy of linacs is 10.5 GeV).
The 50 Hz operation with 3 nC e- bunches on target certainly meets the collider requirement of 2·1011 e+/sec.

## Slide 9
Backup slides:

## Slide 10
Particle tracking of the full distribution:
Transition to quadrupole focusing
10

## Slide 11
Scaling down CLIC Pre-Damping Ring
http://project-clic-cdr.web.cern.ch/project-CLIC-CDR/Drafts/Yannis_DR.pdf
Designed for 2.8 GeV
Similar magnetic field but with 1.5 GeV e+ now:
Remove several FODO-periods.
Proportionally scale all elements
Existing tunnel
11

## Slide 12
Damping ring (scaled down CLIC Pre-Damping Ring)
Wigglers
Wigglers
TME cells
TME cells
Red line marks existing tunnel
Damping times: τx = 7.2 ms, τs = 3.5 ms
Equilibrium emittance: εx = 6.3 nm (including IBS)
http://www.inp.nsk.su/~petrenko/c-tau/Injector/damping_ring/Twiss.html
12

## Slide 13
Turn
Positron bunch capture into the damping ring
Surprisingly the capture is reasonably good even into completely non-optimized optics. (+ to be checked with realistic field errors)
13