## Slide 1: Electronic Readout System for Belle II Imaging Time of Propagation Detector
Dmitri Kotchetkov
University of Hawaii at Manoa
for Belle II iTOP Detector Group
March 3, 2017

## Slide 2: Barrel Particle Identification at Belle II
Belle II experiment at SuperKEKB electron-positron collider
(KEK, Tsukuba, Japan):
asymmetric collisions of 7 GeV electron beam with 4 GeV positron beam
(program’s total integrated luminosity = 50 ab-1)
studies of CP-violating physics processes from decays of U(4S) resonances
need for improved barrel particle identification to detect rare and
previously unobserved phenomena and to mitigate beam backgrounds
in the pT range from 1 GeV/c to 4 GeV/c pions have to be separated from
kaons with the efficiency of 85-90%, while the misidentification efficiency
has to be less than 5%
new 8192-channel Cherenkov radiation imaging Time of Propagation
Detector (iTOP)

## Slide 3: Imaging Time of Propagation Detector
Central Drift
Chamber
Electromagnetic Calorimeter
Electromagnetic Calorimeter
iTOP
Central Drift
Chamber
in each module:
2.5 m long quartz
bar glued from two
125 x 44 x 2 cm2
pieces
16 modules placed between Central Drift Chamber and Electromagnetic Calorimeter
a spherical mirror is glued to one end and a prism is glued to another end of the bar
iTOP

## Slide 4: Cherenkov Radiation in Quartz
y
z
x
quartz
charged
particle
Cherenkov photon from pion
Cherenkov photon
from kaon
Hamamatsu microchannel plate photomultiplier tube (MCP-PMT) R10754-07-M16(N)
16-channels (4 x 4 pixel matrix)
32 MCP-PMTs are attached to each prism
measurement of Cherenkov photon
x-y position at the prism surface
(MCP-PMT pixel coordinate) and
in-quartz propagation time

## Slide 5: Ice Radio Sampler
Ice Radio Sampler version X (IRSX) ASIC
adaptation from designs for neutrino
experiments in Antarctica
0.25 mm TMSC CMOS process
8 channels
switched capacitor array with 32,768
storage cells for each channel sampling
buffer
operational sampling speed is 2.714
gigasamples per second

## Slide 6: Sample and Hold Cell
Vin
Write
Strobe
Trigger
T1
T2
Vpedestal
Csample
to ADC
basic unit or Switched Capacitor Array
trigger or write strobe
closes an analog switch
and an input signal gets
stored in 14 fF capacitor
charge remains held in
the capacitor until it is
overwritten or until discharge occurs through leakage

## Slide 7: Wilkinson Analog-to-Digital Conversion
Ramp Generator
Clock
Gray Code
Counter
Comparator
Register
D (0:11)
Vcomp
Vramp
Vin
Vcomp
Vin
Vramp
12
time
common voltage ramp connected to a positive
input of a comparator
11-bit Gray code counter increments while the ramp voltage increases
when the voltage ramp level exceeds the stored sample voltage, the comparator latches the Gray code value
12th bit is for the phase
stored voltage → time interval → ADC value

## Slide 8: Subdetector Readout Module
128-channel standalone
front-end electronic readout unit
assembly of four ASIC carrier Boards and one Standard Control Read-Out Data (SCROD) board
ASIC carrier board:
four 8-channel IRSX ASICs and one Xilinx Zynq Z-7030 System on a Chip
SCROD board:
one Xilinx Zynq Z-7045 System on a Chip

## Slide 9: SCROD
debugging
trigger
link
programming and clock
data
link
RAM
Zynq
Z-7045
low voltage
power
connectors to
ASIC carrier

## Slide 10: ASIC Carrier Board
connectors to
ASIC carrier
pogo pin assemblies
amplifiers
Zynq
Z-7030
IRSX
connectors to ASIC
carrier or SCROD
IRSX
IRSX
pogo pin assemblies
amplifiers
IRSX

## Slide 11: Front Boards
sockets for MCP-PMT anode and HV contacts (one board per four MCP-PMTs)
contact pads for ASIC carrier pogo pins
contact pads for HV divider board

## Slide 12: High Voltage Board
8 channels (one channel per one MCP-PMT)
each channel: 400 MOhm resistive divider coupled with high voltage transistors
aluminum enclosure
attached to Subdetector Readout Module and to an aluminum water cooling reservoir
pogo pins are pressed against the HV contact pads on two front boards
MCP-PMTs:
operational voltage: from 2100 V to 3100 V
charge gain: from 2 x 105 to 3 x 105

## Slide 13: Single-Photon Laser Signal Data Taking
data fiber link
water cooling reservoir
laser fiber
MCP-PMT
high voltage board
programming and clock

## Slide 14: iTOP Readout Scheme
TOP module
8 MCP-PMTs
8 MCP-PMTs
8 MCP-PMTs
8 MCP-PMTs
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
ASIC carrier
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
4 IRSX ASICs
SRM
SRM
SRM
SRM
one iTOP module:
32 MCP-PMTs
4 Subdetector Readout
Modules (SRMs)
16 ASIC carrier boards
64 IRSX ASICs
512 channels

## Slide 15: SCROD Firmware
Device: Xilinx Zynq Z-7045
PL: Programmable Logic
Kintex-7 FPGA
350,000 cells
218,600 Luck-Up Tables
PS: Processing System Dual-core ARM Cortex-9
1 GHz
T/T: Trigger and Timing
GTX: Gigabit Transceiver
PS Main
Pedestal calculation
Feature extraction
PS
GTX
GTX
PL
Trigger Stream
(Aurora)
GTX
GTX
GTX
GTX
Serial
Serial
Serial
Serial
Trigger Buffer and
Sorter
Input Data Buffering
Output Data Buffering
AXI-Lite
Bus
Local Registers
T/T
Register
Data
DDR
Register
Data
508.9/4 MHz
mezzanine
connectors
Data
System Trigger
B2TT
Trigger

## Slide 16: ASIC Carrier Board Firmware
mezzanine
connectors
PS Main – Status Monitoring
PS
PL
GTX
T/T
Auxiliary Monitoring
Register
Data
AXI-Lite Bus
Output Data Buffering
Digitization
Analog Memory
Trigger Monitoring
Register Interface
Data Readout
Sequencer Control
Readout Buffering
ASIC Master Control
Serial Data Interface
Channel-Level Triggers
Memory Addressing
Digitization (Gray Code)
Serial Data Interface
ASIC
(x 4)
Trigger
Clock
Serial
Device: Xilinx Zynq Z-7030
PL: Programmable Logic
Kintex-7 FPGA
125,000 cells
78,600 Luck-Up Tables
PS: Processing System Dual-core ARM Cortex-9
800 MHz
T/T: Trigger and Timing
GTX: Gigabit Transceiver

## Slide 17: ASIC Carrier Timing Performance
measurement of 20 ns time delay between leading edges of a reconstructed 1.5 V pulse of 7 ns width and its delayed copy
overall time resolution is
20 - 30 ps

## Slide 18: Timing Performance with MCP-PMTs
measurement of a time between leading edges of
a reconstructed pulse from MCP-PMT signal and a reconstructed calibration reference pulse
single photon laser signal
laser trigger is independent from the calibration pulse
overall time resolution at the laser test bench is from
60 ps to 80 ps
(MCP-PMT transit time spread = 30 ps;
laser bench TDC time resolution = 25 ps)

## Slide 19: Back-End DAQ System
High Speed Link Board
COPPER-III board
1.6 GHz Intel Atom Z530 CPU
global clock and trigger
Common Pipelined Platform
for Electronic Readout
(COPPER) version III
9U VME format
one High Speed Link Board
collects data from one SRM
one COPPER-III board serves
one iTOP module
16 COPPER-III boards serve
the iTOP detector

## Slide 20: Integration at the iTOP
Assembled Subdetector Readout Modules: 78
Installed at iTOP (8192 channels): 64
Installed at a spare iTOP module: 4
Uninstalled spare SRMs: 10
In-situ data taking from calibration laser and cosmic muon ray events without magnetic field demonstrated performance comparable to or surpassing the in-lab performance
DAQ tests with 1.5 T magnetic field have started and will be continued
through several campaigns
Calibration software that allows reconstruction of laser, cosmic ray muon, and electron-positron collision data with resolution of less than 50 ps have been developed