## Slide 1: The LHCb Calorimeter System: Design, Performance and Upgrade
Yu. Guz (IHEP Protvino)
on behalf of the LHCb collaboration
February 27 – March 03 2017, Novosibirsk
INSTR – 2017
Instrumentation for Colliding Beam Physics

## Slide 2: The LHCb detector
two RICH detectors
electromagnetic calorimeter with preshower
hadron calorimeter
muon identification system
Main subdetectors:
Vertex Locator (VeLo): a silicon strip detector surrounding the IP
warm magnet, ~4 Tm;
tracker stations (inner: silicon; outer: straw)
2008 JINST 3 S08005

## Slide 3: The LHCb Calorimetry System
  solid angle coverage 300x250 mrad
  distance from IP: ~12.5 m
  four subdetectors: SPD,PS,ECAL,HCAL
  based on scint./WLS technique, light readout with PMT
  provides:
    L0 trigger on high pT e±, π0, γ, hadron
    precise energy measurement of e± and γ
    particle identification: e±/γ/hadron; contributes to Muon ID (HCAL).
HCAL
ECAL
PS/SPD
MUON SYSTEM
beam

## Slide 4: PS / SPD
SPD
PS
Lead
The scintillation light is captured by WLS fibers glued into the tiles, and transported via clear fibers to 64-channel HAMAMATSU multi-anode PMT R7600-00-M64MOD.
Both PS and SPD are equipped with LED monitoring system
Inner 144 tiles 4x4 cm2
Middle 64 tiles 6x6 cm2
Outer 16 tiles 12x12 cm2
The scintillator tiles are 15 mm thick. The light is captured and re-emitted by WLS fiber (3.5 loops) glued in a deep groove machined at the surface of the tile. Light readout: multi-anode PMT.
LED
64-ch
MAPMT
VFE board
# cells
Nphe/MIP
The light yield of all 12032 cells measured on cosmics at production: ~ 25+-12 ph.el. / MIP
HV setting: uniform, ~700-800 V
Preshower detector: two planes of scintillator tiles, with 1.5 cm thick lead plane between them. Size and segmentation: matches ECAL.

## Slide 5: ECAL
Shashlik technology
4 mm thick scintillator tiles and 2 mm thick lead plates, ~25 X0 (1.1 λI); Moliere radius ~ 36 mm;
modules 121.2 x 121.2 mm2, 66 Pb +67 scintillator tiles;
Segmentation: 3 zones  3 module types, Inner (9 cells per module), Middle (4), Outer (1). Total of 3312 modules, 6016 cells, (7.7 x 6.3) m2, ~100 tons.
Light readout: PMT R-7899-20, HAMAMATSU. HV supply: individual Cockcroft-Walton circuit at each PMT.
Inner 9 cells
Middle 4 cells
Outer 1 cell
CW base
PMT
Average performance figures from beam test (there is slight difference between zones):
Light yield: ~ 3000 ph.el. / GeV
Energy resolution:

## Slide 6: HCAL
Performance from the beam test:
energy resolution
light yield 105±10 ph.el. / GeV
beam
PMT
spacers
WLS
fibers
light guide
master plate
scintillators
row 0
row 1
row 2
row 3
row 4
row 5
HCAL module: self-supporting structure containing either 16 outer or 8 outer + 32 inner cells. HCAL consists of 52 modules, 9.5 tons each.
Tilecal technology (originally developed for ATLAS).
The volume ratio Scint:Fe ~ 3:16.
Instrumented depth: 1.2 m, 6 tile rows, ~5.6λI
Outer cells: 26x26 cm2, Inner : 13x13 cm2 (half tiles)
Total of 1488 cells, 2x26 modules, 500 tons
Scintillator, fibers, PMTs, LED system: similar to ECAL
built-in 137Cs calibration system
An HCAL module with optics assembled
Pipes of the source movement system
beam

## Slide 7: The LHCb trigger: Run II
  Hardware Level-0 trigger
      SPD multiplicity  CALORIMETRY
      search for a highest ET object:
          ET (e±/γ) > 2.7 GeV  CALORIMETRY
          ET (hadr.) > 3.6 GeV  CALORIMETRY
          pT (μ) > 1.4 GeV/c  MUON ID system
      up to 1 MHz output, adjustable thresholds
  Software High Level Trigger (HLT)
      ~26000 CPU cores
  Storage rate: 12.5 kHz
L0CALO: 60% of the L0 bandwidth

## Slide 8: Calibration and monitoring

## Slide 9: CALO calibration
The SPD is calibrated on data, via threshold scan with charged tracks. The nominal efficiency is ~95% (threshold ~0.7 MIP).
The PS signal is digitized by 10-bit ADC. The inter-calibration of cells is based on the position of the signal from charged track.
before calibration
after calibration
more details: see talk of D. Pereima, this conference
The ECAL fine calibration on data is based on the π0 peak position.
Up to now, was performed offline.
Starting from 2017, the plan is to do it ~ once per month online (special data stream).
PS
SPD
ECAL
HCAL: the main tool is embedded 137Cs calibration system, calibration out of data taking.

## Slide 10: LED monitoring
Each CALO subdetector is equipped with a LED calibration system.
The HCAL and ECAL monitoring systems have similar design
  LED flash magnitudes are monitored by PIN photodiodes
For HCAL and (since 2015) ECAL: “active” monitoring
  to enable it for ECAL, we had to replace LED light distribution fibers to quartz ones, because of radiation
  The goal is to improve L0 operation stability
  HV corrections are calculated from deviation of average LED amplitudes from reference
    from 2016 – in automatic regime (HV correction at the end of each fill)
  This compensates for the ECAL/HCAL PMT gain drift
    for ECAL it also partially compensates for the radiation degradation of light yield
ECAL
HCAL

## Slide 11: LED monitoring: ECAL in 2016
π0 calib
applied
DAQ failure
Annealing at tech. stops
Outer
Middle
Inner
“Online” π0 mass is ~stable (fraction of MeV degradation).
Active monitoring: HV correction after each LHC fill
More stable detector response: stabilizes L0 rate, facilitates offline calibration.
147 HV updates

## Slide 12: Performance

## Slide 13: Photon reconstruction, e/h separation
μ=782.389 MeV
σ=11.909 MeV
μ=547.539 MeV
σ=9.902 MeV
η,ωπ+π–π0(γγ)
π0,η  γγ
Int.J.Mod.Phys. A30 (2015) 1530022
ECAL E/p
electron
hadron
On average: 5% misID rate for 90% efficiency
e/h separation: momentum dependence of efficiency and mis-ID rate for different

## Slide 14: Ageing effects

## Slide 15: Radiation environment @ CALO
Dose map @ ECAL front, corresponding to the 2012 FLUKA simulation (2.21 fb-1, ECM = 8 TeV)
For ECM = 8 TeV  14 TeV: factor of ~ 1.7 for same integrated luminosity
For the position of EM shower maximum in ECAL: factor of ~2 wrt ECAL front.
Dose profiles at the depth of EM shower max. Rapid decrease with |x|.
(M. Karacson, PhD thesis)
Dose profiles along z at different x positions.
HCAL front: ~0.3 of ECAL front (the CW HV generators are operational till 10-15 kGy)
HCAL back: 0.03 of ECAL front
Instrumented area: |x|>32 cm

## Slide 16: ECAL radiation hardness
The module may be considered operational till ~3-4 Mrad at shower maximum:
10…13 fb-1 @ 14 TeV for the innermost cells (32 cm from the beam)
25…30 fb-1 @ 14 TeV at 48 cm
…
Two ECAL modules were installed in 2009 in the LHC tunnel upstream of the LHCb interaction point, close to the beam pipe.
The dose is measured at the module surface
Sizeable uncertainty (~ x1.5 – x2) in obtaining the dose inside the module
Irradiation of Inner modules in the LHC tunnel

## Slide 17: HCAL radiation degradation
The HCAL radiation degradation can be evaluated in situ from the 137Cs calibration data.
The hadronic shower maximum lays within the tile row 0 (ECAL is ~1.2 λI); the dose in the row 5 is much less.
The light yield degradation in a tile row #i is approximately:
LS1 + beam
commissioning

## Slide 18: PMT ageing
HCAL: up to 100 C/year
ECAL: up to 30 C/year
Compensated by gradually increasing HV
The dynode system ageing was tested in the lab:
Significant DC anode current in HCAL and ECAL PMTs occurs during LHC operation
HCAL
ECAL

## Slide 19: LHCb CALO Upgrade(s)
For the overview of LHCb upgrades: see talk of M. Williams, this conference

## Slide 20: The LHCb trigger: Upgrade
  Solution for LHCb Upgrade:
  No Level-0 trigger any more!
  Event selection will be based of full event reconstruction
All the Front End electronics should work at 40 MHz. The electronics has to be rebuilt for most subdetectors.
Upgrade I.
Step in luminosity to 2·1033 cm-2s-1
With the present trigger organization, 1 MHz L0 limit saturates the physics processes yield with increasing luminosity (especially L0Hadron).

## Slide 21: LHCb CALO Upgrade Phase 1
Present ECAL and HCAL will be kept
PS and SPD will be removed: for particle ID in HLT the tracker information will be used
The ECAL and HCAL Frontend electronics will be rebuilt
The ECAL and HCAL PMT gain will be reduced by factor of 5, to reduce PMT degradation
  PMT linearity: OK within required dynamic range
to compensate, increase x5 the FE preamplifier gain
  low noise frontend ASIC (ICECAL)
detector maintenance should follow radiation degradation of detector components:
  regular replacement of PMTs / CW bases of ECAL
  HCAL degradation in the centre will not affect the LHCb performance
  replace damaged ECAL Inner modules at LS3 (~2025)

## Slide 22: LHCb CALO Upgrade: FEB
CALO FEB prototype
main features:
number of channels: 32
input impedance: 50 Ω
integration time: 25 ns
sensitivity: 4 fC / ADC count
dynamic range: 12 bit
dynamic pedestal subtraction
timing: individual per channel
non-linearity: <1%
spill-over: <1%
cross-talk: <0.5%

## Slide 23: LHCb CALO Upgrade Phase 1b and 2
Phase 1(b) Upgrade (~2025, LS3):
consolidation and enhancement.
LHCb will continue running at L=2·1033cm-2s-1,
to reach ~50 fb-1.
By LS3 HCAL will not be necessary any more
(no hardware EThadron selection)
and will be dismounted, in favor of additional muon filter.
ECAL: at L=2·1033cm-2s-1, occupancy is too high not only in the centre
instead of replacing only very central modules, it is suggested to enhance granularity by replacing all modules in the horizontal band
high granularity  small Moliere radius  W based modules in the centre
CERN-LHCC-2017-003

## Slide 24: LHCb CALO Upgrade Phase 1b and 2
ECAL: migration to new technology
sampling calorimetry
high granularity  W based
timing layer (measure time at ~20 ps precision, to distinguish between primary vertices)
  either 4D Si planes embedded to ECAL modules, or a separate subdetector
First new modules can be installed in the ECAL centre during the Phase I(b) Upgrade (LS3)
Phase 2 (~2030):
the goal is a detector which is able to
take data at L=2·1034cm-2s-1,
Integrated luminosity ~300 fb-1
CERN-LHCC-2017-003

## Slide 25: Conclusions
The Calorimetry system of LHCb is running successfully in 2010-2016, demonstrating very good detector performance.
Upgrade for higher luminosity (2·1033cm-2s-1) is foreseen during LHC LS2.
The Calorimetry system will be subject to the following modifications:
  The Preshower, SPD and lead converter will be removed
  All the Front End electronics of HCAL and ECAL will be rebuilt.
  The gain of all the PMTs will be reduced by factor of 5, with corresponding increase of sensitivity of input amplifiers of Front End Boards
Further LHCb upgrades, Phase 1(b) and 2, are now under consideration, for LHC LS3 and LS4. The final goal is to have a detector running at L=2·1034cm-2s-1.
  HCAL will be removed
  ECAL will be rebuilt using a new technology.

## Slide 26: Thank you!

## Slide 27: backup

## Slide 28: The LHCb operation
LHCb is running at a constant luminosity lower than ATLAS and CMS (3.3·1032 cm-2s-1 in 2016) using luminosity leveling technique.
luminosity leveling

## Slide 29: HCAL ageing
Determined from the 137Cs calibration data